## Slide 1: Multi-link: steps for using a link
Date: 2019-11-16
Authors:
Name | Affiliations | Address | Phone | Email
Laurent Cariou | Intel |  |  | 
Po-Kai Huang |  |  |  | 
Alexander Min |  |  |  | 
Minyoung Park |  |  |  | 
Cheng Chen |  |  |  | 
Dibakar Das |  |  |  | 
Chittabrata Ghosh |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
This presentation discusses multi-link operations for 802.11be, and especially the different steps before using a link, and proposes to better define one of the steps (TID-link mapping step)

## Slide 3: Background – Multi-link Framework
EHT devices (or multi-link logical entity) will be multi-link capable
  Exchange frames over multiple links concurrently or non-concurrently
Note – We assume in this presentation the framework proposed in doc 773r7 and described below
Multi-link logical entity is called MLLE throughout the presentation
Multi-link non-AP logical entity (Non-AP MLLE)
Multi-link AP logical entity
(AP MLLE)
AP 1
AP 2
STA 1
STA 2
Link 1 (e.g., 2.4GHz band)
Link 2 (e.g., 5GHz band)
AP 3
STA 3
Link 3 (e.g., 6GHz band)

## Slide 4: Proposal: Multiple steps to complete before being able to transmit frames between an AP MLLE and a non-AP MLLE
For frame exchange on one or more links, AP/non-AP MLLEs have to go through roughly 3 steps:
  Step1: AP/non-AP MLLEs exchange multi-link capabilities
  Step2: TID-to-link mapping: AP/non-AP MLLEs negotiate and agree which links to use for frame exchange and TID-to-link mapping (if any)
    The TID-link mapping may be updated after this step.
  Step3: a STA of a non-AP MLLE has to be in the awake state for frame exchange on its corresponding link (power state indication)
Multi-link setup phase
After multi-link setup

## Slide 5: Steps after ML capabilities exchange
TID-to-link mapping (step 2):
  Defining the links that will be used for operation:
    TID Mapping:
      All TIDs in all links
      All TIDs in a single link
      TID split: Some TIDs in one link, some TIDs in another link
    What links are enabled/disabled (a link being enabled if at least one TID is mapped to it)
  Management level change
    First established during Multi-link setup
    can be dynamically updated during operation through negotiation
    Can be the same for all STAs, but should be able to be different for each STA

## Slide 6: Steps after ML capabilities exchange
STA power states per link (step 3)
  Each STA has its own power state on each link
  Once a link is mapped/enabled, power state of the STA dictates if the corresponding link can be used for frame exchange
    Awake: available, Doze: unavailable

## Slide 7: Example 1
Mode where AP decides the following:
Link 1,2,3 are setup
Step 2:
  (TID mapping): all TIDs on link 1
Under that mode:
STA can use only link 1
Unavailable/available governed by the power state of the STA on each enabled link
AP can dynamically change TID-link mapping to move the non-AP MLLE to link 2 if it wants for load balancing reasons for instance
Multi-link non-AP logical entity (Non-AP MLLE)
Multi-link AP logical entity
(AP MLLE)
AP 1
AP 2
STA 1
STA 2
Link 1 (e.g., 2.4GHz band)
Link 2 (e.g., 5GHz band)
AP 3
STA 3
Link 3 (e.g., 6GHz band)
Link enabled
Link disabled
Awake
Doze – unavailable

## Slide 8: Example 1 – AP initiated link transition
Mode where AP decides the following:
Link 1,2,3 are setup
Step 2:
  (TID mapping): all TIDs on link 1
Under that mode:
STA can use only link 1
Unavailable/available governed by the power state of the STA on each enabled link
AP can dynamically change link mapping to move the non-AP MLLE to link 2 if it wants for load balancing reasons for instance
Multi-link non-AP logical entity (Non-AP MLLE)
Multi-link AP logical entity
(AP MLLE)
AP 1
AP 2
STA 1
STA 2
Link 1 (e.g., 2.4GHz band)
Link 2 (e.g., 5GHz band)
AP 3
STA 3
Link 3 (e.g., 6GHz band)
Multi-link non-AP logical entity (Non-AP MLLE)
Multi-link AP logical entity
(AP MLLE)
AP 1
AP 2
STA 1
STA 2
Link 1 (e.g., 2.4GHz band)
Link 2 (e.g., 5GHz band)
AP 3
STA 3
Link 3 (e.g., 6GHz band)
AP disables link 1 and enables link 2
All TIDs now in link 2
Link enabled
Link disabled

## Slide 9: Example 2
Mode where AP decides the following:
Link 1,2,3 are setup
Step 2:
  TID-to-link mapping: all TIDs except TID7 on Link 1, TID7 on Link 2
  Link 1 and 2 are enabled
Under that mode:
STA can use only link 1 for TIDs except TID7
STA can use only link 2 for TID7
Unavailable/available governed by the power state of the STA on each mapped link
Multi-link non-AP logical entity (Non-AP MLLE)
Multi-link AP logical entity
(AP MLLE)
AP 1
AP 2
STA 1
STA 2
Link 1 (e.g., 2.4GHz band)
Link 2 (e.g., 5GHz band)
AP 3
STA 3
Link 3 (e.g., 6GHz band)
TID0-6
TID7
Link enabled
Link disabled

## Slide 10: Example 2 – illustration of how a single radio STA handles the 2 links
Mode where AP decides the following:
Link 1,2,3 are setup
Step 2:
  TID-to-link mapping: all TIDs except TID7 on Link 1, TID7 on Link 2
Under that mode:
STA can use only link 1 for TIDs except TID7
STA can use only link 2 for TID7
Unavailable/available governed by the power state of the STA on each mapped link
Multi-link non-AP logical entity (Non-AP MLLE)
Multi-link AP logical entity
(AP MLLE)
AP 1
AP 2
STA 1
STA 2
Link 1 (e.g., 2.4GHz band)
Link 2 (e.g., 5GHz band)
AP 3
STA 3
Link 3 (e.g., 6GHz band)
TID0-6
TID7
Awake
Awake
Doze – disabled
Doze – disabled
Doze – disabled
Link enabled
Link disabled

## Slide 11: Example 3
Mode where AP decides the following:
Link 1,2 are setup
Step 2:
  TID-to-link mapping: all TIDs to Link 1,2
Under that mode:
STA can use link 1,2 without restrictions
Unavailable/available governed by the power state of the STA on each mapped link
  Example: only one STA awake at a time for a single radio device
  Example: two STAs awake at a time for a dual radio device, …
Multi-link non-AP logical entity (Non-AP MLLE)
Multi-link AP logical entity
(AP MLLE)
AP 1
AP 2
STA 1
STA 2
Link 1 (e.g., 2.4GHz band)
Link 2 (e.g., 5GHz band)
Link enabled
Link disabled
Queue

## Slide 12: Example 3 – illustration of different operating modes on different links
Mode where AP decides the following:
Link 1,2 are setup
Step 2:
  TID-to-link mapping: all TIDs to Link 1,2
Under that mode:
STA can use link 1,2 without restrictions
Unavailable/available governed by the power state of the STA on each mapped link
Multi-link non-AP logical entity (Non-AP MLLE)
Multi-link AP logical entity
(AP MLLE)
AP 1
AP 2
STA 1
STA 2
Link 1 (e.g., 2.4GHz band)
Link 2 (e.g., 5GHz band)
20MHz 1SS
80MHz 2SS
Awake
Doze – disabled
Doze – disabled
Doze – disabled
Link enabled
Link disabled
Queue
Awake

## Slide 13: Clarification: Link transition with step 2 or step 3
Link transition with step 2 can be done with an update of the link mapping:
  For instance: from a mapping where all TIDs are on link 1, to a mapping where all TIDs are on link 2
Link transition with step 3 can be done with a STA power state change
  For instance: from STA1 awake on link 1 and STA2 doze on link 2 to STA 1,2 awake on link 1,2
  For instance: from STA1 awake on link 1 and STA 2 doze on link 2 to STA 2 awake on link 2 and STA1 doze on link1

## Slide 14: Clarifications on TID-link mapping (step 2)
In this contribution, we propose to better define step 2 phase (TID-link mapping)
  What does this function do?
  What is the default mode?
  How can it be changed?

## Slide 15: Clarifications on TID-link mapping (step 2)
What does TID-link mapping do?
  Define the mapping of TIDs to the setup links
We propose the following:
  A link is enabled when that link can be used to exchange frames subject to STA power states, and when at least one TID is mapped to that link
  When a link is disabled (i.e. not enabled) by an MLLE, the frame exchanges are not possible and TID are not mapped to that link
  Management frames are allowed on all enabled links, unless explicitly restricted
  At any point in time, a TID shall always be mapped to at least one link that is set up

## Slide 16: Clarifications on TID-link mapping (step 2)
What does TID-link mapping do?
  Define the mapping of TIDs to the setup links
We propose the following:
  If a TID is mapped in UL to a set of enabled links for a non-AP MLLE, then the non-AP MLLE can use any link within this set of enabled links to transmit data frames from that TID
  If a TID is mapped in DL to a set of enabled links for a non-AP MLLE, then:
    the non-AP MLLE can retrieve buffered BUs corresponding to that TID on any links within this set of enabled links, provided that a link is enabled in UL for the non-AP MLLE to indicate a request for delivery
    The AP MLLE can use any link within this set of enabled links to transmit data frames from that TID, subject to existing restrictions for transmissions of frames that apply to those enabled links

## Slide 17: Clarifications on TID-link mapping (step 2)
What is the default mode?
  Mapping TIDs specifically to some link is a good functionality to have, but it seems clear that the main operation would be to allow all TIDs to go in all links
We propose the following:
  The default TID-to-link mapping is:
    All TIDs are mapped to all setup links
  By default all setup links are enabled
  If no TID-to-link mapping information is provided, the default mapping applies

## Slide 18: Clarifications on TID-link mapping (step 2)
How can this be updated?
  This function is a relatively long term operation and both AP MLLE and non-AP MLLE should have a say on this
We propose the following:
  TID-link mapping is negotiated between an AP MLLE and a non-AP MLLE, through a request/response protocol

## Slide 19: Conclusion
We clarify the 3 steps that we see needed before exchanging frames on a link
For step 2 (TID-link mapping) design, we propose
  A default mode (all links enabled and TIDs mapped to all links)
  The basic functionalities of TID-link mapping and rules that need to be respected (all TIDs mapped to at least one link, …)

## Slide 20: Staw poll #1
Do you agree to add the following to the specification framework document:
  default TID-to-link mapping is:
    All TIDs are mapped to all setup links
  by default, all setup links are enabled
  if no TID-to-link mapping information is provided, the default mapping applies

## Slide 21: Staw poll #2
Do you agree to add the following to the specification framework document:
  At any point in time, a TID shall always be mapped to at least one link that is set up, unless admission control is used

## Slide 22: Staw poll #3
Do you agree to add the following to the specification framework document:
  Management frames are allowed on all enabled links, following baseline

## Slide 23: Staw poll #4
Do you agree to add the following to the specification framework document:
  If a TID is mapped in UL to a set of enabled links for a non-AP MLD, then the non-AP MLD can use any link within this set of enabled links to transmit data frames from that TID
  If a TID is mapped in DL to a set of enabled links for a non-AP MLD, then:
    the non-AP MLD can retrieve buffered BUs corresponding to that TID on any links within this set of enabled links
    The AP MLD can use any link within this set of enabled links to transmit data frames from that TID, subject to existing restrictions for transmissions of frames that apply to those enabled links
      An example of restriction is if the STA is in doze state