## Slide 1: Capabilities to support Time-Aware Scheduling in 802.11be
Date: 2018-12-19
Authors:

## Slide 2: Abstract
This presentation describes gaps and new capabilities required to enable Time-Aware scheduling over the 802.11be for time-sensitive and real-time applications.
The presentation focuses on Time-Aware scheduling as defined by the 802.1Qbv standard, but the concepts and solutions described may also be applicable more generally.

## Slide 3: Outline
TSN and Time-Aware scheduling
Issues and new requirements in mapping Time-Aware scheduling over 802.11
  Part 1: Time-Aware (802.1Qbv) scheduling configuration over 802.11
  Part 2: Time-Aware schedule execution enhancements (latency, jitter, reliability)
Conclusions

## Slide 4: IEEE 802.1 Time-Sensitive Networking (TSN)
TSN Components Common Standards
Latency
Reliability
Standard Ethernet with Synchronization, small and/or fixed latency, and extremely low packet loss
Reliability
Ultra reliability: Frame Replication and Elimination (P802.1CB) Path Control and Reservation (802.1Qca) Per-Stream Filtering and Policing (802.1Qci) Reliability for time sync (P802.1AS-Rev)
Synchronization
Time synchronization: Time Synchronization (802.1AS)
Resource Mgmt
Dedicated resources & API Stream Reservation Protocol (802.1Qat) TSN configuration (P802.1Qcc) YANG (P802.1Qcp) Link-local Registration Protocol (P802.1CS)
Bounded low latency: Time-Aware traffic shaping (802.1Qbv) Preemption (802.1Qbu/802.3br) Cyclic Scheduling (802.1Qch) Asynchronous Scheduling (802.1Qcr)
Zero congestion loss
Credit: János Farkas, Ericsson
TSNA Conference 2017, http://www.tsnaconference.com/
√ 802.1AS over 802.11
Timing Measurement (TM)
Fine Timing Measurements (FTM)
√ 802.11aa (SRP over 802.11 for AV)
√ 802.11ak (802.11 links in an 802.1Q network)
Time-Aware scheduling (802.1Qbv) over 802.11 (extension to address bounded latency for scheduled traffic)

## Slide 5: Time-Aware (Qbv) Scheduling – Operation model & Assumptions
CUC: Central User Configuration
CNC: Central Network Configuration
802.1Qcc Centralized Model
Assumptions:
Time-critical traffic streams (max packet size and inter-arrival time) are known a priori (at configuration stage)
The IEEE 802.1Qcc std defines management models (the centralized model is assumed here, other models are also possible)
All TSN devices are synchronized to the same reference clock (through 802.1AS)
The CUC collects the traffic stream requirements from end devices (Talkers/Listeners) and the CNC discovers the network topology
The CNC computes the transmission schedule and the end to end path for each traffic stream and communicate the schedule to the CUC
The CNC configures the schedule at TSN Bridges and the CUC configures the schedule in the end devices (e.g. via control plane using YANG/NETCONF)
Wireless TSN Domain Considerations
802.11 Access Points can be seen as Wireless TSN Bridges
STAs can be configured as talkers or listeners
The CUC/CNC need to coordinate with the WTSN domain (scheduling over wireless is within the 802.11 scope, but it needs to align with the overall CNC schedule)
Control plane (logical connection) between CUC and End Devices
Control plane (logical connection) between CNC and TSN bridges

## Slide 6: Parameters and Example Schedule
Guard-band protects time-critical traffic (the “guard band” behavior is inherent in the defined behavior of the gates, i.e., no explicit guard band is defined in the Qbv specification)
Cycle: list of gate operations (SetGateStates), where each operation has a time delay (Gate Open Duration). The sequence of gate operations terminates at the end of the list and re-starts OperCycleTime after the start of the sequence.
8021.Q Traffic Classes (defined by PCP field in a VLAN Tag) to Queues Mapping on a TSN Bridge
Gate
Gate
Gate
Gate
Timing Data
Gate Control
Traffic Class
#
7
Traffic Class
#
6
Traffic Class
#
5
-
-
Traffic Class
#
0
Transmission Selection
TC#7
TC#6
TC#5
TC#4
TC#3
TC#2
TC#1
TC#0
T0
SetGateStates:
State: C C C C C C C C
TC : 7 6 5 4 3 2 1 0
T1
T2
SetGateStates:
State: 0 C C C C C C C
TC : 7 6 5 4 3 2 1 0
SetGateStates:
State: C O O O O O O O
TC : 7 6 5 4 3 2 1 0
Cycle
Gate Open Duration for Time-critical Traffic (TC#7)
Guard band
Time critical traffic can be protected by a guard band
Gate Open Duration for other (non-protected) traffic classes (TC#0-6)
Time-critical Traffic
The Time-Aware scheduling behavior must be enforced at the MAC (e.g. 802.3 or 802.11)
The Time-Aware scheduling behavior have to coexist/align with the 802.11 access mechanisms (e.g. EDCA and trigger-based access)

## Slide 7: Features required to support Time-Aware Scheduling
Time synchronization
  Support for 802.1AS time synchronization is already enabled by 802.11 TM and FTM
Classification and mapping packets of a traffic stream to a traffic class (aligned with 802.1Q traffic classification)
  802.1Q and TCLAS traffic mapping capabilities defined in the 802.11 spec
Enable a STA to receive a time-aware schedule request from the higher layer at the 802.11 MAC
  The schedule is used by the 802.11 MAC to control medium access and serve the traffic streams
  The 802.11 MAC may accept or reject the request (the decision is implementation specific)
Enable execution of a time-aware schedule, i.e., deliver packets with certain deadlines (bounded latency) at requested time intervals
  The 802.11 MAC needs to provide predictable access to certain packets (preferably with high reliability) and enable non-AP STAs to request such service based on a higher layer trigger
  The time-aware schedule needs to take into account dynamic link states in 802.11 (negotiation with the higher layer may be required – topic for collaboration between 802.1 and 802.11)

## Slide 8: Part 1: Time-Aware Schedule Configuration over 802.11

## Slide 9: Time-Aware Schedule Configuration Extensions
TSN Talker
TSN Listener
CUC: Central User Configuration
CNC: Central Network Configuration
802.1Qcc Centralized Model
Qbv Schedule Computation:
Traffic requirements are known (max pkt size, inter-arrival time)
The CNC uses the link speed to create the schedule
  For Ethernet: The CNC assumes a fixed link speed (e.g. 1 Gbps) to compute the gate open duration for a given max packet size;
  For wireless/802.11: the CNC needs an estimate of time-aware scheduling support provided by the 802.11 MAC (worst-case latency for a given max packet size at predictable time intervals)
Information about 802.11 capabilities could be added as part of Qbv configuration (802.1Qbv parameters wireless links) → topic for collaboration between 802.1TSN and 802.11
The CNC can define a schedule and request the 802.11 devices (AP and STAs) to execute it, 802.11 devices need to indicate whether they can meet the requested schedule
  Need a management interface at the 802.11 MAC and primitives to accept/negotiate a Time-Aware Scheduling request from the higher (Qbv) layer

## Slide 10: Time-Aware Schedule Configuration over 802.11
Outside 802.11 scope
802.1Q TSN mngmt entity
802.11 MLME SAP
Qbv Schedule Config (e.g. from CNC)
TASched.Request
TASched.Response
Qbv Schedule Config Response (e.g. to CNC)
The AP decides whether it can serve the traffic streams according to the requested schedule.
Non-AP STAs need to request the AP to be served according to the TA Schedule before responding.
T0
T0+ 10ms
500 µs
(Guard band)
1 ms
(gate open)
Time-critical
8.5 ms
(gate open)
Other traffic
Example TAS

## Slide 11: STA initiated Time-Aware Scheduling Request (e.g. STA Talker scenario)
Non-AP STA
MLME SAP
TASched.Request
TASched.Response
The AP decides whether it can serve the traffic streams according to the requested schedule.
T0
T0+ 10ms
500 µs
(Guard band)
1 ms
(gate open)
Time-critical
8.5 ms
(gate open)
Other traffic
Example TAS
AP
MLME SAP
TAS.Request (TAS)
TAS.Response ( )
STA responds to the higher layer based on the result of the negotiation with the AP

## Slide 12: Summary of Gaps and Potential Solutions
How to inform the 802.11 MAC of a Time-Aware (Qbv) Schedule request from the SME?
  A new MLME MLME-TA-SCHEDULE.Request (TAS).
How to inform the AP of a STA’s requested schedule?
  The STA can use the schedule information to generate a request to be served according to a certain service period (for a max packet size and inter-arrival time)
  The STA can use a new procedure or updated procedures (e.g. ADDTS Request/Response, TWT setup, …)
  If the AP agrees to schedule the STA as requested, the STA can confirm the upper layer request, otherwise, the STA declines the upper layer time-aware scheduling request
  The AP is responsible for scheduling DL and UL resources (if trigger-based mode is used), STAs can apply the schedule on top of their own queues (if non-trigger-based mode is used)
How to ensure packet prioritization and latency bounds are met by the 802.11 MAC?
  Introduce the concept of a Time-Awareness within the 802.11 MAC to differentiate and prioritize channel access based on an agreed Time-Aware schedule

## Slide 13: Time-aware scheduling support via enhanced AddTS Request/Response
Non-AP STA
SME
Non-AP STA
MAC
AP STA
MAC
AP STA
SME
MLME-AddTS.Request
(TSPEC,
TCLAS:VID,
TAS)
AddTS Request
MLME-AddTS.Indication
MLME-AddTS.Response
AddTS Response
MLME-AddTS.Confirm
(TSPEC: TSID
TCLAS: UP)
TAS Cycle
: Guard band
: Gate Open (Time-critical)
: Gate Open (Other traffic)
SP for Time-critical traffic
Indicates that the AP agrees to serve the STA according to the requested schedule.

## Slide 14: Additional considerations
Other 802.11 mechanisms could also be used in combination with the time-aware scheduling support, e.g.
  If the STA has time-critical and other types of traffic, the TWT SP could help align the periods to save power
  Note: Traffic prioritization within a TWT SP is still according to the Qbv schedule.
TWT SP for time-critical + other traffic
: Guard band
: Gate Open (Time-critical)
: Gate Open (Other traffic)
TWT SP for Time-critical traffic

## Slide 15: Part 2: Time-Aware Schedule Execution Enhancements (latency, jitter, reliability) over 802.11

## Slide 16: Issues if the 802.11 MAC is not aware of time-critical packets and their required transmission schedule
Assuming the high priority AC is selected for the scheduled time-critical traffic
On average, high priority AC should get faster access, but a time-critical frame may still wait in some situations, e.g.:
  other ACs get access first (as backoffs run independently)
  other non-time critical (e.g. voice) frames mapped to the same AC is ahead in the queue
  ongoing (long) TXOP before the scheduled time
Main gaps:
  Lack of protection for time-critical traffic, i.e., prevent other traffic from accessing the medium at certain times
  Provide access at scheduled time for time-critical frames with minimal access delay and jitter
Time-sensitive frame
TXOP (AC_VI)
Time-sensitive frame

## Slide 17: Making the 802.11 MAC time-aware
A Time-Aware schedule is defined by upper layer and passed to the 802.11 MAC via the SME-MLME-SAP interface
Time-critical traffic identified by a given traffic class is mapped to a TID associated with a TSN Queue, other traffic is mapped to other EDCA queues
  If multiple flows are time critical, they can share one queue or multiple TSN queues can be created;
  802.11be may define a mapping of TCs to 802.11 TID/TSN Queue when time-aware scheduling is used
A Time-Aware Shaper (TAS) Function receives the TA Schedule from the Higher Layer
The TAS Function pauses/resumes EDCAFs to avoid contention and protect the time-critical traffic according to the TAS (e.g. when the TSN queue is open, other queues are paused)
A frame selection function (implementation dependent) selects frame(s) for transmission based on their priorities
Higher (Qbv) Layer (TAS = GateControlList)

## Slide 18: TSN Channel Access
The TSN Queue follows access rules to minimize latency and jitter, different modes may be enabled:
  Trigger-based: AP controls access in the DL and UL, STA and AP negotiate on expected service periods that are aligned with the Qbv schedule
  EDCA-based: regular EDCA access behavior (e.g. access parameters TBD)
TC#7 -> TSN
TC#6 -> VO
TC#5 -> VI
TC#4
TC#3
TC#2
TC#1
TC#0
T0
T1
T2
BE
BK
T3
T4
guard band
Time-critical
Example TC to 802.11 Queue mapping and Schedule
TSN Access: Trigger based or EDCA
Regular operation, channel access policing is applied by the Time-Aware Shaper Function

## Slide 19: Impact of unmanaged BSSs
Time-Aware scheduling operates on managed STAs
  Interfering transmissions may impact the capability to guarantee bounded latency
  Unmanaged STAs/OBSSs are seen as interference
The AP can take into account the level of interference when accepting/admitting TA schedules and defining SP durations
  Latency bound vs. capacity tradeoffs will depend on the level of interference and deployment scenario

## Slide 20: Summary of the new requirements to support Time-Aware Scheduling over 802.11be
Interface to receive a time-aware schedule request from the higher layer
Mechanism for STAs to request the AP to be served according to a time-aware schedule
Time-awareness for policing channel access according to an agreed time-aware schedule
Low latency access for time-critical frames (once the gate is open) and differentiation from other traffic classes
  trigger based access can help provide predictable access and control worst-case latency

## Slide 21: Conclusions
Time-Aware scheduling is a key capability to control congestion and worst case latency
  One important requirements for 802.11be is to differentiate (known) time-critical streams from other traffic and serve them with predictable worst-case latency
  This capability will also enable 802.11 to be integrated with Ethernet-based TSN, which is one of the goals identified in the 802.11be/EHT PAR
The 802.11 MAC can introduce enhancements to better support time-aware scheduling
  Proposed modifications are limited to controlling queues and leveraging trigger-based access for higher efficiency and lower latency

## Slide 22: References
IEEE Std 802.1Qbv-2015.

## Slide 23: Example: Setting up a downlink schedule over 802.11
TSN Talker
TSN Listener
802.1Qcc Centralized Model
Example:
Time-critical stream from Talker to (wireless) Listener: 100 bytes every 10 msec
CUC/CNC collect the traffic requirements
The CNC defines a Qbv schedule and configures the gate control list at the TSN bridges and the TSN AP:
T0
T0+ 10ms
500 µs
(Guard band)
1 ms
(gate open)
Time-critical traffic
8.5 ms
(gate open)
Other (Best-Effort) traffic
The TSN AP confirms (via management interface) that it can execute the schedule → new management interface capability needed to agree on the schedule over a 802.11 link
CUC configures the Qbv schedule at the end devices, including all the 802.11 STAs in the WTSN domain (not only the listener) an STAS confirm the reception (through management interface)
TSN bridges, AP and end devices (STAs) start executing the schedule at the specified time
TSN AP transmits the time-critical DL data to TSN Listener STA at the scheduled times, and STAs control channel access accordingly
Example Schedule

## Slide 24: Example: Setting up an uplink schedule over 802.11
TSN Listener
TSN Talker
802.1Qcc Centralized Model
Example time-critical traffic stream:
Talker to (wireless) Listener: 100 bytes every 10 msec
CUC/CNC collect the traffic requirements
CNC defines a Qbv schedule and configures the gate control list at the TSN bridges and the TSN capable STAs and AP:
T0
T0+ 10ms
500 µs
(Guard band)
1 ms
(gate open)
Time-critical traffic
8.5 ms
(gate open)
Other (Best-Effort) traffic
The TSN AP can execute the schedule for its Ethernet port (as it doesn’t need to transmit over wireless)
CUC configures the Qbv schedule at the Talker STA and other 802.11 STAs in the WTSN domain
The Talker STA can confirm whether it can meet the uplink schedule → 802.11 support for a negotiation with the AP is needed, if scheduled access (e.g. triggered) is used
If in trigger-based mode, the AP schedules the UL transmission at the requested times. If not trigger-based access, the Talker STA will try to transmit at the scheduled time
Example Schedule