## Slide 1: Multi-link Framework
Date: 2019-11-11
Authors:

## Slide 2: Recap
Multi-link logical entity: A logical entity that has one or more affiliated STAs. The logical entity has one MAC data service interface and primitives to the LLC and a single address associated with the interface, which can be used to communicate on the DSM [1].
  NOTE –A Multi-link logical entity allows STAs affiliated with the multi-link logical entity to have the same MAC address
  NOTE – The exact name can be changed
  Multi-link operation (MLO) device: A logical entity that enables common management signaling between a collection of one or more Multi-Link Logical Entities (MLLEs) [2]
  Note – the exact name can be changed later

## Slide 3: Framework
This two-layer structure [2] shown below conflicts the terminology of “device” in 802.11md as described in [3]
  There are two layers for multi-link concept, the lower layer is entity, the upper layer is device.
  However, all of these two layers belong to the terminology of “device” in 802.11md
  The definition for each layer is vague
  Each layer has an exception
  One STA in a lower layer could be categorized as multi-link entity
  One multi-link entity in an upper layer could be categorized as multi-link device
  In this contribution, we try to solve the above issues
  Claim that One STA does not belong to multi-link, but we are open to add new operation for this STA if needed
  Try to reuse the existing architectures or do some minor change on them
  We do not touch any related operation, such as FST, about multi-link. It could be discussed later

## Slide 4: Could One STA Belong to Multi-link?
Now for the STA, we have non-tunable single band STA, or tunable single band STA
  For non-tunable single band STA, it only supports one band/sub-band, but can change the operating channel within this band/sub-band. The range of working frequency is relative small
  For tunable single band STA, it can support more than one band/sub-band but work in one band at a time. The range of working frequency is relative large
Reference [4] regarded a special case (a STA) as multi-link logical entity
  A STA that only supports one radio (original name in [4]), but could camp on different links
  Base on the above descriptions, both non-tunable single band STA and tunable single band STA can be regarded as multi-link device
  However, such categorization is not reasonable
  First, it does not keep consistent with multi-band capable device in the draft where it has more than one STA
  There is big difference between STA and multi-link device, one only allows the traffic to be sent in one link at a time, but the other allows the traffic to be sent more than one link simultaneously
  No more extra one link maintenance work like multi-link device for single band STA because only one link is configured to work at a time and this configuration is much quasi-static

## Slide 5: Could One STA Belong to Multi-link?
Besides the categorization, is there any necessity to simplify the protocols for single band STA in 802.11be?
  We are open to it, but we need evaluate its benefit first
  How often does the single band STA change its working channel
  How much is the overhead for one extra link maintenance for single band STA
  Now we also have neighbor report, fast BSS transition, BSS transition management and so on in the draft to achieve the traffic steering for the single band STA. Are they enough?
  In the context of multi-link AP device, is there any other work to do?

## Slide 6: The existing architectures in 802.11REVmd D3.0
In 802.11REVmd D3.0 (4.9.4 Reference model for multi-band operation), it says
  A multi-band capable device can manage operation over more than one frequency band/channel. The operation across the different frequency bands/channels can be simultaneous or nonsimultaneous.
  A multi-band capable device can also support multiple MAC sublayers.
  The multi-band procedures (see 11.32 (Multi-band operation)) allow a pair of multi-band capable devices to discover, synchronize, (de)authenticate, (re)associate, disassociate, and manage resources with each other on any common band/channel that is supported by both STAs.
  There are two kinds of multi-band capable device
  One is to support transparent FST
  Only supports the function of flow level[2]
  But all the STAs share the same MAC
  SAP as packet level architecture [2] and
  multi-link logical entity [1]

## Slide 7: The existing architectures in 802.11REVmd D3.0
The other supports non-transparent FST
  Only supports the function of flow level[2]
  And each STA has its own MAC SAP as
  the flow level architecture [2]
  Here we just want to point out that architectures exist in draft.
  Based on the above reference models, we propose a clear terminology for multi-link in the next slide
  Try to reuse the existing architectures, and keep consistent with terminology of multi-band capable device

## Slide 8: Multi-link capable device
Multi-link capable device: A device that has more than one affiliated STA, which can operate in different frequency bands/channels.
  Multi-link capable transparent device: A device that has more than one affiliated STA, which can operate different frequency bands/channels. The device has a single MAC SAP presented to the logical link control (LLC) layer for all of the affiliated STAs that are identified by one common MAC address.
  Whether the affiliated STA has its own MAC address is TBD
  Multi-link capable non-transparent device: A device that has more than one affiliated STA, which can operate in different frequency bands/channels. The device has a single MAC SAP presented to the logical link control (LLC) layer for each affiliated STA that is identified by a MAC address.
  Multi-link capable AP device: A multi-link capable device, where each affiliated STA is an AP.
  Multi-link capable non-AP device: A multi-link capable device, where each affiliated STA is a non-AP STA

## Slide 9: Summary
A more accurate unified framework for multi-link operation is proposed and it keeps the consistent with the existing architectures of the related multi-band capable device in the draft
  Multi-link capable device, multi-link capable transparent device and multi-link capable non-transparent device
  Do some minor change on them without any conflict, an example of the minor change: replace “Transparent FST Entity” in the figure of slide 4 with “Common high MAC”.
To facilitate the process of the multi-link feature, we suggest to discuss the operations for multi-link capable transparent device and multi-link capable non-transparent device separately
  They may be combined after full discussion later

## Slide 10: References
[1] IEEE 802.11-19/0773r7 Multi-link Operation framework
[2] IEEE 802.11-19/0823r2 Multi-link aggregation
[3] IEEE 802.11-19/1231r3 Multiband and Multichannel Operation in IEEE 802.11be
[4] IEEE 802.11-19/1542r0 multi-link broadcast addressed frame reception

## Slide 11: SP 1
Do you support to add the following sentence to the 11be SFD？
Multiple MAC SAPs Multi-Link device (MMLD): A device that has more than one affiliated STA and has more than one MAC SAP to the LLC.
Note-The device can be logic

## Slide 12: Backup
Q: Could we still use the terminology of multi-band capable device for 802.11be
  A: Suggest to change multi-band to multi-link, in order to match the multi-link feature in 802.11be well. Meanwhile we can reuse the existing architectures of multi-band capable device or do some minor change on them without any conflict, an example of the minor change: replace “Transparent FST Entity” in the figure of slide 4 with “Common high MAC”.
Q: What is the relationship between FST and this proposal.
  A: FST is the protocol of multi-band operation based on the architectures of multi-band capable device in the REVmd D3.0. However, this proposal does not touch any related operation protocols for the multi-link capable device. The group could think about the more advanced protocols to meet the new requirement in 802.11be.
Q: What is the relationship between FST and multi-link operation
  A: Although FST and multi-link operation are all based on the existing architectures in the draft with slight difference, they could be different.

## Slide 13: SP 0
Multi-Link Device (MLD): A device that has more than one affiliated STA and has one MAC data service to the LLC with a single MAC SAP MAC address associated with MAC data service, which can be used to communicate on the DSM.
  The WM MAC address of each STA affiliated with the MLD is TBD
Multiple MAC SAPs Multi-Link device (MMLD): A device that has more than one affiliated STA and more than one MAC data service to the LLC with a MAC SAP MAC address per MAC data service, which can be used to communicate on the DSM.

## Slide 14: SP 1
Multi-link capable device: A device that has more than one affiliated STA, which can operate in different frequency bands/channels.
  Multi-link capable transparent device: A device that has more than one affiliated STA, which can operate different frequency bands/channels. The device has a single MAC SAP presented to the logical link control (LLC) layer for all of the affiliated STAs that are identified by one common MAC address.
  Whether the affiliated STA has its own MAC address is TBD
  Multi-link capable non-transparent device: A device that has more than one affiliated STA, which can operate in different frequency bands/channels. The device has a single MAC SAP presented to the logical link control (LLC) layer for each affiliated STA that is identified by a MAC address.

## Slide 15: SP2
  Multi-link capable AP device: A multi-link capable device, where each affiliated STA is an AP.
  Multi-link capable non-AP device: A multi-link capable device, where each affiliated STA is a non-AP STA