## Slide 1: Latency Measurement for 11be Features
Date: 2020-01-xx
Authors:
Name | Company | Address | Phone | Email
Akira Kishida | NTT |  |  | akira.kishida.fs@hco.ntt.co.jp
Yasuhiko Inoue |  |  |  | 
Yusuke Asai |  |  |  | 
Yasushi Takatori |  |  |  | 
Kengo Nagata |  |  |  | 
Xin Zuo | Tencent |  |  | xinzuo@tencent.com
Suhwook Kim | LG Electronics |  |  | suhwook.kim@lge.com
Kazuyuki Sakoda | Sony |  |  | Kazuyuki.Sakoda@sony.com
Mohamed Abouelseoud |  |  |  | Mohamed.Abouelseoud@gmail.com
Liangxiao Xin |  |  |  | Liangxiao.Xin@sony.com
Notes: I’m Akira Kishida affiliated with NTT.
I’d like to introduce my contribution entitled as “Latency Measurement for 11be Features”.
The Document Number is 1942r6.

## Slide 2: Abstract
According to EHT PAR [1], the scope of TGbe includes at least one mode of operation capable of improved worst case latency and jitter.
As well as IEEE 802.11ax, IEEE 802.11be will use unlicensed spectra, low-latency and jitter functions depend on the radio environments.
  Therefore, measurement of quality of low-latency and jitter is quite important.
This presentation discusses necessity of measurement and report features for IEEE 802.11be low-latency functions.
  Latency characteristics are affected from contention time and retransmission time (Transmit delay defined in REVmd) greatly, then those should be measured for real-time applications (RTAs).
  Statistical measurement and report for worst case latency or jitter should be needed, which requires a number of measurement results.
Notes: As you know, the scope of TGbe includes at least one mode of operation capable of improved worst case latency and jitter.
As well as the past major IEEE 802.11 standards, IEEE 802.11be will use unlicensed spectra, low-latency and jitter functions depend on the surrounding environments.
Therefore, measurement of quality of low-latency and jitter is quite important.
Then, this presentation discusses necessity of measurement and report functions for IEEE 802.11be low-latency functions.
Latency characteristics are affected from contention time and retransmission time greatly, Then those should be measured for real-time applications (RTAs).
Moreover, statistical measurement for worst case latency or jitter should be needed, which requires a number of measurement results.

## Slide 3: Problem Statement
Latency measurement of Wi-Fi could be essential not only for latency/jitter improvement but also for RTAs, Internet Service Provider (ISP) s and Network operators.
  In order to maintain the same QoS and manage network, monitoring and adaptation to the network are important.
statistics captured/predicted at online mobile gaming servers | 
daily active users | tens of millions
users connected through Wi-Fi | ~ 60% of above
bad user experience due to network | 20 ~ 40% of above
problems located at the Wi-Fi link | ~70% of above
Notes: In this slide, we show some problem statements.
Latency measurement of Wi-Fi could be essential not only for latency/jitter improvement but also for RTAs, Internet Service Provider (ISP) s and Network operators.
In order to maintain the same QoS and manage network, monitoring and adaptation to the network are important.
This table shows statistics captured and predicted data at online mobile gaming servers.
There are tens of millions of daily active users, and 60% above of them are connected through Wi-Fi.
And 70% above users whose user experience are bad have problems of Wi-Fi link.

## Slide 4: Problem Statement (cont’d)
Some RTAs (e.g. game app and server) have already integrated adaptive algorithms for network transmission, trying to maintain QoS for users, based on the measurement on Wi-Fi links using other techniques on upper layers. However,
  Measurement frequency is a trade-off between extra network load and efficiency of algorithm.
  Measurements are “blurred” reflections of Wi-Fi links “a moment” ago (not accurate nor immediate as Wi-Fi built-in measurements)
  ISPs have no better understanding of what is going on at Wi-Fi side and thus no better solutions to help end-to-end QoS for users.
Notes: Some RTAs ,game app and server for example, have already integrated adaptive algorithms for network transmission,
in order to maintain QoS for users, based on the measurement on Wi-Fi links using other techniques on upper layers.
However,
Measurement frequency is a trade-off between extra network load and efficiency of algorithm.
Moreover, Measurements are “blurred” reflections of Wi-Fi links “a moment” ago.
Therefore, ISPs have no better understanding of what is going on at Wi-Fi side and thus no better solutions to help end-to-end QoS for users.

## Slide 5: Need for Features of Latency Measurement
RTA Report [2] indicates various use cases of real-time applications and their requirements.
  To meet the requirements of each real-time application, we should know how much latency and jitter are generated in the BSS.
From the perspective of stable network management, low-latency features in IEEE 802.11be should be controlled based on the results of latency measurement.
  Latency measurement can offer recognition or prediction of “Worst Case” for RTA.
  For example, low-latency queue proposed in [3] can be utilized based on the results of latency measurement.
Notes: In this slide, we explain the necessity for features of measurement.
RTA Report indicates various use cases of real-time applications and their requirements.
To meet the requirements of each real-time application, we should know how much latency and jitter are generated in the BSS.
From the perspective of stable network management, low-latency features in IEEE 802.11be should be controlled based on the results of latency measurement.
Moreover, latency measurement and its report functions can offer recognition or prediction of “Worst Case” for RTA.
For example, low-latency queue proposed in LG’s contribution can be utilized based on the results of timing measurement.

## Slide 6: Need for Features of Latency Measurement (cont’d)
Contention time and retransmission time (defined as Transmit delay in REVmd spec) that affect on latency characteristic should be measured at each AP and STA, and statistical information of delay and jitter characteristic should be notified to an AP or networks.
RTA STA should have some functions that can measure latency (including contention time and retransmission time).
  However, concrete method of latency measurement (how AP or STAs measure latency at each side) won't be defined in IEEE 802.11be standard.
    It can be left for implementation matter.
    It may be good that AP or STA measure each packet delay within its normal operation (in-service).
Moreover, features that notify statistical information of latency measurement should be defined in IEEE 802.11be.
Notes: We think that contention time and retransmission time that affect on latency characteristic should be measured at each AP or STA, and statistical information of delay and jitter characteristic should be notified to an AP or networks.
Therefore, RTA STA should have some functions that can measure latency including contention time and retransmission time.
However, concrete method of latency measurement won't be defined in IEEE 802.11be standard and it can be left for implementation matter.
It may be good that AP or STA measure each packet delay within its normal in-service operation.
Moreover, features that notify statistical information of latency measurement should be defined in IEEE 802.11be.

## Slide 7: Time Categorization for Latency Analysis
“Wi-Fi Time Sensitive Networking (17/1734r1)”[4] comprises packet delay as follows.
  Packet Delay = Queueing Delay + Packet Transmission Time
“Latency analysis for EHT (19/0762r1)”[5] divides packet delay as follows.
TW: Contention waiting time
  Time to transmit previously arrived packets
TC: Contention time
TR: Additional time for retransmission
  Time spent for failed transmission
TTX: Transmission time for successful data frame and ACK
Notes: First, we consider latency portions.
Contribution concerning time sensitive network indicates packet delay comprises from queueing delay plus transmission time.
In addition, contribution from LG shows latency portions as shown in this figure.
According to this categorization, packet delay can be separated to four portions.
***
First, contention waiting time denoted as Tw. This is the time from the arrival of the packet in the queue to the end of the previous transmission.
Second, contention time as Tc. This period starts from the beginning of contention to the beginning of initial transmission.
Third, additional time for retransmission as Tr. This is the time spent for failed transmissions.
Last, transmission time for successful data frame and ACK as TTX. This period includes media access delay of successful transmission.

## Slide 8: Time Categorization for Latency Analysis (cont’d)
This figure shows an example of divided time categories based on “Latency analysis for EHT (19/0762r1)”[5]
TW: Contention waiting time
TC: Contention time
TR: Additional time for retransmission
TTX: Transmission time for successful
data frame and ACK
Sending STA
Recieving STA
Previous transmission
Busy for another transmission
Backoff Time
Backoff (carry over)
Busy for another transmission
Backoff Time
Backoff (carry over)
Transmission
failed
×
Contention for retransmission
Queue in
Contention start
TW: Contention waiting time
TC: Contention time
TR: Additional time for retransmission
TTX: Transmission time for successful data frame
and ACK
Successful data transmission and ACK
Initial transmission
Contention time and retransmission time have great impact on latency characteristics for RTA!
Notes: To promote an understanding of the categorization explained in previous slide, we show the example of latency portions as a time chart.
TW is the period from the timing of arrival of packet in the queue to the start of contention.
TC ,the contention time, starts from the beginning of contention and ends at the initial transmission.
Additional time for retransmission denoted as TR includes both contention for retransmission and failed transmission time.
The last portion, TTX indicates transmission time for successful data and ACK.
Especially, Contention time and retransmission time have great impact on latency characteristics for RTA and those latency should be measured.

## Slide 9: Latency Measurement and Notification
Additional measurement functions that can measure contention time and retransmission time should be required.
  Though it can be left for implementation matter, all RTA STAs should have latency measurement functions and we should make agreement for that.
Statistical information about latency and jitter should be measured and notified to determine whether target RTA can be utilized or not.
  Notification function of the information should be defined in IEEE 802.11be.
  Statistical information: Average latency for certain period, worst case latency and jitter, et, al.
Notes: Then, we believe that additional measurement functions that can measure contention time and retransmission time should be required.
Though it can be left for implementation matter, all RTA STAs should have latency measurement functions and we should make agreement for that.
In addition, statistical information about latency and jitter should be measured and notified to determine whether target RTA can be utilized or not.
Notification function of the information should be defined in IEEE 802.11be.

## Slide 10: Conclusions
To obtain more detailed availability of low-latency and jitter features, additional measurement function(s) for contention time, retransmission time will be needed.
To judge whether current RTA is applicable or not, statistical information about latency and jitter should be measured and notified as well.
To control low-latency features in 11be properly, RTA STAs should have latency measurement and notification features.
  However, concrete method of latency measurement will be implementation matter.
Notes: This is the conclusions of this presentation.
To obtain more detailed availability of low-latency and jitter features, additional measurement function(s) for contention time, retransmission time will be needed.
Moreover, to judge whether current RTA is applicable or not, statistical information about latency and jitter should be measured and notified as well.
In addition, to control low-latency features in 11be properly, RTA STAs should have latency measurement and notification features.
However, concrete method of latency measurement will be implementation matter.
That’s all of my presentation. Thank you for your listening.

## Slide 11: References
[1] 802.11/18-1231r1 “EHT draft proposed PAR”
[2] 802.11/19-0006r6 “RTA report draft”
[3] 802.11/19-1524r0 “Latency enhancement for EHT”
[4] 802.11/17-1734r0 “Wi-Fi Time Sensitive Networking”
[5] 802.11/19-0762r1 “Latency analysis for EHT”

## Slide 12: Appendix – TM and FTM
IEEE 802.11v (already merged to IEEE 802.11-2016) defines timing measurement (TM) and fine timing measurement (FTM) as parts of WNM (Wireless Network Management).
  However, TM and FTM are features for timing synchronization or location detection originally.
  Then, WNM offers measurement functions only for medium access delay of successful transmission.

## Slide 13: Existing Features of Timing Measurement: WNM
WNM (Wireless Network Management) defined in IEEE 802.11-2016 establishes Timing Measurement (TM) / Fine Timing Measurement (FTM) procedures.
  However, timing Measurement in WNM can measure only medium access delay of successful transmission (portion of TTX).
  The whole intention of TM and FTM is not latency measurement but timing synchronization or location detection.
TW: Contention waiting time
TC: Contention time
TR: Additional time for retransmission
TTX: Transmission time for successful
data frame and ACK
Notes: IEEE 802.11 has already timing measurement features. Those are defined in Wireless Network Management or WNM.
And WNM establishes Timing Measurement and Fine Timing Measurement procedures.
However, these features can measure only medium access delay of successful transmission.

## Slide 14: Timing Measurement procedure in WNM
Timing Measurement is initiated by transmitting Timing Measurement Request frame.
Timing Measurement frame and corresponding Ack frame are used to measure time difference between STAs.
  Timing Measurement frame is an Action frame.
Measurement period
Notes: This slide indicates the procedure of timing measurement in WNM.
First, Timing Measurement is initiated by transmitting Timing Measurement Request frame from Receiving STA.
Once Timing Measurement is initiated, Sending STA casts an Timing Measurement frame to the receiving STA.
This Timing Measurement frame is an Action frame.
And then, Receiving STA sends ACK frame as its reply.
This procedure enables measurement for medium access delay.
Time of Departure denoted as t1, Time of Arrival denoted as t2,
Time of Departure of ACK denoted as t3 and Time of Arrival of ACK denoted as t4 are measured in this procedure.
Round trip time, that is, medium access delay, can be computed by using these information.

## Slide 15: Scope of Timing Measurement in WNM
Timing Measurement in WNM can measure only medium access delay of successful transmission (portion of TTX).
However, real time applications are greatly affected by contention time (TC) and retransmission time (TR).
  Contention time increases according to transmissions by other STAs.
  Retransmission affects immediately n increase of latency.
Sending STA
Recieving STA
Previous transmission
Busy for another transmission
Backoff Time
Backoff (carry over)
Busy for another transmission
Backoff Time
Backoff (carry over)
×
TW
TC
TR
TTX
Measurement period by timing measurement defined in
WNM
Need to measure for RTA in IEEE 802.11be
Notes: However, real time applications are greatly affected by contention time denoted as TC and retransmission time denoted as TR.
Contention time increases according to transmissions by other STAs.
Retransmission time increases by collisions, interferences or insufficient SINRs.
These affects immediately increase of latency.
Therefore, Additional functions to measure TC and TR should be needed in IEEE 802.11be.