## Slide 1: Multi-Link Security And Aggregation Operations
Date: 2019-10-10
Authors:
Name | Affiliations | Address | Phone | email
Huizhao Wang | Quantenna |  |  | hwang@Quantenna.com
Sigurd Schelstraete | Quantenna |  |  | 
Imran Latif | Quantenna |  |  | 
Debashis Dash | Quantenna |  |  | 

## Slide 2: Abstract
In this contribution we discuss the following topics for Multi-Link:
  Security Association between Multi-Link Device Instances, per LINK PTKSA & GTKSA binding, Tx PN number assignment, and Rx replay check procedures
  Establish per TID BA agreement at Multi-Link Device Instance level
  Frame Sequence Number assignment, BA Tx window management, BA Rx reordering & scoreboard management, BA retry procedure at Multi-Link Device Instance level

## Slide 3: Multi-Link Security Association And Per Link PTKSA & GTKSA Framework (1)
Here we present a framework to be considered by TGbe for Multi-Link Security Association, per Link PTKSA & GTKSA key hierarchy derivation process, the process of PN number assignment at the transmitter side and Rx replay checking process at the receiver side
In this framework, the Multi-Link Security Association is established between AP and STA’s Multi-Link Device Instances through one of the already defined methods in baseline: 802.1x, PSK, SAE etc. The result of Security Association at Multi-Link Device Instance level is the mutually derived PMK binding. This PMK will be used to derive per Link PTASA through modified 4-way key exchange process
Per Link PTKSA: once the Multi-Link Security Association is established with mutually derived PMK, then on the per Link Lower-MAC level, PTKSA 4-way key exchange process should be invoked to derive per Link PTK[link], with the input parameters of: PMK, AP_per_Link_nounce, STA_per_Link_nounce, AP_per_Link_MAC_address, STA_per_Link_MAC_address:
  PTK[link] = KDF(PMK, AP_Lower_MAC[link], AP_nounce[link],
  STA_Lower_MAC[link], STA_nounce[link]);
Per Link GTKSA: per Link GTK[link] is initially delivered to non-AP STA’s per Link Lower-MAC as part of the PTKSA 4-way key exchange, the subsequent GTK[link] rekey process is done through per Link 2-way key exchange

## Slide 4: Multi-Link Security Association And Per Link PTKSA & GTKSA Framework (2)
AP Multi-Link Device AP Instance (authenticator)
2.4G
Lower MAC/PHY
5G
Lower MAC/PHY
6G
Lower MAC/PHY
2.4G
Lower MAC/PHY
5G
Lower MAC/PHY
6G
Lower MAC/PHY
Authentication process: 802.1x, SAE, PSK etc
Mutually derives PMK at Upper MAC level
AP Multi-Link Device STA Instance (supplicant)
3. Create per link PTASA & GTKSA
(through 4-way key-exchange)

## Slide 5: Multi-Link Security Association And Per Link PTKSA & GTKSA Framework (3)
As defined in baseline spec, the PN number space is binding with its PTKSA or GTKSA.
By allowing PTKSA/GTKSA binding at per Link Lower-MAC level, the PN space need to be maintained at the per Link Lower-MAC level as well.
And the PN should be assigned at the transmitter per Link Lower-MAC level, with each Link maintains its own monotonic increase PN[link] space, along with its PTKSA and GTKSA binding
Rx replay checking is done at the receiver side after Rx reordering: if the MPDU’s PN number is larger than the the recorded per Link per TID PN, this MPDU has passed replay checking, and the recorded per Link per TID PN will be replaced by the MPDU’s PN; otherwise, this MPDU has failed the replay checking and is dropped.
Rx replay checking procedure with MPDU retried on the different link is TBD

## Slide 6: BlockACK Agreement In Multi-Link
To take advantage of Multi-Link, we propose to have an option to establish per TID BlockACK agreement (BA agreement) at the Multi-Link Device instance level
If the BA agreement is established at the Multi-Link Device instance level, then the transmitter side BA sliding window management should be done at the same level as well.
If the BA agreement is established at the Multi-Link Device instance level, then the receiver side BA reorder & scoreboard operation should be done at the same level as well.
If the BA agreement is established at the Multi-Link Device instance level, then the BlockACK response (C-BA, or M-STA BA) should be done at the same level as well.

## Slide 7: Tx BA Sliding Window, Rx Reorder & Scoreboard Operations
Transmitter Multi-Link Device Instance
Receiver Multi-Link Device Instance
2.4G
Lower MAC/PHY
5G
Lower MAC/PHY
6G
Lower MAC/PHY
2.4G
Lower MAC/PHY
5G
Lower MAC/PHY
6G
Lower MAC/PHY
MPDU0
MPDU1
MPDU2
MPDUn
MPDUs are assigned SN[TID] based on Tx BA Sliding Window at Multi-Link Device Instance layer
2. A-MPDU aggregation & transmit
4. Rx reorder, scoreboard process and BlockACK response are done at Multi-Link Device Instance layer
MPDU0
MPDU2
MPDU1
MPDUx
Rx reorder
& Scoreboard
3. Receive MPDUs

## Slide 8: Replay Checking In Multi-Link (1)
In baseline RSN specification, replay check is done after the Rx reordering process.
In Multi-Link, with PTKSA and GTKSA are binding at the per Link Lower-MAC level, the PN assignment is done at the transmitter per Link Lower-MAC level.
Here we present the mechanism of conducting replay checking in Multi-Link with PTKSA & GTKSA binding at the per Link Lower-MAC level:
  Receiver Multi-Link Device Instance maintains array of variables of per Link per TID largest PN recorded so far: PN[Link][peer_STA][TID]
  Received Multi-Link MPDUs from the peer STA
  First go through BA Rx reordering & scoreboard process
  Then for each received MPDU passed the Rx reordering & scoreboard process, compare its PN with the recorded PN[Link][peer_STA][TID]:
  If (PN > recorded PN[Link][peer_STA][TID), then this MPDU has passed replay check, and update the recorded PN[Link][peer_STA][TID = PN
  Else, replay check failed, drop the MPDU, and update the replay check failure counter
This mechanism assumes MPDU retransmission is done on the same link.
MPDU retransmission from a different link will need to have a different replay checking mechanism (TBD)

## Slide 9: Replay Check With Multi-Link (2)
AP Multi-Link Device Instance
STA Multi-Link Device Instance
2.4G
Lower MAC/PHY
5G
Lower MAC/PHY
6G
Lower MAC/PHY
2.4G
Lower MAC/PHY
5G
Lower MAC/PHY
6G
Lower MAC/PHY
PN=M
PN=K
PN=J
PN=M+1
PN=K+1
PN=J+1
PN=M+1
PN=M
PN=K+1
PN=K
PN=J+1
PN=J
MPDU0
MPDU1
MPDU2
MPDUn
MPDUs belong to the same TID without PN assigned at MLD level
2. PN assignment at the Lower MACs with each Lower MACs maintain their
Own monotonic increase PN number counter
4. Individual MPDUs are received
3. Encrypt/decrypt using per Link PTK[link] key materials
BA Rx reorder & scoreboard
Replay check:
MPDU PN compare with
Recorded PN[Link][peer_SA][TID]
5. Release or drop
The MPDU

## Slide 10: Conclusions
We have presented the framework of:
  Establish Security Association with PMK binding at Multi-Link Device Instance level
  Establish per Link PTKSA, GTKSA at per Link Lower-MAC level
  Establish BA agreement at Multi-Link Device Instance level
  Tx BA sliding window management, Rx BA reordering & scoreboard operations at the Multi-Link Device Instance level
  Transmitter side PN assignment, and receiver side replay checking process
This framework allows the flexibility of:
  BA agreement binding at Multi-Link Upper-MAC level
  Have the same level of functionality of RSN as in baseline

## Slide 11: SP 1
Do you agree in 11be to allow establishing Security Association and PMK binding at the Multi-Link Device Instance level?
Y/N/A

## Slide 12: SP 2
Do you agree in 11be to allow establishing PTASA & GTKSA binding at the Multi-Link per Link Lower-MAC level?
Y/N/A

## Slide 13: SP 3
Do you agree in 11be to allow per Link PN space for MLD?
Y/N/A

## Slide 14: SP 4
Do you agree in 11be to allow conducting Rx replay check procedure defined at the page 9 & 10?
Y/N/A

## Slide 15: References
IEEE 802.11-19-0773: Multi-Link Operation Framework
IEEE 802.11-19-1962: Multi-Link Upper-MAC Entity Instance & New MAC Header