## Slide 1
Further considerations on 20MHz channel access
Date: 2020-1-14
Authors:

## Slide 2: Introduction
In the last meeting, the basic rule of 20 MHz channel access has been decided[1]
  20MHz channel access performs a backoff procedure based on the channel states of two contiguous 10MHz channels
    Idle states are checked by TBD sensing methods
  TBD IFS sensing period in case of not knowing the duration of channel use in secondary channel
The remaining issues includes:
  Sensing methods for each of two 10 MHz channels consisting 20 MHz channel
  Sensing period in case of unknown channel usage period
  Conditional 10MHz fallback operation
In this contribution, the discussion about the remaining issues of 20 MHz channel access will be continued

## Slide 3: Recap: Agreed channel access method for 20MHz transmission
Uses a single backoff counter, and the counter value is decreased at the end of each slot if and only if both of two 10 MHz channels are sensed idle[2]
  Two contiguous 10MHz channels shall use the same receive sensitivity level

## Slide 4: Sensing period of channel according to the sensing method for 20 MHz channel access
The 20 MHz channel consists of two contiguous 10 MHz channel:
  In one 10 MHz channel (denoted as OCB primary channel), the channel sensing with PD and ED with NAV setting method can be applied
  In the other 10 MHz channel (denoted as OCB secondary channel), various channel sensing methods are suggested, including:
    Some suggestions to enable PD[3], [4]
    GI detection [2]
    Energy Detection
When the OCB primary channel is sensed as channel busy, the channel sensing period should be same as the sensing period of 10 MHz transmission (e.g. AIFS)
  Since the channel usage period can be determined by PD and NAV setting

## Slide 5: Sensing period of channel according to the sensing method for 20 MHz channel access
As in [5], EIFS sensing prevents the hidden node problem and ensure the fairness with 10 MHz transmission in case of no information on channel usage period.
In case of channel sensed busy in the OCB secondary channel and the duration of channel use is not known, EIFS sensing period may prevent hidden node problem and ensure the fairness with 10 MHz transmission
  In case of the detection of IEEE 802.11 signal
To prevent overprotection, AIFS sensing period may be used in case of
  Channel busy period can be determined
  IEEE 802.11 signal is not detected

## Slide 6: Decision of enabling fallback options
In case of channel busy in one 10 MHz channel during 20 MHz channel access, under certain conditions, 10 MHz fallback may cause:
  Adjacent channel interference to the other channel
  Larger congestion level on the OCB primary channel
There are two options for the transmission of frames
  Option 1: Decision of using 10 MHz fallback operation as in the baseline is decided and allowed by upper layer
  Option 2: Not allowing 10 MHz transmission during 20 MHz channel access, no fallback operation

## Slide 7: Fallback option 1: Determined by upper layer
When 10MHz fallback operation is allowed by upper layer:
  When the OCB primary channel is detected channel busy, the cease and resuming backoff procedure is performed
  When the OCB secondary channel is detected channel busy, 10 MHz transmission on the OCB primary channel is performed after the backoff procedure on OCB primary channel during the remaining backoff period
For the decision of enabling fallback operation these information to the upper layer may help the upper layer to make appropriate decision:
  Effects of adjacent channel interference
    E.g., distance of STA (RSSI) using the secondary channel
  Channel busy ratio

## Slide 8: Fallback option 2: Disabling fallback operation
The fallback operation may not be permitted in any case because of the described issues:
  Adjacent channel interference
  Larger congestion level on the OCB primary channel
When either channel is sensed busy, cease and resume the backoff procedure when the both channel is detected idle for certain period

## Slide 9: Conclusion
The remaining issues of 20 MHz channel access is discussed
  The sensing method and sensing period of each 10 MHz channel
  Whether to allow 10 MHz fallback transmission in case of channel busy indicated in one 10 MHz channel
Using the various sensing method, the EIFS detection is proposed to prevent hidden node problem and guarantee fairness in case of
  Channel busy by IEEE 802.11 signal is detected
  The duration of channel usage cannot be determined
In case of channel busy in one channel, there are two options for 10 MHz fallback operation
  Option 1: Enabling transmission using only 10 MHz channel as in the baseline by the indication of upper layer
  Option 2: Cease and resume the backoff procedure for either channel busy, no fallback operation

## Slide 10: Straw poll #1
Do you agree to add the followings to SFD:
  20 MHz channel consists of two contiguous 10 MHz channel:
    In one 10 MHz channel (denoted as OCB primary channel), the channel sensing with PD and ED with NAV setting method shall be applied.
  When the OCB primary channel is sensed as channel busy, the backoff procedure on the OCB primary channel shall be same as the backoff procedure of 10 MHz transmission.
  Y/N/A=11/0/12

## Slide 11: Straw poll #2
Do you agree to add the followings to SFD:
  When OCB secondary channel is sensed busy and the duration of channel busy is not known, EIFS sensing period shall be used.
  When OCB secondary channel is sensed busy and the duration of channel busy can be known, AIFS sensing period shall be used.
  Note: STA is not required to have a capability to detect the duration of channel busy on the OCB secondary channel.
  Y/N/A=4/1/17

## Slide 12: Straw poll #3
Which options do you support regarding the 10 MHz fallback operation?
  Option 1: The decision of using 10 MHz fallback mechanism is indicated by upper layer
  Option 2: The 10 MHz fallback operation during 20 MHz channel access is not allowed in any circumstance
  Option 1/Option 2/Abstain=7/1/10

## Slide 13: Straw Poll #4
Do you agree to add the followings to SFD:
  The decision of whether using 10 MHz fallback mechanism as specified in the baseline spec by the STA is allowed is indicated by upper layer.
  Y/N/A=16/0/5

## Slide 14: Reference
[1] IEEE 802.11-19/497r4, 802.11bd Specification Framework Document, Bahar Sadeghi (Intel)
[2] IEEE 802.11-19/1480r2, Harmonization for 20MHz Channel Access, Insun Jang (LG electronics)
[3] IEEE 802.11-19/1494r0, Fair Sub-Channels Access, Yossi Shaul (Autotalks)
[4] IEEE 802.11-19/1076r1, medium access with 20MHz BW, Liwen Chu (Marvell)
[5] IEEE 802.11-19/1478r2, Study on 20MHz Channel Access Schemes: follow-up, Hanseul Hong (Yonsei Univ.)

## Slide 15: backup

## Slide 16: The concept of EIFS: baseline
In the baseline, STA senses for EIFS before start/resuming the backoff in case of reception failure of the frame
  It provides the enough time for transmitter of STA to receive the ACK frame

## Slide 17: With fallback procedure: 20 MHz access of proposed method
When fallback is enabled,
  ED+PD sensing performed in the channel for remaining backoff counter
  10MHz PPDU transmission after expiration of backoff