## Slide 1: UL Coordination for Throughput Improvement and Interference Reduction
Date: 2019-10-24
Authors:
Name | Affiliation | Address | Phone | Email
Tsodik Genadiy |  |  |  | 
Li Yunbo |  |  |  | 
Shilo Shimi |  |  |  | 

## Slide 2: Introduction
AP coordination is widely discussed in 802.11be, where the main motivation is to increase DL throughput and coverage by allowing two or more APs to transmit simultaneously
This concept is mostly based on advanced Tx BF schemes which can be achieved by aggregating many Tx antennas across several APs
Assuming many APs will be equipped with at least 8 Rx antennas, advanced decoding schemes may also be applied at the AP side
In this presentation we suggest an UL Coordination scheme that may allow parallel transmissions of multiple UL packets and enable better spatial efficiency of the Wi-Fi network

## Slide 3: Problem Formulation
The simplest scenario is two STAs, associated with different APs, where each AP is equipped with multiple receive antennas
AP1 triggers STA1 to transmit an UL frame, and AP2 wants to trigger STA2 to transmit an UL frame
Assuming AP1 transmits a trigger frame first, AP2 would refrain from triggering STA2 and wait till STA1 finishes its UL transmission, otherwise mutual interference may prevent both packets from being detected
This means that spectrum efficiency is limited
AP1
AP2
STA1
STA2
Rx Beam

## Slide 4: Potential Solutions
Spectral efficiency in the scenario we mentioned in the previous slide may be improved if we allow AP2 to transmit/trigger a parallel UL transmission
This problem is addressed in 802.11ax by SR techniques, where the main direction is to limit the Tx power of the parallel transmission and ensure small or negligible interference
However, we can achieve higher spectral efficiency by applying AP coordination methods for UL transmission and considering advanced Rx decoding schemes
The main idea is to reuse the UL MU-MIMO scheme, where each STA will be allocated with different spatial stream indices (columns of the P-matrix)
This means that transmitted signals should be aligned in time and frequency, which is a similar requirement to that of DL AP Cooperation currently discussed in 802.11be
Data Frame
Data Frame
MU-MIMO HE-LTF
MU-MIMO HE-LTF
STA1
STA2

## Slide 5: UL AP Coordination Requirements
The main concept hence is parallel aligned UL transmission; here we discuss the respective requirements
In order to allow the AP to implement efficient MU-MIMO detection or interference mitigation we need to consider at least the following:
  Time and frequency synchronization: similar to AP coordination in the DL, synchronization has a huge impact on the performance; we assume that synchronization will be maintained for DL coordination in 802.11be, thus no need for additional methods to be implemented
  Packet duration: Rx BF may be very efficient in presence of interference, however if interference cancelation is applied on a signal with no interference may cause performance degradation; thus we have to align between duration of two frames or at least to indicate to the receiver when to stop applying Rx BF
  Interference covariance estimation: many Rx BF techniques are based on estimated spatial covariance of the interfering signal, thus we need to allow accurate covariance estimation

## Slide 6: Detection Options
Assuming MU-MIMO format is used, two possible detection schemes can be considered (i.e. not limited only to APs with MIMO detection capabilities):
  Joint detection – similar to regular (UL) MU-MIMO, the AP can decode the received signals jointly and then discard of the irrelevant information
  Interference mitigation – AP may consider the estimated channel of the second signal as an interference and mitigate it applying an Rx beamforming technique (for example, noise covariance whitening)
Rx
MU-MIMO Channel Estimation
MIMO Decoder
FEC
Rx
MU-MIMO Channel Estimation
Interference
Covariance Estimation
Cholesky
Data Detector

## Slide 7: UL Coordination Procedure Diagram
Following the last slide we may apply the next procedure for UL coordination
  Master and Slave AP negotiate such that they are aligned on coordinated UL transmission parameters
  Master AP may suggest or limit the number of spatial streams to be used by parallel UL transmission, while slave AP may respond with actual number of streams
  The relevant information is indicated during coordination negotiation procedure: packet duration, allocated RUs, #Nss, MCS (required for joint detection), Tx power limits etc.
  UL Transmissions are triggered – trigger may be transmitted in several formats (jointly, in parallel or serial trigger transmission)
UL Coordination Negotiation Procedure
Coordinated UL Trigger
Data Frame
Master AP
Slave AP
STA1
STA2
Data Frame
MU-MIMO HE-LTF
MU-MIMO HE-LTF
Full Alignment
Time

## Slide 8: Simulation Parameters
We compare between four different schemes:
  UL transmission with no interference
  Non-Coordinated UL transmission with interference
  Coordinated UL transmission with interference – applying interference cancellation
  UL transmission with no interference, with reduced number of Rx antennas – following the theory that each synchronized interferer requires single antenna to mitigate it
Simulation parameters:
  TGnD channel model, MCS4, LDPC, 1000B
  SIR in range of 7-17dB
  MMSE detection
  8 or 16 Rx antennas, Nss = 2

## Slide 9: Simulation Results
In the figures below we can see the results of the simulations
We can see that very good performance can be achieved in presence of strong interference if synchronization is assumed, where degradation of ~2-2.5dB is observed for UL coordinated transmission with Nss=2 (compared with the no-interference case!)

## Slide 10: Conclusions
UL coordination may significantly improve efficiency of a Wi-Fi network by allowing simultaneous transmissions
Very good performance can be achieved applying existing MU-MIMO transmission format for HE-LTF field
AP can independently choose which type of detection to apply based on its own capabilities
No need for any payload exchange (information bits at Tx or LLRs at Rx)
The proposed method relies on DL AP coordination synchronization techniques (already being considered in 802.11be) and thus requires no additional algorithms

## Slide 11: Straw Poll
Do you support to introduce an UL AP Cooperation procedure in 802.11be? Y/N/A