## Slide 1: CSI-based Context-Assisted Indoor Localization
Authors:
Name | Affiliations | Address | Phone | email
Dinesh Bharadia | Professor, UCSD | 9500 Gilman Dr. San Deigo, CA, 92122 | +1-858-822-0168 | dineshb@ucsd.edu
Roshan Ayyalasomayajula | Student, UCSD |  |  | roshana@eng.ucsd.edu
Aditya Arun | Student, UCSD |  |  | aarun@eng.ucsd.edu
Chengfeng Wu | Student, UCSD |  |  | chw357@ucsd.edu
Debashis Dash | Quantenna Communications | 1704 Automation Pkwy San Jose, CA 95131 | +1 669 209 5661 | ddash@quantenna.com

## Slide 2: Introduction
What is Wi-Fi Sensing? [1, 2, 3]
  Using existing standardized 802.11-based protocols to sense and track changes in the environment
Status
  Interest in WNG July session
  TIG created in September session to further explore Wi-Fi sensing
Why Wi-Fi?
  Ubiquitous, re-use existing technology for new use cases
  Device-free, extra sensor-free, privacy-friendly
Feasibility
  Large-scale autonomous data collection for localization with context
  CSI based sub-meter accurate Indoor localization within indoor maps
  Requires no retraining for small environment updates

## Slide 3: Use Case: Indoor Navigation
CSI Use Cases [1, 2, 3]
  Security, automation, health care etc.
  Indoor Navigation
Indoor Navigation
  Lack of reliable positioning and accurate maps
  Can CSI be a good equivalence?
  Feasibility of context-aware mapping and learning based localization using Wi-Fi CSI

## Slide 4: Context-Assisted Learning Based Localization
Automated data collection
  Autonomous platform for mapping the physical environment and capturing synchronized WiFi CSI
  CSI for GPS-equivalence
  Learning network for coherence
Data-driven navigation
  Mapping and localization algorithm using abundant labeled data
MapFind: Context-aware autonomous robot [5]
DLoc: Learning based map-aware localization

## Slide 5: Enabling Deep Learning from AP
Convert CSI to image representation
AP-STA CSI is used to derive AoA-ToF using MUSIC/Spotfi [4]
Polar to XY for localization
Angle of Arrival, 𝝷°
X axis (m)
Time of Arrival (m)
Y axis (m)
Polar to Cartesian

## Slide 6: Learning Based Localization
Image-to-Image translation challenges
  Network Architecture
  Loss Functions
  Environment changes and Multi-AP CSI
Multi-AP bring challenges
  ToF offsets/errors cause radial shifts
  Multipaths give spurious peaks
  NLOS paths cause AoA and ToF errors
Learning Network Architecture

## Slide 7: MapFind Mapping and Trajectory

## Slide 8: Results: MapFind Autonmous Mapping
1. CSI-enabled AP
2. Lidar
3. Camera
4. Laptop

## Slide 9: Results: Learning based Localization
Trained on 25k locations and tested on 100k locations in a 18mx8m large space with 4 APs we achieve sub-m accurate Indoor localization. While RSSI based algorithms show median errors up to few meters.
Median Error: 65 cm
90th Percentile: 160 cm

## Slide 10: Results: Localization across various Bandwidths
Dloc 80MHz
Dloc 40MHz
Robustness to the change in Bandwidths while inference improves with available CSI BW

## Slide 11: Results Across various environments and settings
Test Scenario | Median Localization Error(cm)
1(trained) | 65
2 (not seen) | 85
3 (not seen) | 85
4 (not seen) | 91
Model tested on multiple scenarios
  Location of furniture and reflectors are modified to mimic day-to-day changes
Training data and learning network unchanged
Median Localization error still stays sub-meter level
Scenario-1
Scenario-2
Scenario-3
Scenario-4

## Slide 12: Standardization
How can standardization help? [3]
Consistent CSI availability
TX parameter optimization indication e.g. beamforming
Efficient CSI extraction and scheduled CSI
Privacy preserving CSI for client localization

## Slide 13: Conclusions
Wi-Fi sensing is growing in demand with many implemented solutions indicating feasibility
  CSI-based solutions close in performance for indoor localization
Standardization can make the CSI extraction process private, efficient and improve interoperability

## Slide 14: References
[1] [2] Wi-Fi sensing, IEEE 802.11-19/1164
[2] Wi-Fi sensing: cooperation and standard support, IEEE 802.11-19/1416
[3] CSI-based Wi-Fi sensing, IEEE 802.11-18/1769
[4] “Spotfi: Decimeter Level Localization using WiFi”, Manikanta Kotaru, Kiran Joshi, Dinesh Bharadia, Sachin Katti
[5] "Towards Context-assisted Indoor Navigation", Ayyalasomayajula Roshan, Aditya Arun, Chenfeng Wu, Sanatan Sharma, Deepak Vasisht, Abhishek Sethi, Dinesh Bharadia