## Slide 1: Power Save for Multi-link
Date: 2019-11-11
Authors:

## Slide 2: Background
Multi-link feature not only increases the throughput[1], but also can improve latency performance by duplicate transmission[2]
However, power consumption issue[3] becomes more serious when multi-link feature is implemented at the STA, especially for the battery powered non-AP STA
  More than one link operate concurrently
  More than one link maintenance work, such as DL traffic delivery, BSS or link parameters update
  In this work, we focus on power save mechanisms for multi-link, including
  The necessity for primary link
  DL traffic delivery
  BSS or link specific parameters update and TWT setup

## Slide 3: Primary link
In 802.11 ax, we have (D)TIM, (U)-APSD, WNM, TWT, intra-PPDU and so on.
For the multi-link capable device (MLCD), the above features could be implemented at each link
However, the power consumption increases linearly with the number of links
  Take beacon reception shown in the following figure for an example, the power consumption is doubled
STA based primary link is proposed to address the above issue
  Multi-link capable STA does not need to receive the beacon in a non-primary link with the aid of primary link
Link 1
Link 2
Beacon
Beacon
Link 1
Link 2
AP
STA
PM =1 for Link 1&2
awake
awake
Beacon
Beacon
awake
awake
skip
skip

## Slide 4: Primary link
Before the primary link selection, multi-link capable AP will broadcast the set of primary links through the beacon frame
  Based on the set of primary links, each STA could choose its own primary link
  Primary link selection could be done in the phase of association or could be changed after the association
  The power consumption for the non-primary link could be reduced if the following work could be done in the primary link
  DL traffic delivery notification
  BSS or link specific parameters update notification
AP1/ 2.4G
AP2/ 5G
AP4/ 6G
STA1/ 2.4G
STA2/ 5G
STA/ 2.4G
STA1/ 5G
STA2/ 6G
Primary link 1
MLCD STA 2
MLCD STA 3
Primary link 2
Primary link 3

## Slide 5: DL traffic delivery
DL traffic delivery notification for a non-primary link is proposed to be sent in the primary link
  DL traffic includes group addressed MSDUs/MMPDUs and individual addressed MSDUs/MMPDUs
To support the above DL traffic delivery notification for a non-primary link , we propose to reuse the existing TIM element
  Use the same Partial Virtual Bitmap field in the TIM element to indicate whether there are buffered BUs for the primary link and non-primary link
  Assign another AID to a non-primary link based on the meaning of each bit in Partial Virtual Bitmap field
  For non primary link，the buffered BUs could either be individual addressed BU or both two kinds buffered of BU
  Moreover, there may exist two options to notify the DL traffic buffered at the AP for a non-primary link
  A unified notification for both group addressed BUs and individual addressed BUs, no necessity to separate them because of the same target-wake up the non-primary link
  Have two notifications for group addressed BUs and individual addressed BUs, respectively

## Slide 6: DL traffic delivery
Regarding group addressed BU delivery, there may exist divergence
  The direct way is to deliver the group addressed BUs in the related link, no any change for the route of this kind of traffic
  Slightly prefer this option
  On the other hand, the route of the group addressed BUs could be changed as described in the first bullet
  AP duplicates the group addressed BUs on all the primary links [4] and sends them in each primary link such that the multi-link capable STA does not need to wake up its non-primary link in this case
  However, it will increase power consumption for the primary link
  The transmission time for the group addressed BU in the primary link will increase significantly
  The duplicated group addressed BUs from the non-primary link may not be needed for some STAs in this primary channel

## Slide 7: Link specific parameters update and TWT setup
Besides the DL traffic delivery notification in the primary link, link specific parameters update for non-primary link could also be done in primary link
  No need to wake up the non-primary link frequently to receive the new link specific parameters
TWT setup could be done in one link for another link [5]
To support both the peak throughput and power save, the same TWT parameters could be applied for more than one link
Link 1
Link 2
STA
awake
awake
awake
awake
awake
awake
TWT SP
TWT SP

## Slide 8: Summary
Power save mechanism is proposed based on primary link
  Primary link is STA based
  DL traffic delivery notification and link specific parameters notification for non-primary link are proposed to be sent in the primary link
  Non-primary link does not need to receive its beacon frame
  TWT setup could be done in one link for another link，and the same TWT parameters could also be applied for all the links

## Slide 9: References
[1] IEEE 802.11-19/1291r3 Performance aspects of Multi-link operations
[2] IEEE 802.11-19/1101r1 Conditional Packet Duplication in Multiple Link System
[3] IEEE 802.11-19/1231r3 Multiband and Multichannel Operation in IEEE 802.11be
[4] IEEE 802.11-19/1526r0 multi-link power save
[5] IEEE 802.11-19/1510r0 power saving considering multi-link

## Slide 10: SP 1
Do you agree that each multi-link STA chooses its own primary link

## Slide 11: SP 2
Do you agree that the non-primary link of the multi-link STA does not need to receive the beacon frame