## Slide 1: eBCS Demonstration
Date: 2019-11-10
Authors:

## Slide 2: Abstract
This presentation introduces an implementation and demonstration of the concept of eBCS.

## Slide 3: System Architecture
Web server
Web server
Web server
eBCS AP
eBCS AP
eBCS AP
eBCS STA
eBCS STA
eBCS STA
HTTP (unicast)
eBCS (broadcast)

## Slide 4: Web Server
Usual Web server
  Nginx
  No modifications
Provide contents
  Web pages
  Live video streaming (HLS)
Provide contents information
  Title
  File list
  Hash value of each file
  Destination multicast IP address / UDP port
Storage
bcsgenci
nginx
Read contents
Write contents
information
HTTP

## Slide 5: eBCS AP
bcstx
  Get contents from web servers by HTTP
  Serialize, compress, separate into packets
  Apply LDPC-Staircase/Triangle (RFC5170)
  Transmit the packets to loopback interface as IP multicast
bcsap
  Receive IP multicast packets from loopback interface
  Generate keys
  Transmit eBCS Info frames and eBCS Data frames
  Use digital signature and TESLA
  Please refer 11-19/451r5 for the frame sequence
  Both eBCS Info frames and eBCS Data frames are Action frames
Kernel
  Modify to enable configuring transmission rate
bcstx
Loopback I/F
bcsap
Get contents
By HTTP
IP multicast
IP multicast
eBCS Info
eBCS Data
Serialize/compress/separate
LDPC-Starcase/Triangle
Generate keys
Generate eBCS Info/Data frames

## Slide 6: eBCS STA
bcssta
  Receive eBCS frames via PCAP
  Authenticate eBCS frames
  Transmit the packets to loopback interface as IP multicast
bcsrx
  Receive IP multicast packets from loopback interface
  Reconstruct contents with LDPC-Staircase/Triangle
  Write contents to the storage
nginx
  Provide contents to bcsplay
bcsplay
  Poll contents
  Display contents
Kernel
  Modify the driver to enable monitor mode
bcssta
Loopback I/F
bcsrx
eBCS Info/Data
(PCAP)
IP multicast
IP multicast
Contents
Authenticate
Reconstruct contents
Storage
nginx
bcsplay
HTTP
Display

## Slide 7: Parameters
WLAN
  2.4GHz
  20MHz bandwidth (Ch11)
  IEEE 802.11n (HT) MCS3 for eBCS Data
  IEEE 802.11n (HT) MCS1 for eBCS Info
eBCS
  Digital signature: RSA2048
  Hash for TESLA: SHA256
  eBCS Info interval: 1s
  TESLA Key Change Interval: 100ms
Application Layer
  LDPC-Triangle
  Code rate: 2/3
  Packet transmission interval: 1ms

## Slide 8: Demonstration Video

## Slide 9: References
11-19/451r5 eBCS Frame Authentication Proposal
11-19/850r0 Expected Total System Architecture