## Slide 1
On Unintentional Beamforming
Date: 2019-11-1317-12-14
Authors:
Name | Affiliations | Address | Phone | email
Qinghua Li | Intel | Santa Clara 12 3600 Juliette Lane Santa Clara, CA 95054 USA |  | Qinghua.Li@intel.com
Feng Jiang |  |  |  | Feng1.Jiang@intel.com
Jonathan Segev |  |  |  | Jonathan.Segev@intel.com
Assaf Gurevitz |  |  |  | 
Robert Stacy |  |  |  | 

## Slide 2: Abstract
Contribution, IEEE 802.11-19/1572r4, discussed a potential problem due to unintentional beamforming in 11az secure ranging. The solution proposed in 1572r4 multiplies the memory size scalar by the number of antennas for storing the secure sounding signals. This contribution depicts a simple solution, which can be implementation specific

## Slide 3: Problem Statement (1/2)
The signals sent by antennas 1 and 2 are the same except the global phases may be different
The received signals may superimpose each other constructively and destructively
Signal 1
TX antenna 1
TX antenna 2
- Signal 2
Signal 3
- Signal 4
Signal 1
Signal 2
Signal 3
Signal 4
HE-STF
…
HE-STF
…
NSTS = 2 , LTFREP = 2

## Slide 4
RX RSSI
9.6us
Destructive
interference
Constructive
interference
Unintentional beamforming may cause received signal level stays low for 9.6 us
Zero GI
Problem Statement (2/2)
Signal 1
TX antenna 1
TX antenna 2
- Signal 2
Signal 3
- Signal 4
Signal 1
Signal 2
Signal 3
Signal 4
HE-STF
…
HE-STF
…

## Slide 5
Discussions
The diminishing of received power may only happen for short distance and LOS channels with ideal antenna radiation patterns
The current 11az spec draft meets the regulation requirements
WiFi-compliant device will not transmit due to the power diminishing

## Slide 6
Robustness Enhancement ‒ Adding Delayed Signal
Signal 1
TX antenna 1
- Signal 2
Signal 3
- Signal 4
Signal 1
Signal 2
Signal 3
Signal 4
HE-STF
HE-STF
Signal 1’
Signal 2’
Signal 3’
Signal 4’
HE-STF’
TX antenna 2
β •
•
Linear or CSD shifts
TX power splitting and random phase rotation

## Slide 7
No Effect to ToA Measurement
Multipaths for TX antenna 1
β
Multipaths for TX signal
not delayed
Since the delayed transmission only introduces multipaths after the first channel arrival, it doesn’t affect the ToA estimation
Multipaths for TX antenna 2
Multipaths for TX signal
delayed
Delay
Delay
ToA

## Slide 8
Example
Assuming two antennas have the same channel response i.e. 1
Signal 1
TX antenna 1
- Signal 2
Signal 3
- Signal 4
Signal 1
Signal 2
Signal 3
Signal 4
HE-STF
HE-STF
Signal 1’
Signal 2’
Signal 3’
Signal 4’
HE-STF
TX antenna 2
β •
•
RX RSSI
1 •

## Slide 9
Stabilized Received Power
RX RSSI
Assuming two antennas have the same channel response i.e. 1
 |  | Sounding Power Loss
 | (+2.3, -5.3) dB | 1.2 dB
 | (+2.6, -7.4) dB | 0.8 dB
 |  | Sounding Power Loss
 | (+2.3, -5.3) dB | 1.2 dB
 | (+2.6, -7.4) dB | 0.8 dB

## Slide 10
Conclusions
The current secure ranging signal meets the regulation requirements
The effect of the potential unintentional beamforming can be mitigated by transmitting a delayed sounding signal
The solution can be implementation specific such that no spec change is needed