## Slide 1: 802.11 MAC layer support for LC PHY operation
Date: 2019-11-12
Authors:
Name | Affiliations | Address | Phone | Email
Harry Bims | Bims Laboratories, Inc. |  |  | harrybims@me.com
Notes: September 2012

## Slide 2: Abstract
Scope of 802.11 MAC layer changes that support the LC PHY is limited by the LC PAR
  “This amendment specifies changes to the IEEE 802.11 MAC that are limited to the following: 1) Hybrid coordination function (HCF) channel access,
  2) Overlapping basic service set (OBSS) detection and coexistence,
  3) Existing power management modes of operation (excluding new modes), and modifications to other clauses necessary to support these changes.”
We need to clarify the scope of MAC changes includes:
  Changing/adding 802.11 MAC features that affect the LC PHY
  Limiting the optional modes of the 802.11 MAC

## Slide 3: Motivation (1)
TGbb has been discussing two MAC/PHY combinations
  (AX approach): 802.11ax MAC + 802.11ax PHY
    (PHY change necessary to support LC PHY)
  (G.hn approach): 802.11 ?? MAC + G.hn PHY
    (requires more extensive MAC changes)
Both approaches have flaws and advantages
  And both can be supported in the LC MAC layer

## Slide 4: Motivation (2)
However, both approaches will allow many 802.11 MAC features that are not necessary
  Some are optional, some are mandatory
  Can limit unnecessary mandatory features by limiting the MAC to the appropriate 802.11 MAC amendment
  Can limit unnecessary optional features through management layer configuration
G.hn approach will not work without modifying the 802.11 MAC

## Slide 5: Comparison of LC MAC mode Frameworks
802.11ax MAC
802.11ax PHY
Option 1
MAC/PHY layers
802.11 ?? MAC
G.hn PHY
Option 2
MAC/PHY layers
PHY SAP
MLME-PLME SAP
PLME SAP
Message formats
?? PHY SAP
?? MLME-PLME SAP
?? PLME SAP
?? Message formats
Existing
Changed

## Slide 6: Example MAC amendments for consideration
802.11n
  Minimal features to support high throughput
802.11ac
  Enhanced features to support very high throughput
802.11ax
  Maximum features that support future throughput needs

## Slide 7: 802.11n (1)
The IEEE 802.11 HT STA provides
  physical layer (PHY) and medium access control (MAC) features that can support a throughput of 100 Mb/s and greater, as measured at the MAC data service access point (SAP).
Some PHY features that distinguish an HT STA from a non-HT STA are referred to as
  multiple input, multiple output (MIMO) operation;
  spatial multiplexing (SM); spatial mapping (including transmit beamforming);
  space-time block coding (STBC);
  low-density parity check (LDPC) encoding;
  and antenna selection (ASEL).

## Slide 8: 802.11n (2)
An HT STA has MAC features that include
  frame aggregation,
  some Block Ack features,
  power save multi- poll (PSMP) operation,
  reverse direction (RD),
  and protection mechanisms supporting coexistence with non-HT STAs.

## Slide 9: 802.11ac STAs (1)
The IEEE 802.11 VHT STA operates in frequency bands below 6 GHz excluding the 2.4 GHz band.
A VHT STA is an HT STA that, in addition to features supported as an HT STA,
  supports VHT features identified in Clause 8, Clause 9, Clause 10, Clause 13, Clause 18, and Clause 22.

## Slide 10: 802.11ac (2)
The main PHY features in a VHT STA that are not present in an HT STA are the following:
  Mandatory support for 40 MHz and 80 MHz channel widths
  Mandatory support for VHT single-user (SU) PPDUs
  Optional support for 160 MHz and 80+80 MHz channel widths
  Optional support for VHT sounding protocol to support beamforming
  Optional support for VHT multi-user (MU) PPDUs
  Optional support for VHT-MCSs 8 and 9

## Slide 11: 802.11ac (3)
The main MAC features in a VHT STA that are not present in an HT STA are the following:
  Mandatory support for the A-MPDU padding of a VHT PPDU
  Mandatory support for VHT single MPDU
  Mandatory support for responding to a bandwidth indication in a non-HT and non-HT duplicate RTS frame
  Optional support for MPDUs of up to 11 454 octets
  Optional support for A-MPDU pre-end-of-frame (pre-EOF) padding (see 9.12.2 (A-MPDU length limit rules)) of up to 1 048 575 octets
  Optional support for VHT link adaptation

## Slide 12: 802.11ac (4)
Most VHT features, among other benefits, increase the maximum throughput achievable between two VHT STAs over that achievable using HT features alone.
The VHT features are available to VHT STAs associated with a VHT AP in a BSS.
The support for VHT transmit beamforming sounding and VHT MU PPDUs in a VHT AP and more than one VHT STA within a VHT BSS enables the optional use of downlink MU multiple input, multiple output (DL-MU-MIMO).
The use of certain HT features, such as RIFS, is not permitted for STAs operating as VHT STAs.

## Slide 13: 802.11ac (5)
With DL-MU-MIMO the AP can create up to four A-MPDUs, each carrying MPDUs destined for an associated MU-capable STA. The AP uses group identifiers (GIDs) to signal potential recipient STAs. The AP transmits the A-MPDUs simultaneously in separate space-time streams such that each recipient STA is able to demodulate the space-time streams carrying its A-MPDU.
The simultaneous transmission of A-MPDUs in a single VHT MU PPDU provides a means to increase aggregate throughput over that achieved by sending the A-MPDUs in separate SU PPDUs.
The use of certain HT features, such as RIFS, is not permitted for STAs operating as VHT STAs.

## Slide 14: 802.11ax (1)
The IEEE 802.11 HE STA operates in frequency bands between 1 GHz and 7.125 GHz.
The main PHY features in an HE STA that are not present in VHT STA or HT STA are the following:
  Mandatory support for DL MU-MIMO by an HE AP that supports 4 or more spatial streams MU-MIMO is done on the entire PPDU bandwidth
  Mandatory support for DL MU-MIMO reception for a non-AP HE STA
  Mandatory support for the HE sounding protocol to support beamforming
  Optional support for HE-MCSs 10 and 11
  Optional support for UL MU-MIMO
  Optional support for preamble puncturing

## Slide 15: 802.11ax (2)
The main MAC features in an HE STA that are not present in VHT STA or HT STA are the following:
  In an AP, mandatory support for the role of operating mode indication (OMI) responder and optional support for the role of OMI initiator
  In a non-AP STA, optional support for the roles of OMI initiator and responder
  In an AP, optional support for two NAV operation
  In a non-AP STA, mandatory support for two NAV operation
  In an AP, mandatory support for individual target wake time (TWT) operation
  In a non-AP STA, optional support for individual TWT operation
  Optional support for broadcast TWT
  Optional support for UL OFDMA-based random access (UORA)
  Optional support for spatial reuse operation
  Optional support for multi-TID A-MPDU operation
  Optional support for ER BSS
  Mandatory support for multiple BSSID operation in a non-AP STA
  Optional support for the NDP feedback report

## Slide 16: 802.11ax (3)
These features can
  reduce protocol overhead and increase aggregate network throughput (e.g., DL and UL OFDMA, DL/UL MU-MIMO),
  enhance peak link throughput (e.g., MCS 10, 11),
  enhance dense network efficiency (e.g., spatial reuse),
  and/or enhance power conservation (e.g., TWT).
  These features can, under certain circumstances, improve the average throughput per STA in a BSS by a factor of four, compared to VHT.

## Slide 17: Conclusion
It is within the scope of the LC MAC to support both an 802.11ax PHY and a G.hn PHY
  A two mode MAC implementation can resolve the PHY discussions
We should focus MAC proposals
  to 802.11ax, 802.11ac, and 802.11n amendments as candidate starting points
  Recommend 802.11ac for G.hn PHY – reduced complexity while keeping enhanced features of VHT
However, a clarification of the MAC scope is necessary:
  To allow changes so the MAC can properly interface to the LC PHY
  To allow MAC proposals that address the need to simplify the MAC implementation