## Slide 1: Broadcast Ack Operation
Date: 2019-12-03
Authors:
Onn Haran, Autotalks

## Slide 2: Is Broadcast Needed? Only Groupcast?
  Groupcast assures delivery within group: platooning, negotiation
  Groupcast (many-to-many) ≠ Multicast (one-to-many)
  Broadcast assured delivery is valuable as well, for example:
  Left Turn Assistance: A vehicle driving straight would benefit from assured delivery to a vehicle on opposite road about to turn left
  Crossing pedestrian: Assured delivery of cooperative perception message to vehicles approaching the pedestrian
  Assuring Broadcast delivery requires similar effort to Groupcast delivery, so why not adding the value and flexibility?
  Some modifications are needed any way

## Slide 3: Setup and Teardown Should be Eliminated to Scale to All-to-All Negotiation
X
X

## Slide 4: Pre-agreed Parameters
Parameter | Possible values | Pre-agreed value
Policy | Immediate / Delayed | Single recipient message (BlockAck): Immediate Multi-recipient message (if added): Sequenced
Buffer size | 0-1023 | 1 Only content of most recent message is relevant. No reason to acknowledge older messages
The same parameters should be applied by all supporting devices without negotiation

## Slide 5: Capability Support
  Alternative #1: Mandatory
  All NGV devices would be required to respond to BlockAckReq
  Delivery can be always assured
  Alternative #2: Optional
  A bit in NGV MAC header indicates BlockAckReq support
  Flexible
Alternative #2 is recommended

## Slide 6: Naming Convention
  A unique name should represent the dedicated messages
  Block is a bad term since only a single message is acknowledged
  Suggesting BroadcastAck
  BroadcastAckReq
  BroadcastReq
  BroadcastAckReqMR (Multi-Recipients)

## Slide 7: Multiple Requests
  Multiple requests are sent to the stations
  Reminder: stations are identified by upper layer
  Retry when a single station failed to acknowledge
  After retry – No need to send requests to stations previously acknowledged
Broadcast / Groupcast
BroadcastAckReq
Originator
Recipient #1
Recipient #2
BroadcastAck
BroadcastAck
BroadcastAckReq

## Slide 8: BroadcastAckReq Format
Frame control
Octets
2
Duration
2
RA
6
TA
6
BAR control
2
BA information
2
Ack policy
1
Multi-TID
1
Compressed
1
GCR mode
2
Reserved
7
TID
4
Bits
Value
0
0
0
10
0
0
Unused combination
FCS
4
Fragment number
4
Starting sequence number
8
0

## Slide 9: BroadcastAck Format
Frame control
Octet
2
Duration
2
RA
6
TA
6
BAR control
2
BA information
3
FCS
4
Value
As in BlockAckReq
Starting sequence number
2
Bitmap
1
Octet
1 bit reports last message from TA, either Broadcast or Groupcast

## Slide 10: Adjustment to Requested Feedback from Multiple Recipients
From 10.24.3 “Data and acknowledgement transfer using immediate block ack policy and delayed block ack policy”
If an immediate block ack policy is used, the recipient shall respond to a Basic BlockAckReq frame with a Basic BlockAck frame. If the all recipients sends the Basic BlockAck frame, the originator updates its own record and retries any frames that are not acknowledges in the Basic BlockAck frame, either in another block or individually

## Slide 11: Multi-Recipients Request
  Each handshake “wastes” BlockAckRequest duration and SIFS
  Latency further increases by repeated wait for channel access
  Combining BroadcastAckReq into a single message minimizes channel load
  A sequence of up to 8 (TBD) STAs respond sequentially at pre-determined time points
Broadcast / Groupcast
BroadcastAckReqMR
Originator
Recipient #1
Recipient #2
Recipient #3
BroadcastAck
BroadcastAck
BroadcastAck
Other STAs
NAV
2*SIFS+ packet duration
3*SIFS+ 2*packet duration

## Slide 12: BroadcastAckReqMR Format
Frame control
Octets
2
Duration
2
RA
6
TA
6
BAR control
2
BA information
2
Ack policy
1
Multi-TID
1
Compressed
1
GCR
2
Reserved
7
TID
4
Bits
Value
0
0
0
11
0
0
Unused combination
FCS
4
Fragment number
4
Starting sequence number
8
0
Broadcast / groupcast
Number of recipients
Address recipient #1
3
48