## Slide 1: OCB Operation in eBCS
Date: 2019-12-10
Authors:

## Slide 2: Abstract
This presentation provides a summary of the online and offline discussions regarding use of OCB in eBCS, leading to the conclusion that eBCS should make use of GAS public frames and not OCB for transmissions by unassociated STAs.

## Slide 3: Background: Outside the Context of a BSS (OCB)
A mode of operation in which a STA is not a member of a BSS and does not utilize 802.11 authentication, association, or data confidentiality services.
OCB communication is possible only between STAs that are able to communicate directly over the wireless medium.
Introduced in 11p, but not limited to any band
  OCB communication outside of 5.9GHz band, uses LPD
BSSID = wildcard
OCB uses different EDCA default parameters specified
Only mandatory PHY rates guaranteed to be supported, TXOP=0, no synchronization required

## Slide 4: Use of OCB in eBCS (1/2)
For unassociated eBCS communications
  eBCS to be defined as a service over MAC operating in OCB mode
  eBCS AP has a relay (forwarding) function that can intercept eBCS MSDUs and cause them to be sent to eBCS STA and vice versa.
eBCS STA eBCS AP
802.11 STA operating in OCB mode
802.11 AP
802.11 STA operating in OCB mode
eBCS Service
eBCS Service
MAC SAP SAP
eBCS Relay function
Hitoshi

## Slide 5: Use of OCB in eBCS (2/2)
Applicable to unassociated eBCS communications
Requires definition of eBCS service over .11 MAC
Requires definition of eBCS AP architecture consisting of eBCS STA and an AP and a forwarding function
Requires ensuring all the OCB communication rules apply to eBCS and potential gaps are addressed

## Slide 6: Is there an alternative solution?
Use of GAS Public Action frames:
Requires no new definition or architectural changes in AP or STA
Can be used by an associated STA
No specific communication rules outside of existing rules for broadcast transmissions

## Slide 7: Summary and Conclusion
Use of OCB for eBCS unassociated communication is possible, however, it requires definition of eBCS as a service over MAC and specific architecture definition for eBCS AP among other changes.
Hence, given availability of an alternative solution, i.e., use of GAS public action frames, that fits the needs of eBCS without major changes required, it is proposed for eBCS not to rely on OCB for unassociated communication and instead utilize GAS public action frames.

## Slide 8: Backup slides

## Slide 9: MAC Data Plane Architecture
From: IEEE 802.11-13/0115r3
In the non-RSNA case, it seems simple that an AP has a relay (forwarding) function that can intercept received MSDUs and cause them to be sent back out to another associated non-AP STA. This covers the simple, intra-BSS forwarding case.