## Slide 1: EHT RTS and CTS Procedure
Date: 2020-01-10
Authors:

## Slide 2: EHT PHY Support in MAC
Agreed EHT PHY features [1]
  802.11be supports 320 MHz and 160+160 MHz PPDU.
    802.11be needs to support 320 MHz and 160+160 MHz bandwidth indication in the RTS and CTS bandwidth signaling procedure.
  802.11be supports 240 MHz and 160+80 MHz transmission.
    Whether 240/160+80 MHz is formed by 80 MHz channel puncturing of 320/160+160 MHz is TBD.
    802.11be needs to support 240 MHz and 160+80 MHz bandwidth indication in the RTS and CTS bandwidth signaling procedure.

## Slide 3: EHT PHY Support in MAC
Agreed EHT PHY features [1]
  The 802.11be amendment shall support a preamble puncture mechanism for an EHT PPDU transmitted to multiple STAs.
    802.11be needs to define the MU-RTS and CTS frames sent in a non-HT duplicate PPDU with preamble puncturing.
  The 802.11be amendment shall support a preamble puncture mechanism for an EHT PPDU transmitted to a single STA.
    802.11be needs to define the RTS and CTS frames sent in a non-HT duplicate PPDU with preamble puncturing.

## Slide 4: EHT PHY Support in MAC
In order to support 240/160+80/320/160+160 MHz bandwidth and the preamble puncture mechanism, a new EHT RTS and CTS frames are proposed.
  The EHT RTS and CTS frames can be a new Control frame.
    Because only Subtype 1 and 15 in Control Type are only available, another extension frame that is similar to the Control Frame Extension of 802.11ad/ay can be defined.

## Slide 5: EHT RTS and CTS Procedure
A TXOP holder may transmit to a TXOP responder an EHT RTS frame in a non-HT duplicate PPDU with the following TXVECTOR parameters:
  CH_BANDWIDTH: CBW40, CBW80, CBW160, CBW80+80, CBW240, CBW160+80, CBW320, CBW160+160.
  INACTIVE_SUBCHANNELS: Indicates the 20 MHz subchannels that are punctured, if present.

## Slide 6: EHT RTS and CTS Procedure
The TXOP holder shall not transmit the EHT RTS frames on 20 MHz subchannels on which CCAs are busy.
  The TXOP holder indicates in the Disallowed Subchannel Bitmap field the 20 MHz subchannels on which the EHT RTS frames are not sent.
    For example, bit field corresponding to 20 MHz subchannel on which the EHT RTS frame is not sent is set to 1. Otherwise, it is set to 0.
  The TXOP responder is disallowed to transmit the EHT CTS response on the 20 MHz subchannels indicated in the Disallowed Subchannel Bitmap field in the EHT RTS frame.
Frame Control | Duration | RA | TA | Disallowed Subchannel Bitmap | FCS
2 octets | 2 octets | 6 octets | 6 octets | 2 octets | 4 octets
<EHT RTS frame format>

## Slide 7: EHT RTS and CTS Procedure
The TXOP responder transmits to the TXOP holder an EHT CTS frame in a non-HT duplicate PPDU with the following TXVECTOR parameters:
  CH_BANDWIDTH: CBW40, CBW80, CBW160, CBW80+80, CBW240, CBW160+80, CBW320, CBW160+160.
  INACTIVE_SUBCHANNELS: Indicates the 20 MHz subchannels that are punctured, if present.
The TXOP responder can transmit the EHT CTS frame on only 20 MHz subchannels in which the TXOP holders sent the EHT RTS frames.

## Slide 8: EHT RTS and CTS Procedure
The TXOP responder shall not transmit the EHT CTS frames on 20 MHz subchannels of which CCAs are busy.
  The TXOP responder indicates in the Disallowed Subchannel Bitmap field the 20 MHz subchannels on which the EHT CTS frames are not sent.
    For example, bit field corresponding to 20 MHz subchannel on which the EHT CTS frame is not sent is set to 1. Otherwise, it is set to 0.
  The TXOP holder is disallowed to transmit frames on the 20 MHz subchannels indicated in the Disallowed Subchannel Bitmap field in the EHT CTS frame.
Frame Control | Duration | RA | Disallowed Subchannel Bitmap | FCS
2 octets | 2 octets | 6 octets | 2 octets | 4 octets
<EHT CTS frame format>

## Slide 9: EHT RTS and CTS Procedure
For example, the TXOP holder solicits the EHT CTS response on the primary 80 MHz and secondary 80 MHz channel. But, since the TXOP holder indicates that the upper 20 MHz channel of the secondary 40 MHz channel is the disallowed subchannel, the TXOP responder replies with the EHT CTS frame on idle channels excluding the corresponding disallowed subchannel.
At the TXOP responder, CCA is busy.
Primary 80 MHz
Secondary 80MHz
SIFS
PIFS
PIFS
PIFS
PIFS
PIFS
Preamble punctured SU PPDU
At the TXOP holder, CCA is busy.
Preamble punctured SU PPDU
ACK
ACK
ACK
ACK
ACK
SIFS
SIFS
EHT RTS
EHT RTS
EHT RTS
EHT RTS
EHT RTS
EHT RTS
EHT CTS
EHT CTS
EHT CTS
PIFS
EHT RTS
EHT CTS
EHT CTS

## Slide 10: EHT MU-RTS and CTS Procedure
An AP that is a TXOP holder may transmit to one or more non-AP STAs an EHT MU-RTS Trigger frame in a non-HT duplicate PPDU with the following TXVECTOR parameters:
  CH_BANDWIDTH: CBW40, CBW80, CBW160, CBW80+80, CBW240, CBW160+80, CBW320, CBW160+160.
  INACTIVE_SUBCHANNELS: Indicates the 20 MHz subchannels that are punctured, if present.

## Slide 11: EHT MU-RTS and CTS Procedure
The AP shall not transmit the EHT MU-RTS frames on 20 MHz subchannels of which CCAs are busy.
  The EHT MU-RTS Trigger frame includes the Disallowed Subchannel Bitmap subfield in the User Info field whose the AID12 subfield is set to 2047.
  The AP indicates in the Disallowed Subchannel Bitmap subfield the 20 MHz subchannels on which the EHT MU-RTS frames are not sent.
    For example, bit field corresponding to 20 MHz subchannel on which the EHT MU-RTS frame is not sent is set to 1. Otherwise, it is set to 0.
  The non-AP STA is disallowed to transmit the CTS response on the 20 MHz subchannels indicated in the Disallowed Subchannel Bitmap field in the EHT MU-RTS frame.

## Slide 12: EHT MU-RTS and CTS Procedure
The non-AP STA transmits to the AP a CTS frame in a non-HT duplicate PPDU with the following TXVECTOR parameters:
  CH_BANDWIDTH: CBW40, CBW80, CBW160, CBW80+80, CBW240, CBW160+80, CBW320, CBW160+160.
    The RU Allocation subfield in the User Info field addressed to the non-AP STA determines CH_BANDWIDTH parameter.
  INACTIVE_SUBCHANNELS: Indicates the 20 MHz subchannels that are punctured, if present.
The non-AP can transmit the CTS frame on only 20 MHz subchannels in which the AP sent the EHT MU-RTS frames, subject to other rules 26.2.6 (MU-RTS Trigger/CTS frame exchange procedure).

## Slide 13: EHT MU-RTS and CTS Procedure
For example, the AP solicits the CTS response on the primary 80 MHz and secondary 80 MHz channel. But, since the AP indicates that the upper 20 MHz channel of the secondary 40 MHz channel is the disallowed subchannel, the STA responds with the CTS frame on idle channels excluding the corresponding disallowed subchannel.
Primary 80 MHz
Secondary 80MHz
SIFS
PIFS
PIFS
PIFS
PIFS
PIFS
Preamble punctured MU PPDU
At the TXOP holder, CCA is busy.
Preamble punctured MU PPDU
TB PPDU
TB PPDU
TB PPDU
TB PPDU
TB PPDU
TB PPDU
SIFS
SIFS
MU-RTS
MU-RTS
MU-RTS
MU-RTS
MU-RTS
MU-RTS
CTS
CTS
CTS
PIFS
TB PPDU
MU-RTS
CTS
CTS
CTS
CTS

## Slide 14: Conclusion
802.11be can efficiently utilize more wider 240/160+80/320/160+160 MHz bandwidth through the preamble puncture mechanism.
  Because the chance that continuous channels of 240/320 MHz are idle is very low.
This submission proposes the RTS and CTS support for the preamble puncture mechanism (including a support of new bandwidth modes).
  Additional information to help other EHT features (e.g., the multi-link operation) can be exchanged through the HE RTS and CTS procedure.
  Other control frames (e.g., BlockAckReq and BlockAck, etc.) that can have the bandwidth signaling TA also need similar updates.

## Slide 15: References
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-1262-05-00be-specification-framework-for-tgbe.docx

## Slide 16: Straw Poll 1
Do you support to define the (MU-)RTS and CTS procedure for 240/160+80/320/160+160 MHz bandwidth and the preamble puncture mechanism?