## Slide 1: EHT RTS and CTS Procedure
Date: 2020-03-13
Authors:

## Slide 2: EHT PHY Support in MAC
Agreed EHT PHY features [1]
  802.11be supports 320 MHz and 160+160 MHz PPDU.
    802.11be needs to support 320 MHz and 160+160 MHz bandwidth indication in the RTS and CTS bandwidth signaling procedure.
  802.11be supports 240 MHz and 160+80 MHz transmission.
    Whether 240/160+80 MHz is formed by 80 MHz channel puncturing of 320/160+160 MHz is TBD.
    802.11be needs to support 240 MHz and 160+80 MHz bandwidth indication in the RTS and CTS bandwidth signaling procedure.

## Slide 3: EHT PHY Support in MAC
Agreed EHT PHY features [1]
  The 802.11be amendment shall support a preamble puncture mechanism for an EHT PPDU transmitted to multiple STAs.
    802.11be needs to define the MU-RTS and CTS frames sent in a non-HT duplicate PPDU with preamble puncturing.
  The 802.11be amendment shall support a preamble puncture mechanism for an EHT PPDU transmitted to a single STA.
    802.11be needs to define the RTS and CTS frames sent in a non-HT duplicate PPDU with preamble puncturing.

## Slide 4: Recap: BW indication and negotiation with >160MHz PPDU [2]
Proposed solutions
  Update RTS/CTS
    Additional one bit in Service field of non-HT duplicate PPDU to indicates >160MHz BW or BW unit in 40MHz.
  The HE/EHT Control field, e.g. Trigger + QoS Null, indicates the >160MHz BW.
  MU-RTS + CTS method.
    MU RTS in non-HT duplicate PPDU indicates the BW and possibly the punctured RUs through the frame body.
  The Control frame content in new defined control frame indicates the BW.
In order to support the punctured channel, we prefer to define new EHT RTS and CTS frames.

## Slide 5: EHT RTS and CTS Procedure
A TXOP holder may transmit to a TXOP responder an EHT RTS frame in a non-HT duplicate PPDU with the following TXVECTOR parameters:
  CH_BANDWIDTH: CBW40, CBW80, CBW160, CBW80+80, CBW240, CBW160+80, CBW320, CBW160+160.
  INACTIVE_SUBCHANNELS: Indicates the 20 MHz subchannels that are punctured, if present.

## Slide 6: EHT RTS and CTS Procedure
The TXOP holder shall not transmit the EHT RTS frames on 20 MHz subchannels on which CCAs are busy.
  The TXOP holder indicates in the Punctured Channel Information the 20 MHz subchannels on which the EHT RTS frames are not sent.
  The TXOP responder is disallowed to transmit the EHT CTS response on the 20 MHz subchannels indicated in the Punctured Channel Information in the EHT RTS frame.
Frame Control | Duration | RA | TA | Punctured Channel Information | FCS
2 octets | 2 octets | 6 octets | 6 octets | TBD | 4 octets
<EHT RTS frame format>

## Slide 7: EHT RTS and CTS Procedure
The TXOP responder transmits to the TXOP holder an EHT CTS frame in a non-HT duplicate PPDU with the following TXVECTOR parameters:
  CH_BANDWIDTH: CBW40, CBW80, CBW160, CBW80+80, CBW240, CBW160+80, CBW320, CBW160+160.
  INACTIVE_SUBCHANNELS: Indicates the 20 MHz subchannels that are punctured, if present.
The TXOP responder can transmit the EHT CTS frame on only 20 MHz subchannels in which the TXOP holders sent the EHT RTS frames.

## Slide 8: EHT RTS and CTS Procedure
The TXOP responder shall not transmit the EHT CTS frames on 20 MHz subchannels of which CCAs are busy.
  The TXOP responder indicates in the Punctured Channel Information the 20 MHz subchannels on which the EHT CTS frames are not sent.
  The TXOP holder is disallowed to transmit frames on the 20 MHz subchannels indicated in the Punctured Channel Information in the EHT CTS frame.
Frame Control | Duration | RA | Punctured Channel Information | FCS
2 octets | 2 octets | 6 octets | TBD | 4 octets
<EHT CTS frame format>

## Slide 9: EHT RTS and CTS Procedure
For example, the TXOP holder solicits the EHT CTS response on the primary 80 MHz and secondary 80 MHz channel. But, since the TXOP holder indicates that the upper 20 MHz channel of the secondary 40 MHz channel is the disallowed subchannel, the TXOP responder replies with the EHT CTS frame on idle channels excluding the corresponding disallowed subchannel.
At the TXOP holder, CCA is busy.
Primary 80 MHz
Secondary 80MHz
SIFS
PIFS
PIFS
PIFS
PIFS
Preamble punctured SU PPDU
At the TXOP holder, CCA is busy.
ACK
ACK
ACK
SIFS
SIFS
EHT RTS
EHT RTS
EHT RTS
EHT RTS
EHT RTS
EHT CTS
EHT CTS
EHT CTS
PIFS
EHT RTS

## Slide 10: EHT MU-RTS and CTS Procedure
An AP that is a TXOP holder may transmit to one or more non-AP STAs an EHT MU-RTS Trigger frame in a non-HT duplicate PPDU with the following TXVECTOR parameters:
  CH_BANDWIDTH: CBW40, CBW80, CBW160, CBW80+80, CBW240, CBW160+80, CBW320, CBW160+160.
  INACTIVE_SUBCHANNELS: Indicates the 20 MHz subchannels that are punctured, if present.

## Slide 11: EHT MU-RTS and CTS Procedure
The AP shall not transmit the EHT MU-RTS frames on 20 MHz subchannels of which CCAs are busy.
  The EHT MU-RTS Trigger frame includes the Disallowed Subchannel Bitmap subfield in the User Info field whose the AID12 subfield is set to 2047.
  The AP indicates in the Disallowed Subchannel Bitmap subfield the 20 MHz subchannels on which the EHT MU-RTS frames are not sent.
    For example, bit field corresponding to 20 MHz subchannel on which the EHT MU-RTS frame is not sent is set to 1. Otherwise, it is set to 0.
  The non-AP STA is disallowed to transmit the CTS response on the 20 MHz subchannels indicated in the Disallowed Subchannel Bitmap field in the EHT MU-RTS frame.

## Slide 12: EHT MU-RTS and CTS Procedure
The non-AP STA transmits to the AP a CTS frame in a non-HT duplicate PPDU with the following TXVECTOR parameters:
  CH_BANDWIDTH: CBW40, CBW80, CBW160, CBW80+80, CBW240, CBW160+80, CBW320, CBW160+160.
    The RU Allocation subfield in the User Info field addressed to the non-AP STA determines CH_BANDWIDTH parameter.
  INACTIVE_SUBCHANNELS: Indicates the 20 MHz subchannels that are punctured, if present.
The non-AP can transmit the CTS frame on only 20 MHz subchannels in which the AP sent the EHT MU-RTS frames, subject to other rules 26.2.6 (MU-RTS Trigger/CTS frame exchange procedure).

## Slide 13: EHT MU-RTS and CTS Procedure
For example, the AP solicits the CTS response on the primary 80 MHz and secondary 80 MHz channel. But, since the AP indicates that the upper 20 MHz channel of the secondary 40 MHz channel is the disallowed subchannel, the STA responds with the CTS frame on idle channels excluding the corresponding disallowed subchannel.
Primary 80 MHz
Secondary 80MHz
SIFS
PIFS
PIFS
PIFS
PIFS
PIFS
Preamble punctured MU PPDU
At the TXOP holder, CCA is busy.
Preamble punctured MU PPDU
TB PPDU
TB PPDU
TB PPDU
TB PPDU
TB PPDU
TB PPDU
SIFS
SIFS
MU-RTS
MU-RTS
MU-RTS
MU-RTS
MU-RTS
MU-RTS
CTS
CTS
CTS
PIFS
TB PPDU
MU-RTS
CTS
CTS
CTS
CTS

## Slide 14: Conclusion
802.11be can efficiently utilize more wider 240/160+80/320/160+160 MHz bandwidth through the preamble puncture mechanism.
  Because the chance that continuous channels of 240/320 MHz are idle is very low.
This submission proposes the RTS and CTS support for the preamble puncture mechanism (including a support of new bandwidth modes).

## Slide 15: References
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-1262-05-00be-specification-framework-for-tgbe.docx
[2] https://mentor.ieee.org/802.11/dcn/20/11-20-0062-00-00be-protection-with-more-than-160mhz-ppdu-and-puncture-operation.pptx

## Slide 16: Straw Poll 1
Do you support to transmit the MU-RTS/RTS and CTS frames in a non-HT duplicate PPDU on 20 MHz subchannels which are not punctured?

## Slide 17: Straw Poll 2
Do you support that the MU-RTS frame can signal the punctured 20 MHz subchannels on which the MU-RTS frames are not sent?