## Slide 1: Multi-link Acknowledgement Follow Up
Date: 2020-01-13
Authors:
Name | Affiliation | Address | Phone | Email
Taewon Song | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | taewon.song@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Sungjin Park |  |  |  | allean.park@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Namyeong Kim |  |  |  | namyeong.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Overview
We have addressed multi-link acknowledgement methods in multi-link environment in [1-3]
On the other hand, multi-link operation constraint issue has been raised in [4, 5]
In this contribution...
  We address potential internal tx/rx interference situations for non-STR non-AP MLD
  We then suggest practical proposals to mitigate the problem mentioned above

## Slide 3: Recap on candidate multi-link ack methods [1]
Per-link acknowledgement
  A recipient responds with an acknowledgement on the same link where the reception operation occurred
  It is independent of multi-link environment and synchronization mode
Single aggregated acknowledgement
  An acknowledgement frame can contain ack information of multiple links
  A recipient may or may not respond with the aggregated acknowledgements on its own link
  Relatively low reliability and high throughput gain
Aggregated acknowledgement with duplication
  Duplicated acknowledgement frames containing ack information of multiple links are transmitted simultaneously over multiple links
  High reliability due to the redundant acknowledgement information

## Slide 4: Recap on non-AP’s constraints [4, 5]
Simultaneous transmit-receive (STR) constraint
  Non-AP may not be capable due to in-device power leakage from insufficient frequency separation
  Example: Link A operating in lower 5 GHz and link B operating in upper 5 GHz

## Slide 5: Assumptions
We assume that AP MLD is capable of STR
On the other hand, we assume that non-AP MLD is not capable of STR
We only consider downlink traffic; from AP MLD to non-AP MLD
In this scenario, starting time of PPDU on each link does not need to be necessarily aligned

## Slide 6: Problem: STR situation may occur during transmission
In case of immediate response (e.g., implicit BAR ack policy), internal tx/rx interference may occur without any alignment of the transmissions (See left figure)
Even if all data frames have to solicit delayed response (e.g., Block Ack ack policy), internal tx/rx interference can also occur during the exchange of BlockAckReq frame and BlockAck frame (See right figure)
: Internal tx/rx interference
Non-AP MLD
(Non STR link set)
AP MLD
(STR link set)
Data A1
Data A1
Data B1
Data B1
Link A
Link B
Link A
Link B
BA
BA
: Short inter-frame space
Non-AP MLD
(Non STR link set)
AP MLD
(STR link set)
Data A1
Data A1
Data B1
Data B1
Link A
Link B
Link A
Link B
BAR
BAR
BAR
BAR
BA
BA
BA
BA
: Backoff

## Slide 7: Proposal 1: End time alignment
STR situation can be alleviated with end time alignment of transmissions on the links
  With the aligned transmissions, immediate responses become available
Transmission information (E.g., PPDU transmission start time of other links, PPDU duration of other links) should be shared between the STAs of the AP MLD to append padding or limit the length of following data frame
Due to the additional padding, channel efficiency may decrease
Fragmentation may be happen in case when the end time of the latter data frame is later than the former data frame (See right figure)
Per-link acknowledgement is suitable for this proposal
  Aggregated acknowledgement can also be used as long as non-AP MLD is capable of ack aggregation
Data A1
Data A1
Data B1
Data B1
BA
BA
Padding
Padding
BA
BA
Data A1
Data A1
Data B1
Data B1
BA
BA
BA
BA
(ML) Implicit BAR
(ML) Implicit BAR
(ML) Implicit BAR
(ML) Implicit BAR
Non-AP MLD
(Non STR link set)
AP MLD
(STR link set)
Link A
Link B
Link A
Link B
Non-AP MLD
(Non STR link set)
AP MLD
(STR link set)
Link A
Link B
Link A
Link B

## Slide 8: Proposal 2: Restriction on ack policy
If end times are not aligned, ack policy may need to be restricted
  Specifically, normal Ack and Implicit BAR ack policies may be prohibited when the non-AP MLD does not support STR capability since they require immediate responses
Since asynchronized per-link acknowledgement may cause STR situation as well, BAR – BA exchange on the only one link can reduce internal tx/rx interference
  Ack designated link can be negotiated in advance or on each occasion
Therefore, in this proposal, acknowledgement information sharing among the STAs of non-AP MLD and allowing the non-AP MLD to response other links’ acknowledgement information can help increase channel efficiency by releasing channel
  Non-AP MLD may have plenty of time to share acknowledgement information (e.g., scoreboarding)
  Negotiating ack information sharing capability between AP MLD and non-AP MLD may also be helpful
  Immediate aggregated response without BAR frame is possible if acknowledgement information can be aggregated and the aggregated ack frame can be formed within SIFS period
Data A1
Data A1
Data B1
Data B1
BA
BAR
BAR
Block Ack
Block Ack
BA
Non-AP MLD
(Non STR link set)
AP MLD
(STR link set)
Link A
Link B
Link A
Link B

## Slide 9: Summary
We addressed acknowledgement issues especially when non-AP MLD is not capable of STR
We may align end time of PPDUs to prevent STR situation
  For this proposal, transmission information, such as PPDU transmission start time of other links or PPDU duration of other links, needs to be shared among the STAs in a same MLD
Even if the end times are not aligned, we can prevent an STR situation in a non-STR non-AP MLD by prohibiting an immediate response to a corresponding PPDU
  Further, with acknowledgement information sharing among receiver’s links, channel can be used much efficiently

## Slide 10: References
[1] 19/1887r0, “Multi-link Acknowledgement”
[2] 19/1512r6, “Multi-link acknowledgement”
[3] 19/1532r1, “Discussion on multi-link acknowledgement”
[4] 19/1405r7, “Multi-link Channel Access Discussion”
[5] 19/1836r0, “Multi-link Channel Access Discussion Follow-up”

## Slide 11: SP #1
Do you agree to add the following text to the 11be SFD?
  If end times of DL PPDUs, each of which is destined to a STA affiliated with a same non-STR non-AP MLD, are not aligned, ack policies of QoS data frames in the PPDUs may be constrained (e.g., ack policy is not set to 00).
    How to restrict ack policy is TBD.

## Slide 12: SP #2
Do you agree to add the following text to the 11be SFD?
  A non-AP MLD can notify an AP MLD whether a STA of the non-AP MLD can get acknowledge information (e.g., scoreboarding) from other STA(s) within the same non-AP MLD and can form an aggregated acknowledgement frame or not.
    Aggregated acknowledgement frame can contain the ack information of other link(s)