## Slide 1: 11be PPDU format
Date: 2020-01-13
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jan. 2020

## Slide 2: Introduction
In the previous F2F meeting, we made decisions about the Signal field such as following.
  RL-SIG field
    immediately following the L-SIG field.
  U-SIG field
    immediately after the RL-SIG in 11be preamble
    is consists of 2 OFDM symbols jointly encoded.
    contains both version independent fields and version dependent fields
  EHT-SIG field
    immediately after the U-SIG
    in an EHT PPDU sent to multiple users shall have a common field and user-specific field(s)
In 11be PPDU, we can consider the various type of PPDU formats such as SU, MU, TB, ER-SU as in 11ax.
Thus, in this contribution, we discuss consideration for the signal field according to 11be PPDU format as well as an indication of PPDU format.

## Slide 3: 11be preamble
Basic concept of 11be preamble
  U-SIG is similar to HE-SIGA in 11ax PPDU
For multiple user transmission
  Here, EHT-SIG field is similar to HE-SIGB in 11ax PPDU

## Slide 4: PPDU Format indication
11be targets a variety of use cases/applications so may require different PPDU formats similar to 11ax, i.e. SU/MU/TB/ER-SU.
  Other PPDU format is TBD.
Because PPDU has a different configuration according to PPDU format, the PPDU format should be indicated for the correct decoding of received PPDU.
In 11ax, for the indication of PPDU format, step by step indication is applied by using the value of Length mod 3 and format indication bit in HE-SIGA.
But, since the Length field value in L-SIG sets to Length mod 3 = 0, the similar indication way can not be used in 11be.
So, for the indication of PPDU format, we suggest using some bits in the U-SIG.
  The bits for indication of PPDU format may consist of 2 or 3 bits and included in version dependent fields of U-SIG field.

## Slide 5: U-SIG (1/2)
As described in [1], U-SIG is composed of 2 OFDM symbols and contains following fields.
  Version independent fields can be composed including below information
    PHY version identifier: 3 bits
    UL/DL flag: 1 bit.
    BSS color : more than 6bits considered.
    TXOP duration : more than 7bits considered.
  At least more than 17 bits are required to accommodate above information.
  Also, the version dependent fields can consist of the similar information included in HE-SIGA except the information included in the independent fields as well as new information fields.
    Except for the tail and CRC, it is possible to use equal to or less than 25 bits to accommodate the version dependent information if we reuse the concept of extra tones as in 11ax.

## Slide 6: U-SIG (2/2)
We can consider following various information as the version dependent fields.
  For example,
    HE-SIGA like information in SU
      BW(>2), MCS(4), STBC(1), Spatial Reuse(4), Beam Change(1), DCM(1), GI+LTF(2), NSTS and MP(>3), Coding(1), LDPC Extra Symbol(1), Beamformed(1), Pre-FEC Padding(2), PE Disambiguity(1), Doppler(1)
    New information
      Format indication, functionality (e.g., HARQ, Multi-AP operation), etc.
  and, as described in appendix(slides 21-22), according to PPDU format, the contents and size of bits for version dependent information can be different.
But, due to the limitation of room for U-SIG, U-SIG can not contain all information addressed above.
Therefore, to accommodate all common signaling considered in 11be transmission, we need to consider the additional method in addition to the U-SIG field.

## Slide 7: Consideration for additional signaling method
We can consider the following way to contain the information that is not included in the U-SIG.
  Reusing the EHT-SIG field which is defined for multiple user transmission in 11be SFD.
    The overflowed version dependent information from U-SIG can be included in common fields of EHT-SIG.
      The common fields include one CRC and tail bits
    It is possible to unify PPDU formats for some PPDU types, for example, SU PPDU and MU PPDU, by using the EHT-SIG field after U-SIG.
      The composition of EHT-SIG can be different depending on the PPDU format sent because SU doesn’t require user-specific fields.
In the next slides, we more discuss how to design the PPDU format of EHT by considering the SIG field configuration.

## Slide 8: EHT SU PPDU format
For the SU transmission, SU PPDU can have the following format by taking into account the SIG configuration.
  Similar to multiple user transmission, SU PPDU includes the EHT-SIG field after U-SIG.
  But, EHT-SIG field is composed of only the common field part without user-specific fields.
    The common field can consist of version dependent information and common information.
    This field shall be BCC encoded at rate, R=1/2, and modulated with the BPSK and includes one CRC and tail bits.
    In addition, it can support the multi-RU allocation or preamble puncturing in SU transmission without additional signal field.
    This field is TBD in size, but may consist of 1 or 2 OFDM symbols considering the information included.
  The composition of the EHT-SIG field can be configured by using the format indication bits in U-SIG.

## Slide 9: EHT MU PPDU format
For EHT MU PPDU, we can consider the following structure.
  MU PPDU contains the 2 SIG fields (U-SIG and HE-SIG)
    As in [1], the EHT-SIG field consists of Common fields and User-specific fields.
      EHT-SIG can be composed of various number of OFDM symbols.
    EHT-SIG shall be encoded by BCC and can be modulated with various MCSs.
      MCS of EHT-SIG is indicated by using the version dependent bits in U-SIG.
    As described in slide 7, some of version dependent information should be included in common field of EHT-SIG.
      The common field can consist of two information bits (i.e., version depend bits and common bits for MU)
      The One CRC and tail bits can be applied to the common field.
    The user specific field consists of zero or several user block fields
      Each user block (e.g. like in 11ax) includes one CRC and tail bits.

## Slide 10: EHT TB PPDU format
HE-SIGA in 11ax TB PPDU already has the 10 reserved bits.
In 11be, to compose the U-SIG, this free room can be used for containing new information bits and extension of some information bits, for example, TXOP,BSS color, BW.
  And, some existing information may be excluded to allow more bits.
    Need more discussion on which information is included or excluded in 11be
So, since we can contain all needed information in U-SIG, EHT TB PPDU can be constructed by the following format.
  EHT TB PPDU only contains the U-SIG as the Signal field.
  It has equal signaling overhead compared to 11ax.

## Slide 11: EHT ER SU PPDU format
To provide at least equivalent coverage with 11ax, we can consider the EHT ER SU PPDU format in 11be transmission.
  Similar with 11ax, the SIG fields in EHT SU PPDU can be repeated for range extension.
So, for the ER SU PPDU format, we can consider the following configuration.
    In this format, the sizes of U-SIG field and EHT-SIG field are twice as the U-SIG field and EHT-SIG field in EHT SU PPDU format, respectively.
    The details on the repetition of U-SIG and EHT-SIG are TBD.

## Slide 12: Conclusion
11be can have various PPDU formats such as SU, MU, TB, ER-SU as in 11ax.
For the indication of these PPDU formats, U-SIG includes the information bits for differentiating PPDU formats.
  PPDU format indication field can consist of 2 or 3 bits.
  If the unified PPDU format is used for SU and MU transmission, it can configure the composition of the EHT-SIG field.
We proposed the following EHT PPDU formats for SU, MU, TB, ER-SU.
  EHT SU PPDU
    L-STF/L-LTF/L-SIG/RL-SIG/U-SIG/EHT-SIG/EHT-STF/EHT-LTF/DATA
  EHT MU PPDU
    L-STF/L-LTF/L-SIG/RL-SIG/U-SIG/EHT-SIG/EHT-STF/EHT-LTF/DATA
  EHT TB PPDU
    L-STF/L-LTF/L-SIG/RL-SIG/U-SIG/EHT-STF/EHT-LTF/DATA
  EHT ER SU PPDU
    L-STF/L-LTF/L-SIG/RL-SIG/U-SIG/EHT-SIG/EHT-STF/EHT-LTF/DATA
      The size of U-SIG and EHT-SIG are twice as the ones in EHT SU PPDU

## Slide 13: Straw poll 1
Do you agree to add the following into the 11be SFD?
  The extra 4 subcarriers are applied to L-SIG and RL-SIG.
    The indices for extra subcarriers are [-28, -27, 27, 28]
    The extra subcarriers are BPSK modulated
    The coefficients [-1 -1 -1 1 ] as in 11ax are mapped to the extra subcarriers
  Y/N/A: 32/0/0

## Slide 14: Straw poll 2
Do you agree to add the following into the 11be SFD?
  11be has the four PPDU formats, i.e., SU PPDU, MU PPDU, TB PPDU, ER SU PPDU.
    Other PPDU format is TBD
    Deferred

## Slide 15: Straw poll 3
Do you agree to add the following into the 11be SFD?
  The version dependent field of U-SIG includes the information field for indicating the PPDU format.
    Size of the information field for format indication is TBD
    Withdrawn

## Slide 16: Straw poll 4
Do you agree that EHT SU PPDU format is configured as following?
  EHT-SU PPDU consists of L-STF, L-LTF, L-SIG, RL-SIG, U-SIG, EHT-SIG, EHT-STF, EHT-LTF, DATA
  EHT-SIG field contains only common field.
    Common field contains the version dependent information.
    This field shall be encoded by BCC at rate, R=1/2, and modulated with BPSK.
    The size of EHT-SIG field is TBD.
    Deferred

## Slide 17: Straw poll 5
Do you agree that one PPDU that is sent to multiple user is configured as following?
  L-STF, L-LTF, L-SIG, RL-SIG, U-SIG, EHT-SIG, EHT-STF, EHT-LTF, DATA
    Additional fields are TBD
Y/N/A: 33/0/1

## Slide 18: Straw poll 6
Do you agree that EHT TB PPDU format is configured as following?
  EHT TB PPDU consist of L-STF, L-LTF, L-SIG, RL-SIG, U-SIG, EHT-STF, EHT-LTF, DATA
  Additional fields are TBD
  Y/N/A - 19/ 2/ 7

## Slide 19: Straw poll 7
Do you agree that EHT-ER SU PPDU is configured as following?
  EHT ER-SU PPDU consists of L-STF, L-LTF, L-SIG, RL-SIG, U-SIG, EHT-SIG, EHT-STF, EHT-LTF, DATA
    The sizes of U-SIG field and EHT-SIG field are twice as the U-SIG field and EHT-SIG field in EHT SU PPDU format, respectively
    The detail on the repetition of U-SIG and EHT-SIG is TBD
    Deferred

## Slide 20: Motion 1
Move to add the following text into 11be SFD:
  The extra 4 subcarriers are applied to L-SIG and RL-SIG.
    The indices for extra subcarriers are [-28, -27, 27, 28]
    The extra subcarriers are BPSK modulated
    The coefficients [-1 -1 -1 1 ] as in 11ax are mapped to the extra subcarriers
  Mover : Dongguk Lim

## Slide 21: Motion 2
Move to add the following text into 11be SFD:
  One PPDU format that is sent to multiple users is configured as L-STF, L-LTF, L-SIG, RL-SIG, U-SIG, EHT-SIG, EHT-STF, EHT-LTF, DATA
    Additional fields are TBD
  Mover : Dongguk Lim

## Slide 22: Reference
[1] IEEE 802.11-19/1262r6, Specification Framework for TGbe

## Slide 23: Appendix-HE-SIGA contents (1/2)
SU PPDU and ER SU PPDU
field | bit
Format | 1
beam change | 1
DL/UL | 1
MCS | 4
DCM | 1
BSS Color | 6
reserved | 1
spatial reuse | 4
BW | 2
GI+LTF | 2
NSTS and MP | 3
TXOP | 7
Coding | 1
LDPC Extra symbol | 1
STBC | 1
Beamformed | 1
Pre-FEC padding | 2
PE Disambiguity | 1
reserved | 1
doppler | 1
CRC | 4
Tail | 6

## Slide 24: Appendix-HE-SIGA contents (2/2)
MU PPDU
TB PPDU
field | bit
UL/DL | 1
SIGB-MCS | 3
SIB-DCM | 1
BSS color | 6
SR | 4
BW | 3
Number of SIGB symbols or MU-MIMO users | 4
SIB compression | 1
GI+LTF | 2
doppler | 1
TXOP | 7
reserved | 1
number of LTF symbols and MP | 3
LDPC Extra symbol | 1
STBC | 1
Pre-FEC padding | 2
PE Disambiguity | 1
CRC | 4
Tail | 6
field | bit
Format | 1
BSS color | 6
SR1 | 4
SR2 | 4
SR3 | 4
SR4 | 4
reserved | 1
BW | 2
TXOP | 7
reserved | 9
CRC | 4
Tail | 6