## Slide 1: MLO: Acknowledgement Procedure
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
George Cherian | Qualcomm Inc. |  |  | 
Duncan Ho | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Date: 2020-01-06

## Slide 2: Overview
Past contributions [1, 2, 3] have discussed the benefits of multi-link operation and the need for a unified framework to support various aspects of the feature.
Contributions [2, 4] have proposed to increase BA Bitmap length to at least 1024 to account for increases in peak throughput
Further, contributions [2, 4, 5] propose to have a single block ack setup and common sequence number space for multiple links
This contribution continues the discussion on multi-link acknowledgement procedure and highlight some of the challenges in gathering cross-link Rx status

## Slide 3: Motivation
MLO framework needs to account for MLDs with STAs that do not exchange information instantaneously
  A STA of an MLD may not have knowledge of the most recently received (or transmitted) MPDUs by another STA of that MLD
  Hence, unable to provide SIFS based responses on-behalf of the other STA
Further MPDUs may be in transit on one link when a BA is being sent on another link
Multi-link BA framework needs to consider these constraints in the design

## Slide 4: Baseline BA procedure
Today, in a single link case, the originator solicits Rx status for MPDUs that it has transmitted.
Recipient STA indicates successful reception for an MPDU by setting the bit position for that MPDU to 1 in the BA bitmap
  Since the originator knows which MPDUs it has transmitted so far, there is no ambiguity when a 1 or a 0 is received.
Some contributions (e.g., [4, 6, 7]) have suggested that a single BA could acknowledge MPDUs received on multiple links
  However, in case of multi-link operation, there is an ambiguity when gathering cross-link Rx-status as we describe in following slides.

## Slide 5: BA procedure with multi-link
In multi-link operation, at the originator MLD, the MPDUs can be transmitted by any STA of the MLD
  Therefore, a STA of an MLD may not have knowledge of the MPDUs transmitted by another STA of that MLD
Further, on the recipient MLD, a STA may not have knowledge of the most recently received MPDUs by another STA of the MLD
  There can be a lag in updating the MPDU Rx information cross STAs of an MLD
Furthermore, MPDUs may be in transit on one link when BA is being sent on another link.
  In addition, each STA of the originator MLD may have local retry policy for failed MPDUs tx-ed on its link
Therefore, a transmitting STA can accurately determine the Rx status only for MPDUs that it had transmitted on its own link
  A value 1 in the BA Bitmap indicates the MPDU was successfully received

## Slide 6: BA procedure with multi-link
For ack status received for MPDUs transmitted on another link:
  A value 0 in the BA Bitmap provides no information
    This is because the STA cannot determine if an MPDU is yet to be transmitted by another STA of the MLD or is in-transit on another link or is indeed lost or will be retried.
  A value 1 in the BA Bitmap is unambiguous and indicates that the MPDU was successfully received
Therefore, a STA of an originating MLD can, if and when available, only make a determination about the successful reception of an MPDU transmitted by another STA of its MLD

## Slide 7: BA procedure with multi-link
The originator MLD consolidates (ORs) the BA reports from its STAs to update the common BA scoreboard and make decisions regarding:
  Advancing the Tx window
  Retransmitting failed MPDUs
    determination of an MPDU’s failure based on the report from the STA to which the MPDU was allocated

## Slide 8: BA procedure with multi-link
In conclusion we propose to follow the baseline BA procedures with the following considerations:
  Recipient STA of an MLD provides receive status for MPDUs received on the link that it is operating on
  Additionally, a recipient STA of an MLD may provide receive status for an MPDU successfully received by another STA of that MLD
  Originator MLD updates the receive status for an MPDU corresponding to the BA agreement only if the received status indicates successful reception

## Slide 9: Summary
This contribution highlights the challenges in gathering cross-link receive status and provides directions for determining the success of an MPDU transmitted on any link.

## Slide 10: SP #1
Do you support that the 802.11be amendment shall define mechanism for multi-link operation that enables the following:
  A STA of a recipient MLD shall provide receive status for MPDUs received on the link that it is operating on and may provide information on successful reception of MPDUs received by another STA of that MLD
  Y:
  N:
  A:

## Slide 11: SP #2
Do you agree that an originator MLD of an BA agreement:
  shall update the receive status for an MPDU corresponding to the BA agreement only if the received status indicates successful reception.
  shall not update the receive status for an MPDU corresponding to the BA agreement that has been already positively acknowledged.
  Y:
  N:
  A:

## Slide 12: References
[1]: 11-19-0773 Multi-link Operation Framework (Po-Kai Huang - Intel)
[2]: 11-19-0823 Multi-Link Aggregation (Abhishek Patil - Qualcomm)
[3]: 11-19-0821 multiple band discussion (Liwen Chu - Marvell)
[4]: 11-19-1512 Multi-Link acknowledgement (Rojan – Panasonic)
[5]: 11-19-1856 A-MPDU and BA (Liwen – NXP)
[6]: 11-19-1532 Discussion on Multi-link Acknowledgement (Ryuichi – Sony)
[7]: 11-19-1887 Multi-Link acknowledgement (Taewon – LG Electronics)
[8]: 11-19-1262r6 Specification Framework for TGbe

## Slide 13: Appendix

## Slide 14: Approved Motions [8]
Motion 36
  A single block ack agreement is negotiated between two MLDs for a TID that may be transmitted over one or more links.
    NOTE – The format of the setup frames is TBD.
Motion 37
  Sequence numbers are assigned from a common sequence number space shared across multiple links of a MLD, for a TID that may be transmitted to a peer MLD over one or more links.

## Slide 15: Inter-module coordination

## Slide 16: Current interpretation of bits in Block Ack Bitmap
802.11ax D6.0 (P109L55):
If bit position n of the Block Ack Bitmap subfield is 1, it acknowledges receipt of an MPDU with sequence number value SN and fragment number value FN with n = 4 × (SN – SSN) + FN, where SSN is the value of the Starting Sequence Number subfield of the Block Ack Starting Sequence Control subfield and the operations on the sequence numbers are performed modulo 4096. If bit position n of the Block Ack Bitmap subfield is 0, it indicates that the MPDU has not been received.