## Slide 1
Multi-link Association Follow Up
Date: 2020-01-10
Authors:
Name | Affiliations | Address | Phone | Email
Guogang Huang | Huawei | Shenzhen, China |  | huangguogang1@huawei.com
Yunbo Li |  |  |  | liyunbo@huawei.com
Yuchen Guo |  |  |  | guoyuchen@huawei.com
Ming Gan |  |  |  | ming.gan@huawei.com
Dandan Liang |  |  |  | dandan.liang@huawei.com
Jian Yu |  |  |  | ross.yujian@huawei.com

## Slide 2
A non-AP multi-link device (MLD) associates with an AP MLD through a single link is mentioned in several presentations, in order to save signaling overhead [1,2];
Several potential solutions are proposed in [3];
  Solution 1. Using Neighbor Report elements to indicate the multi-link info
  Solution 2. Through carrying a new element in the current Association Request/Response frame to perform the multi-link association
  Solution 3. Using aggregated multiple OCT MMPDUs to perform the multi-link association
Introduction (1/2)

## Slide 3
  The question is how to indicate the info on multiple links in a high-efficient manner?
  For a multi-link device, most of the capability/operating info on each link is normally the same.
  Considering the above fact, Solution 1 and Solution 3 are not likely to save signaling overhead.
  Hence, we consider Solution 2 and a detailed design is provided for discussion.
Introduction (2/2)

## Slide 4
Multi-link Association Procedure
  Step 1. Non-AP MLD sends an Association Request frame which carries info on Link 1, Link 2 and Link 3 to AP MLD in Link 1, referred as transmitted link
  Step 2. AP MLD replies an Association Response frame which carries info on Link 1, Link 2 and Link 3 to non-AP MLD in Link 1.
Recap
AP1 operating
on 2.4 GHz
AP2 operating
on 5 GHz
AP3 operating
on 6 GHz
Multi-link AP device
Non-AP STA1
Non-AP STA2
Non-AP STA3
Multi-link non-AP device
Link 1
Link 2
Link 3
Non-transmitted links
Transmitted link

## Slide 5
A newly defined element, named as Multi-link Association element, can be included in the Association Request/Response frames. The specific format is given as the below figure
  Multi-link common info, which maybe contain the following info, e.g.
    MAC SAP Address and STR bitmap indication across links of AP MLD’s side
      which may be reserved when this Multi-link Association element is included in an Association Request frame
    MAC SAP Address and STR bitmap indication across links of non-AP MLD’s side
    STA MAC Address Present
  Non-transmitted multi-link profile subelement is used to indicate the info on non-transmitted links
Multi-link Association Request/Response
(1/2)
Element ID | Multi-link common info | non-transmitted multi-link profile subelement
Link-index element | … | Xx element | Link-index element | … | Xx element | … | Link-index element | … | Xx element
Link #2
Link #3
Link #N

## Slide 6
  For the non-transmitted multi-link profile subelement
  The info on each non-transmitted link is began with a newly defined element, named as link-index element, which maybe contain the following info, e.g.
    Link ID, BSSID, Operating class, Channel Number
    TSF Offset
    If STA MAC Address Present is set to 1, then the STA MAC Address is presented in the following each Link-index element. If STA MAC Address Present is set to 0, then the STA MAC Address is not presented in the following each Link-index element.
    Capability info, Listen Interval, which are the same with fixed fields carried in the current Association Request frame
    Status code, AID. These two fields are valid only in an Association Response frame; Otherwise, they are reserved
  Only when some element of the non-transmitted link is different from the one of the transmitted link, it needs to be carried in the non-transmitted multi-link profile subelement.
Multi-link Association Request/Response
(2/2)
Element ID | Multi-link common info | non-transmitted multi-link profile subelement
Link-index element | … | Xx element | Link-index element | … | Xx element | … | Link-index element | … | Xx element
Link #2
Link #3
Link #N

## Slide 7
In this contribution, we propose a signaling indication method for multi-link association.
  For the non-transmitted links, only the elements that have different content from elements for the transmitted link need to be carried.
  This method can significantly reduce the signaling overhead especially when most info on affiliated STAs of MLD is the same.
Summary

## Slide 8
[1] 11-19-0821-00-00be-multiple-band-discussion
[2] 11-19-0773-00-00be-multi-link-operation-framework
[3]11-19-1549-01-00be-multi-link-accociation
Reference

## Slide 9
Do you support that the non-AP MLD should reuse the Association Request/Response frames to do the multi-link association with the AP MLD?
  Yes
  No
  Abstain
Straw Poll 1

## Slide 10
Do you support that only the elements of non-transmitted links that have different content from elements of the transmitted link are included in the association Request/Response frame?
  Yes
  No
  Abstain
Straw Poll 2