## Slide 1: Discussion on EHT PPDU Formats
Date: 2020-01-12
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Yanyi Ding |  |  |  | 
Urabe Yoshio |  |  |  | 
Rojan Chitrakar |  |  |  | 

## Slide 2: Background
According to 11be SFD [2], an EHT PPDU comprises legacy preamble, RL-SIG and U-SIG. Furthermore, an EHT PPDU transmitted to multiple users comprises an EHT-SIG immediately after the U-SIG.
However, it is unclear whether EHT-SIG is present in other types of EHT PPDU, e.g.
  an EHT PPDU transmitted to a single user;
  an EHT PPDU for trigger-based uplink transmission; or
  an EHT PPDU for trigger-based multi-AP joint transmission.
This contribution addresses different EHT PPDU formats.
L-STF
L-LTF
L-SIG
RL-SIG
U-SIG
…
EHT-SIG

## Slide 3: Presence of EHT-SIG in EHT PPDU
U-SIG in 11be SFD [2]
  2 OFDM symbol long and jointly encoded
  sent using 52 data tones and 4 pilot tones per-20MHz.
  modulated in the same way as the HE-SIG-A field of 802.11ax.
  EHT PPDU transmitted to a single user
  U-SIG may not have enough data bits to accommodate all version dependent information which comprises
    similar information to HE-SIG-A of HE SU PPDU with extended support for up to 320 MHz bandwidth and 16 space-time streams; and
    preamble puncturing information.
  EHT-SIG may be required for EHT PPDU transmitted to a single user to contain some version dependent information.
    EHT-SIG of an EHT PPDU transmitted to single STA may have a different format from that of an EHT PPDU transmitted to multiple STAs.
EHT PPDU for trigger-based uplink transmission or multi-AP joint transmission
  most of version dependent information can be included in the soliciting triggering frame.
  EHT-SIG may not be present in EHT PPDU for trigger-based transmission.

## Slide 4: EHT PPDU Formats
We propose EHT PPDUs can be broadly classified into two formats:
  EHT basic PPDU which is used for non-trigger-based transmission
    EHT-SIG is present in EHT basic PPDU
  EHT TB PPDU which is used for trigger-based transmission
    EHT-SIG is not present in EHT TB PPDU
L-STF
L-LTF
L-SIG
RL-SIG
U-SIG
…
EHT-SIG
L-STF
L-LTF
L-SIG
RL-SIG
U-SIG
…
EHT Basic PPDU
EHT TB PPDU

## Slide 5
U-SIG in EHT Basic PPDU
  PPDU format
    0: EHT Basic PPDU
    1: EHT TB PPDU
  SU/MU
    0: EHT Basic PPDU transmitted to a single user;
    1: EHT Basic PPDU transmitted to multiple users.
  BW field
    0: 20 MHz.
    1: 40 MHz.
    2: 80 MHz non-preamble puncturing mode.
    3: 160 MHz and 80+80 MHz non-preamble puncturing mode.
    4: 320 MHz and 160+160 MHz non-preamble puncturing mode.
    5: 80 MHz preamble puncturing mode.
    6: 160 MHz and 80+80 MHz preamble puncturing mode.
    7: 320 MHz and 160+160 MHz preamble puncturing mode.
U-SIG has a unified format regardless of whether EHT basic PPDU is transmitted to a single STA or multiple STAs.
U-SIG comprises two parts: U-SIG1 and U-SIG2, each containing 26 data bits.
U-SIG include all version independent bits and some version dependent bits (e.g. PPDU Format, SU/MU Flag, BW, EHT-SIG related info, and Spatial Reuse).
Example U-SIG content

## Slide 6
U-SIG in EHT TB PPDU
U-SIG include all version independent bits and all necessary version dependent bits (e.g. PPDU Format, BW and Spatial Reuse).
Example U-SIG content

## Slide 7
EHT-SIG in EHT Basic PPDU Transmitted to a Single User
EHT-SIG contains remaining version dependent bits.
There is a single EHT-SIG content channel regardless of the BW of EHT basic PPDU.
User-specific field comprises a single user field, which is jointly encoded with common field
  User field has a similar format to the type 1 user field proposed in [2].
  Note: For Preamble Puncturing Bitmap subfield, each bit indicates whether or not a 20 MHz frequency segment which is not primary 20 is punctured.
Example common field content

## Slide 8
EHT-SIG in EHT Basic PPDU Transmitted to Multiple Users
There is one or more EHT-SIG content channels depending on the BW of EHT basic PPDU.
Common field comprises 1st common subfield and 2nd common subfield, which are separately encoded.
  The 1st common subfield is the same for all EHT-SIG content channels; while the 2nd common subfield differs among the EHT-SIG content channels.
  The 2nd common subfield has similar format to the common field in 11ax, which is not present in case of full BW MU-MIMO mode.
The user-specific field has similar structure to 11ax.
  The formats of user fields have been addressed in [2].
Example 1st common field content

## Slide 9: Summary
Two EHT PPDU formats (i.e. EHT basic PPDU and EHT TB PPDU) are proposed.
  EHT-SIG is present in EHT basic PPDU but not present in EHT TB PPDU.
  EHT-SIG contains version dependent bits which cannot be accommodated in U-SIG.

## Slide 10: Reference
IEEE 802.11-19/1262r6, Specification Framework for TGbe, November 2019
IEEE 802.11-19/1868r2, Signaling support for multi-RU assignment, January 2020

## Slide 11: SP #1
Do you agree that EHT-SIG is present immediately after U-SIG in an EHT PPDU transmitted to a single user?

## Slide 12: SP #2
Do you agree that EHT-SIG is not present in an EHT PPDU used for trigger-based uplink transmission or multi-AP joint transmission?