## Slide 1: Multi-Link Grouping
Date: 2020-1-7
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Yifan Zhou |  |  |  | 
Yiqing Li |  |  |  | 

## Slide 2: Introduction
The channel access scheme for multi-link transmission has been discussed in many contributions [1-6].
Several channel access modes are proposed:
  Asynchronzied channel access mode
  Synchronized channel access mode
  Quasi-asynchronized channel access mode
Different channel access modes are suitable for different type of devices
For STR capable multi-link devices (MLDs), asynchronized mode is good enough
  Independent channel access in different links, no impact of each other, easy to implement
For non STR capable MLDs, synchronized (or quasi-asynchronized) channel access mode should be used to avoid the situation that the MLD is transmitting on one link, while receiving on the other link.
Since MLDs with different capabilities may exist in the network at the same time, it is necessary to have a mixed mode, which is a combination of the above mentioned modes.
In this contribution, we propose a multi-link grouping method which serves such a purpose.

## Slide 3: Basic Idea
The basic idea is to put the “non-STR links” into a link group, the links that belong to the same group should use the synchronized mode, while the links from different groups can use the asynchronized mode.
The link grouping is only done on the AP MLD side:
  For those links that the AP MLD can not support STR, they should be put into the same link group.
  For those links that the AP MLD can support STR with all other links, they can form an independent link group.
There is one primary link for each link group, EDCA can only be done on the primary link
For the non-primary (or secondary) links, they can only be used together with the primary link. Similar method of the 80+80 channel access can be used, i.e., PIFS idle before the backoff done of the primary link means the secondary link is idle, in which case the secondary links can be used in synchronized mode with the primary link.

## Slide 4: Basic Idea
An important point of the link grouping architecture is that: if multiple links are in the same group, then EDCA can only be done on one of the multiple links
Let’s have a look what happens if EDCA is allowed on more than one links.
  If the AP MLD only uses one link, then other STAs may transmit to the AP MLD on the other link, but the AP MLD can not receive
Link 1
Link 2
AP MLD 1
STA MLD 1
AP MLD 1
STA MLD 2
Simultaneous TX&RX happens
Channel Busy
Note: Quasi-asynchronized channel access mode proposes that the AP MLD can occupy the link 2 as long as the channel becomes idle, but it is not guaranteed, i.e., other STAs may still jump in.

## Slide 5: Basic Idea
Another important point of the link grouping architecture is that: if multiple links are in different groups, then EDCA can be done on each of the multiple links, no matter the STA MLD supports STR among these links or not
Suppose there is a Non-AP MLD2 which does not support STR on link 1 and link 2, then the following rules can be designed to work well
Hence, there’s no necessary to do the link grouping for each individual STA MLD
 | Link 1 | Link 2
AP MLD1 | TX to non-AP MLD2 | If TX to non-AP MLD2, then the ending time should be aligned with link 1; If TX to other STAs, no restriction
 | TX to other STA | No restriction
 | RX from non-AP MLD2 | EDCA，TX to other STAs
 | RX from other STA | No restriction
 | Before identify the TA, RA for a RX pkt | EDCA, TX to async MLD STA or single link STA
Non-AP MLD2 | TX to AP MLD1 | If TX to AP MLD1, then the ending time should be aligned with link 1
 | RX, RA is broadcast addr or itself | Pending backoff
 | RX, RA is neither broadcast addr nor itself | EDCA, TX to AP MLD1
 | Before identify the TA, RA for a RX pkt | pending backoff

## Slide 6: Link Grouping principle
How to do the link grouping?
In simple words, just put the non-STR links into the same group, so that the links in the same group behave synchronously.
After link grouping, the following condition shall be satisfied:
  For any two links that belong to two different link groups, the AP MLD can support STR on the two links
In most cases, if there are more than one link in a link group, for any link L within a link group, there exists at least one other link L* inside the same group that the AP MLD does not support STR on L and L*, since otherwise, L can form another link group.
Let’s take the following example to explain why we need such a link grouping principle

## Slide 7: Grouping example
Here is an example for the link grouping.
Assume the AP MLD has 4 links: L1, L2, L3 and L4
The AP MLD does not support STR for the following link pairs:
  <L1, L2> ; <L2, L3>
Meanwhile, it supports STR for the following link pairs:
  <L1, L3> ; <L1, L4> ; <L2, L4> ; <L3, L4>
Then the 4 links can be divided into two link groups:
  Group1 = {L1, L2, L3} ; Group2 = {L4}

## Slide 8: Operations of the AP/non-AP MLD under link grouping
If only one link group is used for transmission, then the AP or non-AP STA MLD can perform EDCA on the primary link of the link group, secondary links can be used if PIFS idle
If more than one link groups are used for transmission, then the situation is: AP supports STR between different groups, but STAs may or may not support STR between different groups. Given a particular link group G1:
  If the non-AP STA MLD supports STR between G1 and all other link groups, then the AP MLD or non-AP STA MLD can work independently on the link groups to transmit to each other
  If there exists a link group G2 that the STA MLD does not support STR between G1 and G2, then
    AP side: the AP MLD can only use G1 to transmit to the non-AP STA MLD as long as the non-AP STA MLD is not transmitting on G2
    Non-AP STA side: The non-AP STA MLD can only use G1 to transmit to the AP as long as the non-AP STA MLD is not receiving its own packet on G2
  Note that further rules may be defined, see slide 5.

## Slide 9: Conclusion
  We propose a link grouping based channel access architecture for multi-link operation, including
    Link grouping principle
    Operations of the AP and non-AP STA MLDs

## Slide 10: Straw Poll
  Do you support to have a link grouping based channel access method for multi-link operation in TGbe?

## Slide 11: References
  [1] 11-19-1116-04-00be-channel-access-in-multi-band-operation
  [2] 11-19-1548-01-00be-channel-access-design-for-synchronized-multi-links
  [3] 11-19-1541-01-00be-performance-aspects-of-multi-link-operations-with-constraints
  [4] 11-19-1546-00-00be-legacy-performance-impact-on-multi-link-operation
  [5] 11-19-1405-07-00be-multi-link-operation-channel-access-discussion
  [6] 11-19-1916-00-00be-mlo-asynch-qsynch-synch