## Slide 1: NGV SIG Content Follow-up
Date: 2020-01-13
Authors:

## Slide 2: Introduction
NGV-SIG
  Most content bits are decided [1]
  The full content and bit location need to be finalized.
We propose the tables for NGV-SIG and MCS.

## Slide 3: NGV SIG Content
Number of bits: total 20 bits
  BW: 1 bit
  MCS: 4 bits
  Nss: 1 bit
  Midamble periodicity: 2 bits
  LDPC Extra symbol: 1bit
  LTF format: 1 bit
  Tail: 6 bits
  CRC: 4 bits
How to use the 4 extra bits?
  Option 1: Reserved all 4 bits for future use or some proprietary use
  Option 2: PHY version bits: 2 bits and Reserved: 2 bits.

## Slide 4: NGV SIG Table I
Bit | Field | Number of bits | Description
B0 | Bandwidth | 1 | Set 0 for 10MHz, set 1 for 20MHz.
B1-B4 | MCS | 4 | MCS table
B5 | Nss | 1 | Set 0 for 1 ss, and set 1 for 2ss.
B6-B7 | Midamble Periodicity | 2 | Set 0 for 4 symbols, set 1 for 8 symbols, set 2 for 16 symbol. Value 3 is reserved.
B8 | LTF format | 1 | Set 0 for uncompressed LTF; set 1 for compressed LTF.
B9 | LDPC Extra OFDM Symbol | 1 | Set to 1 if the LDPC PPDU encoding process results in an extra OFDM symbol as described in 21.3.10.5.4 (LDPC coding). Set to 0 otherwise.
B10-B13 | Reserved | 4 | Reserved and set to 1.
B14-B17 | CRC | 4 | CRC calculated as in 19.3.9.4.4 (CRC calculation for HTSIG).
B18-B23 | Tail | 6 | Used to terminate the trellis of the convolutional decoder. Set to 0.

## Slide 5: NGV SIG Table II
Bit | Field | Number of bits | Description
B0-B1 | PHY version | 2 | Set 0 for 11bd, other three options are reserved for future generations.
B2 | Bandwidth | 1 | Set 0 for 10MHz, set 1 for 20MHz.
B3-B6 | MCS | 4 | MCS table
B7 | Nss | 1 | Set 0 for 1 ss, and set 1 for 2ss.
B8-B9 | Midamble Periodicity | 2 | Set 0 for 4 symbols, set 1 for 8 symbols, set 2 for 16 symbol. Value 3 is reserved.
B10 | LTF format | 1 | Set 0 for uncompressed LTF; set 1 for compressed LTF.
B11 | LDPC Extra OFDM Symbol | 1 | Set to 1 if the LDPC PPDU encoding process results in an extra OFDM symbol as described in 21.3.10.5.4 (LDPC coding). Set to 0 otherwise.
B12-B13 | Reserved | 2 | Reserved and set to 1.
B14-B17 | CRC | 4 | CRC calculated as in 19.3.9.4.4 (CRC calculation for HTSIG).
B18-B23 | Tail | 6 | Used to terminate the trellis of the convolutional decoder. Set to 0.

## Slide 6: NGV MCS Level
Propose the following MCS table:
  Reuse most VHT MCS table
  Remove BPSK, R=3/4
  Add three MCSs
    256QAM, R=3/4
    256QAM, R=5/6
    BPSK with DCM, R=1/2
MCS index | Modulation | Code rate
0 | BPSK | ½
1 | QPSK | ½
2 | QPSK | ¾
3 | 16QAM | ½
4 | 16QAM | ¾
5 | 64QAM | 2/3
6 | 64QAM | ¾
7 | 64QAM | 5/6
8 | 256QAM | ¾
9 | 256QAM | 5/6
10 | BPSK with DCM | 1/2

## Slide 7: Reference
[1] Rui Cao and etc., “Discussion of miscellaneous NGV preamble designs”, IEEE 802.11-19/1824.

## Slide 8: Straw Poll 1
Do you agree that NGV SIG includes the following?
  Option 1: 4 Reserved bits
  Option 2: 2 PHY version bits + 2 Reserved bits
Option 1:
Option 2:
N:
A:

## Slide 9: Straw Poll 2
Do you agree to add the following text into Section 3 of SFD?
  “The 24-bit NGV SIG content table is defined in slide 4.”
Y:
N:
A:

## Slide 10: Straw Poll 3
Do you agree to add the following text into Section 3 of SFD?
  “11bd defines the following MCS table.”
Y:
N:
A:
MCS index | Modulation | Code rate
0 | BPSK | ½
1 | QPSK | ½
2 | QPSK | ¾
3 | 16QAM | ½
4 | 16QAM | ¾
5 | 64QAM | 2/3
6 | 64QAM | ¾
7 | 64QAM | 5/6
8 | 256QAM | ¾
9 | 256QAM | 5/6
10 | BPSK with DCM | 1/2