## Slide 1: Discussion on NGV PHY Modes
Date: 2020-01-13
Authors:

## Slide 2: Introduction
All PHY modes for 10MHz and 1SS will be mandatory for 11bd STA.
  Limit the baseline PHY modes will benefit chip development for 11bd STAs.
20MHz and 2SS are optional high-throughput modes for hardware-capable STAs.
  Range extension design is not needed.

## Slide 3: Coding and Midamble Options
LDPC is the mandatory coding scheme for 11bd. [1, 2]
  Together with Midamble, good performance gain in Doppler channels.
Do we need BCC for 11bd? [2]
  BCC+No Midamble can achieve similar goodput as LDPC+Midamble in some scenarios. Midamble efficiency compensates coding deficiency.
  11bd BCC is NOT the same BCC as 11p BCC:
    A new set of interleavers designed for 52 data tones.
    For high-throughput modes, 20MHz and/or 2SS BCC are new.
    For 2SS, channel tracking (critical to BCC) will also need to extended.
    Keeping BCC in 11bd is not as simple as thought.
Propose to make LDPC the only coding scheme for 11bd.
Midamble periodicity of 0 is not needed.
  Midamble 16 is the option for high efficiency in low Doppler scenarios.

## Slide 4: Preamble for High-Throughput Modes
Legacy preamble power-boost (3dB L-STF and 3dB L-LTF) and repeated NGV-LTF are designed for range-extension in 11bd. [3]
For two spatial streams and 20MHz modes, preamble detection and channel estimation are not the bottleneck.
Propose to limit the preamble modes for high-throughput transmissions:
  Limit L-STF and L-LTF power boost for 11bd 10MHz PPDU with one spatial stream.
  Limit Repeated NGV-LTF for 11bd 10MHz PPDU with one spatial stream.

## Slide 5: Preamble for High-Throughput Modes (2)
Compressed NGV-LTF formats [4]
  Compressed NGV-LTF (NGV-LTF-1x) is allowed for one spatial stream for better Midamble efficiency and goodput. [5]
  Compressed NGV-LTF for two spatial streams has goodput loss in most Doppler channels. [6]
  This is due to channel interpolation loss across single steam pilots.
Propose to disallow NGV-LTF-1x for 11bd transmissions with two spatial streams.

## Slide 6: Reference
[1] Rui Cao and etc., “11bd MCS Discussions”, IEEE 802.11-19/0688.
[2] Ioannis Sarris, “NGV PHY Performance Results” , IEEE 802.11-19/1104.
[3] Prashant Sharma and etc, “NGV Frame Format: Simulations”, IEEE 802.11-19/1470.
[4] Rui Cao and etc., “NGV Midamble Design Followup”, IEEE 802.11-19/1472.
[5] Yujin Noh and etc., “Compressed Midamble in NGV”, IEEE 802.11-19/1152.
[6] Rui Cao and etc., “NGV-Midamble-Design-followup”, IEEE 11-19/1472

## Slide 7: Straw Poll 1
Do you agree to add the following text into Section 3 of SFD?
  “LDPC is the only coding scheme for 11bd.”
Y:
N:
A:

## Slide 8: Straw Poll 2
Do you agree to add the following text into Section 3 of SFD?
  “Only three Midamble periodicity are defined in 11bd. The fourth option is Reserved.”
Y:
N:
A:

## Slide 9: Straw Poll 3
Do you agree to add the following text into Section 3 of SFD?
  “For 11bd transmission with BPSK modulation, if the transmission is using 20MHz bandwidth or two spatial streams,
    no power boost shall be applied on L-STF and L-LTF fields
    NGV-LTF is not repeated.”
Y:
N:
A:

## Slide 10: Straw Poll 4
Do you agree to add the following text into Section 3 of SFD?
  “For NGV transmissions with two spatial streams, NGV-LTF-1x is disallowed.”
Y:
N:
A: