## Slide 1: NGV Secondary 10MHz Detection for 20MHz Operation
Date: 2020-01-13
Authors:

## Slide 2: Introduction
11bd defines contiguous 20MHz operation.
Harmonized 20MHz channel access scheme is decided in last meeting [1]
  backoff procedure is based on the channel states of two contiguous 10MHz channels.
  backoff counter decreases when two contiguous 10MHz channels are idle.
  Idle states are checked by TBD sensing methods (e.g., Packet detection, GI detection, energy detection)
In this contribution, we will discuss the channel detection/sensing methods, and share the performance of GI detection.

## Slide 3: Channel Detection Schemes
Primary 10MHz channel can use packet detection (PD) and achieves 10MHz detection sensitivity of <=-85dBm.
Secondary 10MHz channel sensing method is TBD.
There are multiple ways to detect the secondary 10MHz
  Option 1: Packet Detection
  Option 2: Energy detection
  Option 3: GI detection

## Slide 4: Comparison
Option 1: Packet Detection (PD)
  Separate BCC decoder to decode LSIG and payload.
  Same sensitivity as primary with ~2x hardware cost and complexity.
Option 2: Energy Detector (ED)
  Only energy detection with time-domain samples.
  Limited hardware cost, but relaxed sensitivity, >10dB worse.
Option 3: GI Detection (GD)
  All time-domain processing is needed. Better sensitivity than ED.
  Compromised hardware cost and performance.
LSTF Carrier sensing
LSIG LENGTH decoding
MAC Duration decoding
LSTF Carrier sensing
OFDM GI Detection

## Slide 5: GI Detection
Correlation between most recent 1.6us samples with the 1.6us samples that is 8us apart.
By check the correlation peak, the number of OFDM symbols can be counted, and packet duration can be detected.
GI
GI
GI
GI
…

## Slide 6: Simulations
Settings:
  1x1, 11p 10MHz PPDU
  100 data OFDM symbols
  Nosie floor: -98dBm
  Five C2C Doppler channels.
  GI Detection scheme
    AGC gain uncertainty: the input y samples are normalized in amplitude.
    OFDM is detected is the GI correlator output is higher the threshold.
  Metric:
    PFA: false detection probability of two or more OFDM symbols during noise portion
    Pmiss: miss detection of two or more OFDM symbols within data packet.

## Slide 7: Rural LOS
PFA is low at 3e-4.
Pmiss is below 1e-4 @ rxPower >=-85dBm. ~8dB margin from 10% Pmiss.

## Slide 8: Urban Approaching LOS
PFA is low at 3e-4.
Pmiss is below 1e-4 @ rxPower >=-85dBm. ~8dB margin from 10% Pmiss.

## Slide 9: Urban Crossing NLOS
PFA is low at 3e-4.
Pmiss is below 1e-4 @ rxPower >=-85dBm. ~8dB margin from 10% Pmiss.

## Slide 10: Highway LOS
PFA is low at 3e-4.
Pmiss is below 1e-4 @ rxPower >=-85dBm. ~8dB margin from 10% Pmiss.

## Slide 11: Highway NLOS
PFA is low at 3e-4.
Pmiss is ~1e-3 @ rxPower >=-85dBm. ~8dB margin from 10% Pmiss.

## Slide 12: Discussions
The GI detection performance is promising.
  The 10% Pmiss is -93dBm, which is 8dB from -85dBm target.
  PFA floor is low @3e-4.
The performance metric is defined to miss two OFDM symbol (16us) or more.
  Pmiss will be even lower if consecutive miss of N symbols is considered as IDLE. (see Appendix)
  PFA will also be lower if carrier sense is required before GI detection.

## Slide 13: Summary
In this contribution, we compared three channel detection schemes for secondary 10MHz channel in 20MHz operation.
The performance of GI detection is evaluated with C2C channels.
The results show that GI detection is promising as a channel detection scheme.

## Slide 14: Reference
[1] Insun Jang, and etc. “Harmonization for 20MHz Channel Access”, IEEE 802.11-19/1480.

## Slide 15: Straw Poll 1
Do you agree to add the following text into Section 3 of SFD?
  “The 20MHz CCA shall use GI detection for the secondary 10MHz channel detection.”
Y:
N:
A:

## Slide 16: Appendix

## Slide 17: Rural LOS

## Slide 18: Urban Approaching LOS

## Slide 19: Urban Cross NLOS

## Slide 20: Highway LOS

## Slide 21: Highway NLOS