## Slide 1: Multi-link Block Ack Architecture
Date: 2020-01-10
Authors:
Name | Company | Address | Phone | Email
Rojan Chitrakar | Panasonic Corporation | 202 Bedok South Avenue 1, #02-11 Singapore 469332 |  | rojan.chitrakar@sg.panasonic.com
Lei Huang |  |  |  | 
Yanyi Ding |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
Overview
The following aspects related to Multi-link block ack have been added to the 11be SFD :
  A single block ack agreement is negotiated between two MLDs for a TID that may be transmitted over one or more links.
  Sequence numbers are assigned from a common sequence number space shared across multiple links of a MLD, for a TID that may be transmitted to a peer MLD over one or more links.
  For each block ack agreement, there exists one receive reordering buffer based on MPDUs in the MLD which is the recipient of the QoS Data frames for that block ack agreement. The receive reordering buffer operation is based on the Sequence Number space that is shared between the two MLDs.
This contribution shares one possible architecture for Multi-link block ack. Other architectures are also possible and are discussed in [2] and [3].

## Slide 3
Originator MLD

## Slide 4
Recipient MLD

## Slide 5
Scoreboard size
Different links may have different data rates (e.g. due to different bandwidths, # of antennas etc.). Consequently, the recipient MLD can expect to receive more MPDUs on the faster link and may need to negotiate different Per-link Scoreboard sizes for different links during the setup of block ack parameters between two MLDs. Else, if all links are required to have the same Scoreboard size, the scoreboard size of a slower link may constrain a faster link’s throughput.
The size of the BA Bitmap of BAs may also get restricted by the scoreboard sizes.
The scoreboard size of different links may be different.
Notes: E.g. Link 2 is 4 times faster than link 1. => Link 2 may maintain a buffer size that is 4 times bigger than Link1’s.
The size of the Receiver Reordering buffer >= Sum of scoreboard sizes of all enabled links.

## Slide 6
Example Recipient Implementation
Recipient MLD may also maintain a common scoreboard to keep a longer term record of received MPDUs (not limited by TXOPs). Per-link scoreboard may be implemented as partial-state, while common scoreboard may be implemented as full-state. The common Scoreboard is updated regularly with the content of the per-link Scoreboards (e.g. every time the Per-link scoreboard is updated, or at a very minimum at the end of each link’s TXOP).
Recipient MLD may maintain a common scoreboard for a Multi-link TID.
Notes: common scoreboard may prevent the receipt status of a link being lost, for e.g. due to switch of TIDs between TXOPs.
The size of the Common Scoreboard >= Maximum scoreboard sizes among all enabled links.

## Slide 7
Conclusion
This contribution shared one possible architecture for Multi-link block ack operations.
We proposed that the block ack agreement for a TID that may be transmitted over multiple links be allowed to maintain different scoreboard sizes for different links.
We also proposed that a recipient MLD may maintain a common scoreboard to consolidate the receipt status of MPDUs of a TID received via different links.

## Slide 8: Reference
IEEE 802.11-19/1512r6 – Multi-link acknowledgment
IEEE 802.11-19/1575r0 – Multi-link BA Operation
IEEE 802.11-19/1856r0 – A-MPDU and BA

## Slide 9
Straw Poll 1
Do you support to add the following to the 11be SFD:
  Different scoreboard sizes may be negotiated for different links of an MLD during negotiation of a block ack agreement for a TID that may be transmitted over one or more links.
  Y/N/A

## Slide 10
Straw Poll 2
Do you support to add the following to the 11be SFD:
  An MLD may maintain a common scoreboard to record the receipt status of MPDUs of a TID received via different links?
  Y/N/A