## Slide 1: Preparations for Coordinated OFDMA
Date: 2020-01-10
Authors:
Name | Company | Address | Phone | Email
Rojan Chitrakar | Panasonic Corporation | 202 Bedok South Avenue 1, #02-11 Singapore 469332 |  | rojan.chitrakar@sg.panasonic.com
Lei Huang |  |  |  | 
Yanyi Ding |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
Overview
Coordinated OFDMA may be considered as a simpler scheme among the various Multi-AP Coordination schemes being considered in 11be.
Coordinated OFDMA may substantially improve worst case latency (3.5x reduction in maximum access time compared to EDCA). [4]
To achieve effective results, prior coordination of the frequency resources among the participating APs may be helpful.

## Slide 3
Candidate STAs for Coordinated OFDMA
Not all STAs benefit equally from Coordinated OFDMA. Some may benefit more than others. [1]
STAs that may benefit the most from Coordinated OFDMA should be identified prior to the coordinated transmissions: for example STAs within the transmission range of multiple APs.
  For example an AP may collect reports (e.g. interference measurement reports) from associated STAs to identify the candidate STAs.
Notes: STA1 and STA2 associated with AP1 and AP2 respectively.

## Slide 4
Preferred frequency resources
Each AP also identifies the frequency resources (within its operating bandwidth) that may be preferable for its candidate STAs. Alternatively, APs may identify the frequency resources that are not preferable for their candidate STAs (e.g. due to presence of high OBSS interference).
APs participating in Coordinated OFDMA transmissions exchange the information of the preferred (or not-preferred) frequency resources prior to coordinated transmissions (e.g. during the coordinated OFDMA Setup phase [3]).

## Slide 5
Coordinated OFDMA Transmission
During the Coordinated OFDMA transmissions, the Coordinating AP uses the information of the preferred frequency resources to allocate sub-channels to participating APs (e.g. during the Schedule Allocation phase [2], or in Coordinated OFDMA Announcement (COA) frame [3]).
exchange of preferred frequency resources
Identification of preferred frequency resources
Coordinated OFDMA transmission

## Slide 6
Conclusion
To achieve effective results, prior coordination of the frequency resources among the participating APs may be helpful.
APs participating in Coordinated OFDMA transmissions may exchange the information of the preferred (or not-preferred) frequency resources prior to coordinated transmissions.
During Coordinated OFDMA transmissions, the Coordinating AP can use the information of the preferred frequency resources to allocate sub-channels to participating APs.

## Slide 7: Reference
IEEE 802.11-19/0071r0 - Coordinated Multi-AP Transmission for EHT
IEEE 802.11-19/1582r0 - Coordinated AP Time/Frequency Sharing in a Transmit Opportunity in 11be
IEEE 802.11-19/1788r0 - Coordinated OFDMA Operation
IEEE 802.11-19/1879r0 - Gain Analysis of Coordinated AP Time/Frequency Sharing in a Transmit Opportunity in 11be
IEEE 802.11-19/1919r0 - Coordinated OFDMA

## Slide 8
Straw Poll 1
Do you support to add the following to 11be SFD:
  The sharing AP may solicit feedback from one or more APs from the AP candidate set to learn the frequency resources preferred for Coordinated OFDMA transmissions.
  Y/N/A