## Slide 1: BW Negotiation, TXOP Protection with >160MHz PPDU and Puncture Operation
Date: 2020-01-06
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: BSS with >160MHz BW and Puncture Operation
A PPDU can have >160MHz BW, e.g. 320 MHz, 160+80MHz, 160+160MHz.
The PPDU with preamble puncture can be transmitted to a single STA, AP, e.g. 20+40MHz, 80+40MHz, 20+40+20+40MHz, .
320MHz EHT PPDU at 5GHz or 6GHz band
160+80 MHz EHT PPDU at 5GHz or 6GHz band

## Slide 3: Recap: BW Indication and Negotiation
In PHY header, the PPDU BW is indicated, e.g. in VHT SIG, HE SIG.
In Service field of legacy duplicate PPDU, BW is indicated for PPDU BW indication, TXOP protection and BW negotiation.
In MU-RTS/CTS, BW is indicated in MAC layer, e.g. in frame body.
EHT should provides the BW indication, TXOP protection, BW negotiation.
  The methods defined in 11ac, 11ax are not applicable to >160MHz BW and/or multiple bands.

## Slide 4: >160MHz TXOP Negotiation and TXOP Protection
Option 1:
  Adding additional one bit in Service field of non-HT duplicate PPDU to indicates >160MHz BW.
    The signaling TA indicates that BW is defined in Service field.
  Pros:
    No new control frame definition.
  Cons:
    Not extensible.
    3-bit random value may not be enough. This may have influence to scrambling operation.
    No support of dynamic puncture operation.

## Slide 5: >160MHz TXOP Negotiation and TXOP Protection (Cont’d)
Option 2:
  The BW information is indicated in frame.
  Pros:
    extensible.
    no influence to scrambling operation.
    Support dynamic puncture operation.
  Cons:
    new control frame definition or frame updation is needed.
We prefer option 2.

## Slide 6: TXOP with Punctured BW
An EHT BSS can have punctured BSS operating channel or no punctured BSS operating channel.
TXOP BW Option 1:
  Dynamic bandwidth negotiation is allowed however a TXOP holder is not allowed to further puncture the 20MHz channels within the occupied TXOP BW.
  no channel puncture indication, e.g. 20MHz channel bitmap, is required.
160MHz BSS
80MHz TXOP
160MHz TXOP
80+40MHz BSS
80MHz TXOP
80+40MHz TXOP
Allowed TXOP BW
Disallowed TXOP BW
2x(20+40) MHz TXOP
Disallowed TXOP BW
20+40 MHz TXOP
Allowed TXOP BW

## Slide 7: TXOP with Punctured BW
TXOP BW Option 2:
  Dynamic bandwidth negotiation is allowed and a TXOP holder is allowed to further puncture the 20MHz channels within the occupied TXOP BW.
  The channel puncture indication, e.g. 20MHz channel bitmap, is required.
160MHz BSS
80MHz TXOP
160MHz TXOP
80+40MHz BSS
80MHz TXOP
80+40MHz TXOP
Allowed TXOP BW
2x(20+40) MHz TXOP
20+40 MHz TXOP
Allowed TXOP BW
E-RTS
E-CTS
E-RTS
E-CTS
TXOP BW negotiation
TXOP BW negotiation

## Slide 8: Enhanced RTS/CTS
Option 1:
  Currently three Control subtypes are reserved0000, 0001, 1111. One of them is defined as Extended Control frame.
    A Extended Subtype field is added in the Extended Control frame to further indicate the new control frame, e.g. enhanced RTS, enhanced CTS, possibly new defined NDPA.
Frame Control field of Extended Control frame
1
Extended Subtype
Control Information
(Extended Control)

## Slide 9: Enhanced RTS/CTS
Option 2:
  Redefined the current control frame to carry the enhanced RTS/CTS.
    Option 2.1: in NDPA, STA Info field with specific AID value, e.g. one AID value that is more than 2007, is used to carry enhanced RTS/CTS information, BW, dynamic indication, 20MHz channel bitmap etc.
    Option 2.2: in Trigger, User Info field with specific AID value, e.g. one AID value that is more than 2007, is used to carry enhanced RTS/CTS information, BW, dynamic indication, 20MHz channel bitmap etc.

## Slide 10: Straw Poll 1
Do you support that 11be defines a MAC mechanism to protect TXOP for PPDUs with >160MHz and/or PPDUs with preamble puncturing?