## Slide 1: Implicit Sounding Scheme
Date: 2020-01
Authors:

## Slide 2: Abstract
There is ‘overhead’ issue when using .11ax sounding scheme for candidate features of TGbe, such as 16ss, multi AP.
Many contributions about how to reduce the overhead have been discussed, including improved explicit sounding and implicit sounding.
In this contribution, we analyze the feasibility of implicit sounding schemes.

## Slide 3: Implicit Sounding Schemes
SU based multi-trigger sequential sounding
STA transmits NDP sounding PPDU in response to the soliciting trigger frame containing its AID.
In case of multi-AP, slave APs could be re-synchronized by the NDP-trigger frame and refresh channel information of the specified STA from the following NDP sounding PPDU.
AP(master)
STA1
AP(slave)
STA2
Trigger
NDP
NDP
Trigger
Trigger
NDP
NDP
Trigger
NDP
NDP
SU based single-trigger sequential sounding
STAs transmit NDP sounding PPDU in response to the soliciting trigger frame containing their AIDs.
  Trigger frame contains information indicating the timing at which the STAs respectively transmit NDP
MU based simultaneous sounding
The difference to SU based scheme is that multiple STAs response NDP simultaneously, leveraging spatial multiplex.
SU: multi-trigger
SU: single-trigger
MU

## Slide 4: Challenges of Implicit Sounding
Calibration accuracy to maintain channel reciprocity
  [5] shows relative calibration is possible, adding no complexity to STA and estimating channel status accurately.
UL/DL power difference
Power offset among STAs （MU based scheme）
  Could develop STA selection algorithm to select STAs with similar power for MU-MIMO based scheme
Inter-user interference caused by residual CFO （MU based scheme）
In the following slides, we focus on the 2nd and 4th challenges.

## Slide 5: UL/DL power difference
In order to compensate for UL/DL transmission power difference, repetitions of EHT-LTF in NDP frame are required
  ChD: 20MHz
  AP NRX: 4,8
  STA NTX : 1,2
  STA Tx Power: 9 dBm
  Noise Power: -90 dBm
  HE-LTF repeated 1~20 times for implicit sounding
  HE-LTF mode: 4x, GI: 3.2 msec
Based on various EIRP requirements and Wi-Fi products we define three main cases
  For MU based scheme or STA with >1 Nss, it’s natural to have more than one HE-LTF, may not need additional HE-LTF for compensation.
  With repetitions of EHT-LTF, implicit sounding still have benefit in terms of ‘overhead’ .

## Slide 6: Overhead Comparison
Overhead comparison consumption
# | Use Case | #users | Nss per user | #AP Tx Ant | MU-MIMO Size | Power Difference
1 | Residential | 4 | 2 | 8 | 2 | 6dB
2 | Residential | 2 | 2 | 8 | 1 | 6dB
3 | Office | 8 | 2 | 16 | 4 | 12dB
4 | Office | 8 | 2 | 16 | 6 | 12dB
5 | Office | 8 | 4 | 16 | 2 | 12dB
6 | Dense Network | 16 | 2 | 16 | 1 | 3dB
7 | Dense Network | 16 | 2 | 16 | 4 | 3dB
8 | AP Coop | 2 | 2 | 8X2 | 2 | 9dB
9 | AP Coop | 4 | 2 | 16X2 | 2 | 9dB
10 | AP Coop | 12 | 1 | 4x4 | 1 | 12dB
11 | AP Coop | 12 | 1 | 4x4 | 12 | 12dB
Ng: 4
MCS: 3
BW: 20 MHz
HE-LTF mode: 2x, GI: 0.8 msec
Overhead comparison result considering repetitions of EHT-LTF
Explicit sounding
Multi-trigger
Single-trigger
Feedback Procedure Duration (µsec)
Duration
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Sum of Implicit total(new) | 232.8 | 232.8 | 405.6 | 405.6 | 748 | 1189.6 | 517.6 | 176.8 | 290.4 | 2117.6 | 234.4
Sum of Implicit total | 312 | 312 | 484.8 | 484.8 | 985.6 | 2377.6 | 755.2 | 176.8 | 369.6 | 2988.8 | 234.4
Sum of Explicit total | 984.8 | 796 | 1644 | 1644 | 2925.6 | 7748 | 3053.6 | 910.4 | 2789.6 | 4055.2 | 728

## Slide 7: Residual CFO in MU based Sounding
Channel estimation accuracy is extremely important for 16ss and joint transmission.
With number of concurrent user increasing, it requires much smaller CFO to achieve same level EVM as single user. ( Single user --- 350Hz, 8 users --- ~20Hz)
  ChD: 20MHz
  AP NRX: 8
  STA NTX : 1
  STA NSTA : 1, 2,4,8
  STA Tx Power: 9 dBm
  Noise Power: -90 dBm
  CFO for Users: 0~350Hz
  HE-LTF mode: 4x, GI: 3.2 msec
4800 STAs in the cell, 40cm apart
Notes: Channel Estimation for MU-Sounding Assumptions:
  ChD: 20MHz
  AP NRX: 8
  STA NTX : 1
  STA NSTA : 2,4,8
  STA Tx Power: 9 dBm
  Noise Power: -90 dBm
  CFO for Users: ± 0~350Hz, 选择的用户有相同的± CFO
  HE-LTF mode: 4x, GI: 3.2 msec
  Topo: see the figure
  Random select the Users from the topo for MU-Sounding. 10000 Times
  4800 STAs in the cell, 40cm apart
A STA that transmits an HE TB PPDU compensates for carrier frequency offset (CFO) error and symbol clock error. After compensation, the absolute value of residual CFO error with respect to the PPDU carrying the soliciting Trigger frame shall not exceed 350 Hz for data subcarriers when measured at the 10% point of the complementary cumulative distribution function (CCDF) of CFO errors in AWGN at a received power of –60 dBm in the primary 20 MHz.

## Slide 8: Residual CFO in MU based Sounding
Masked LTF in .11ax cannot maintain small CFO if there is Timing Offset.
Timing Offset may be caused by
Distance between STAs and AP is different
A certain amount of symbol synchronization error (Detection Delay) introduced by implementation algorithm
Conclusion:
If no timing offset residual CFO is 10Hz @90%.
If consider timing offset caused by propagation distance and implementation algorithm, residual CFO is impacted.
  ChD: 20MHz
  AP NRX: 8
  STA NTX : 1
  STA NSTA : 6
  STA Tx Power: 12 dBm
  Noise Power: -90 dBm
  CFO for Users: random(200~350Hz）
  HE-LTF mode: 4x, GI: 3.2 msec

## Slide 9: Replicated LTF(s)
Replicate LTF(s) in NDP sounding frame can solve the problem.
EHT-LTF
EHT-LTF
EHT-LTF
EHT-LTF
Group 1
Group 2
Conclusion:
Timing offset has no impact on residual CFO when using replicated LTF(s).
Residual CFO is <5Hz @90%
EHT-LTF
EHT-LTF
EHT-LTF
EHT-LTF
EHT-LTF
EHT-LTF
EHT-LTF
EHT-LTF
2x2 example
  ChD: 20MHz
  AP NRX: 8
  STA NTX : 1
  STA NSTA : 6
  STA Tx Power: 12 dBm
  Noise Power: -90 dBm
  CFO for Users: random(200~350Hz）
  HE-LTF mode: 4x, GI: 3.2 msec

## Slide 10: More simulation on Replicated LTF(s)
  ChD: 20MHz
  AP NRX: 8
  STA NTX : 1
  STA NSTA: 4,6
  STA Tx Power: 3,6,9,12,15 dBm
  Noise Power: -90 dBm
  CFO for Users: random(200~350Hz）
  HE-LTF mode: 4x, GI: 3.2 msec
Conclusion:
Residual CFO of STA is always within 10Hz, no big difference when number of MU increases.

## Slide 11: Summary
We discussed several implicit schemes, including SU-based and MU-based.
Repetitions of EHT-LTF can solve UL/DL power difference issue and residual CFO issue in MU based scheme.
Based on the analysis, we propose implicit sounding as an option in TGbe to help improve sounding efficiency.

## Slide 12: SP1
Do you support to introduce implicit sounding as an optional mode in TGbe?
Y:
N:
Abstain:

## Slide 13: SP2
Do you support to enable non-simultaneous NDP response with multiple trigger for implicit sounding?
Y
N
Abstain
AP(master)
STA1
AP(slave)
STA2
Trigger
NDP
NDP
Trigger

## Slide 14: SP3
Do you support to enable non-simultaneous NDP response with single trigger for implicit sounding?
Y
N
Abstain
AP(master)
STA1
AP(slave)
STA2
Trigger
NDP
NDP

## Slide 15: SP4
Do you support to enable simultaneous NDP response for implicit sounding?
Y
N
Abstain
AP(master)
STA1
AP(slave)
STA2
Trigger
NDP
NDP

## Slide 16: References
[1] 19/1268 Implicit sounding overhead analysis
[2] 19/767 Implicit Channel Sounding in IEEE 802.11 (Feasibility Study)
[3] 18/1191 MU sounding improvements
[4] 19/768 Implicit Channel Sounding in IEEE 802.11
[5] 19/1939 Calibration of Implicit Sounding

## Slide 17: Backup

## Slide 18: MU-MIMO Based Implicit Sounding Challenge
Replication LTF could also work on the residual CFO problem.
Take 2x2 UL MU-MIMO for example.
STA1
STA2
AP
-1,1
1,1
h11
h21
h12
h22
If there is no residual CFO, H
P matrix
Assume residual CFO of STA1 and STA2 are and respectively, H=Y
matrix
By replicating LTF on STA side, residual CFO between STA and AP( and ) can be calculated, then with , inter-user interference is eliminated and H could be got correctly.
Notes: Channel Estimation for MU-Sounding Assumptions:
  ChD: 20MHz
  AP NRX: 8
  STA NTX : 1
  STA NSTA : 2,4,8
  STA Tx Power: 9 dBm
  Noise Power: -90 dBm
  CFO for Users: ± 0~350Hz, 选择的用户有相同的± CFO
  HE-LTF mode: 4x, GI: 3.2 msec
  Topo: see the figure
  Random select the Users from the topo for MU-Sounding. 10000 Times
  4800 STAs in the cell, 40cm apart
A STA that transmits an HE TB PPDU compensates for carrier frequency offset (CFO) error and symbol clock error. After compensation, the absolute value of residual CFO error with respect to the PPDU carrying the soliciting Trigger frame shall not exceed 350 Hz for data subcarriers when measured at the 10% point of the complementary cumulative distribution function (CCDF) of CFO errors in AWGN at a received power of –60 dBm in the primary 20 MHz.

## Slide 19: MU-MIMO Based Implicit Sounding Challenge
=
=
Original LTF
Replicated LTF
By Eigenvalue Decomposition of on AP side, and can be calculated.