## Slide 1
Authors:
Multi-Link Power Saving Discussion
Date: 2020-01-11
Name | Affiliation | Address | Phone | Email
Yonggang Fang | ZTE (TX) |  |  | yfang@ztetx.com
Bo Sun | ZTE |  |  | 
Zhiqiang Han | ZTE |  |  | 
Nan Li | ZTE |  |  | 
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Abstract
This contribution follows up the discussion of EHT multi-link communication to support low latency, high reliability and high throughput applications, and discusses the issue of power consumption in ML operation. It also proposes a possible approach for establishing an anchored link for ML power saving operation.

## Slide 3: Introduction
Multi-Link framework requirements
  In [1], it proposed the ML framework requirements
    Dynamic selecting and switching an operating link to address the use cases of reducing access latency for fast connection, balancing loads, etc..
    Concurrent transmit or receive packets over multiple links to address the use cases of improving transmission reliability and increasing peak-throughput.
    Utilizing multi-link efficiently for power saving especially for stations.
Power consumption issue
  In [2], it summaries power consumption of 802.11ax devices (single link)
    the power consumption in the idle mode is 50mA, 60mA and 75mA for bandwidth 20MHz, 40MHz and 80MHz, respectively.
    the power consumption of receiving mode is 100mA, 140mA and 200mA for bandwidth 20MHz, 40MHz and 80MHz, respectively.
  In ML operation, the power consumption could be multiple times of a single link’s when multiple links are turned on in idle state. Therefore a mechanism is required to address the power consumption issue in ML operation.

## Slide 4: MLD Power Saving Proposal
  Principle
  In MLD active operation mode, at least one link of MLs is enabled and in active state when
    the AP MLD and the non-AP MLD has data to transmit, or
    the non-AP MLD receives from the AP MLD a message for establishing ML operation.
  In MLD power saving operation mode
    Define an anchored link for communication between AP MLD and non-AP MLDs
      optimize the transmission of groupcast frames,
      further reduce the power consumption of non-AP MLD,
      further reduce the overhead of broadcast management frame, e.g. multi-link information may be broadcast only on the anchored link.

## Slide 5: MLD Power Saving Proposal
  MLD Power Saving Operation Setup
  AP MLD may optionally designate one or more links as anchor link(s) and ensure all associated non-AP MLDs to be able to anchor on for the power save operation, and broadcast the information of anchored link(s) in Beacon frames.
    An anchored link may be shared by different non-AP MLDs.
  A non-AP MLD negotiates with the AP MLD for its anchored link and gets confirmed. If the non-AP MLD is a single-link device, it should anchor on the associated link.
  AP MLD or non-AP MLD can change the anchored link at anytime.
    If the AP MLD wants to change anchored link(s), it shall notify non-AP MLDs before the change.
    If a non-AP MLD wants to its anchored link, it needs to negotiate with the AP MLD for the change and gets confirmed.

## Slide 6: MLD Power Saving Proposal
  MLD Operation Modes
  MLD Active Operation (MLD-AO):
    Non-AP MLD enables one or more links based on the need of ML Operation.
  MLD Power Saving Operation (MLD-PSO):
    A non-AP MLD only wake up to receive the buffer state indication in Beacon and the groupcast data on its anchored link. Therefore the non-AP MLD can sleep for a longer time to reduce the power consumption.
    AP-MLD can wake up other link of non-AP MLD on the anchored link.
  A MLD can switch its mode between MLD-AO and MLD-PSO
  Switching Anchored Link
  A MLD (either AP or non-AP) may switch the anchored link for MLD power saving operation when some case happens
    such as for load balance or interference avoidance.
  A MLD may include a new anchored link information for the ML power saving operation in ML switching message exchange.

## Slide 7: MLD Power Saving Proposal
  Non-AP MLD Link State
  Non-AP MLD maintains the state of each link of ML.
    Link-Disabled: This link is disabled for any activity.
    Link-Enabled: This link is in either MLD active operation or MLD power saving operation
      Link-Active: This link is in MLD active operation. The non-AP MLD can receive and/or transmit frames over this link at anytime.
      Link-Awake: This link is in MLD power saving operation. The non-AP MLD can listen the transmission on this link, but not transmit.
      Link-Doze: This link is in sleep for power saving. The non-AP MLD does not listen or transmit on the link.
Link-Active
Link-Awake
Link Disabled
Link-Doze
Power Saving
Link Enabled

## Slide 8: MLD Power Saving Proposal
  ML UL transmission
  Non-AP MLD in MLD-PSO mode can activate one or more non-anchored links at anytime for UL transmissions, i.e. transit the anchored link and/or non-anchored links to the active state for UL transmissions.
ML DL transmission
  AP MLD may send Beacon frames with wake-up indication over the anchored link to wake-up anchored link or non-anchored link(s) of a non-AP MLD in MLD-PSO mode.
    AP MLD may send other frame to wake up one or more than one link on anchored link.
  A non-AP MLD in MLD-PSO mode will activate the indicated non-anchored link(s) after receiving the wake-up indication in Beacon frame, i.e. transit the anchored link and/or non-anchored links to the active state for receiving frames from the AP MLD.
    The non-AP MLD may send a response to notify the AP MLD which link(s) are active.

## Slide 9: Summary
In this contribution, we discuss
  Power consumption issues in ML operation
  A possible approach to address the power consumption on ML operation.

## Slide 10: Straw Poll
  Do you support to include the following in SFD ?
  A non-AP MLD may negotiate with the associated AP MLD a link as the anchored link for the power saving operation.
  YES/NO/ABS

## Slide 11: References
11-19-1095-00-00be-multi-link-requirement-discussion
11-14-0980-16-00ax-simulation-scenarios

## Slide 12
Thank you!