## Slide 1: MLO Synchronous Transmission
Date: 2020-01-10
Authors:
Name | Affiliations | Address | Phone | Email
Matthew Fischer | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | Matthew.fischer@broadcom.com
Notes: November 2012

## Slide 2: Abstract
EHT non-AP STA devices will have operating conditions with restrictions on TX and RX behavior
  E.g. Simultaneous TX/RX might be restricted for certain link channel combinations for non-AP STA aka Synchronous mode
When a Synchronous STA starts a TX on one Link1, medium state of Link2 is lost
  Due to NEXT
Need mechanisms and rules to maintain Link2 medium state during Link1 TX operation
  Main mechanism is to synchronize PPDUs on both links

## Slide 3: Terms (1)
MLD = Multi Link Device
  A device that can perform transmissions and receptions on more than one wireless interface link
SMLD = Synchronous MLD
  Is an MLD that, during transmission on one link is unable to assess the medium condition on at least one other link according to the required performance limit of receiver minimum sensitivity
EBSL = EDCA Backoff Suspended Link
  Is a link of an MLD for which EDCA has been suspended because a transmission by the same MLD on another link has caused an inability to assess the medium condition on this link within the required performance limit of receiver minimum sensitivity

## Slide 4: Terms (2)
AMLD = Asynchronous MLD
  Is an MLD that, during transmission on one link is able to assess the medium condition on at least one other link according to the required performance limit of receiver minimum sensitivity
Note:
  An MLD may have N links for which the relationship of any two links may be either Synchronous or Asynchronous
EHT STA = Extremely High Throughput STA
  A STA that conforms to Extremely High Throughput definition of 802.11 TGbe
EBSL
  EDCA Backoff Suspended Link

## Slide 5: Terms (3)
SLBSS
  Synchronized Links BSS

## Slide 6: Synchronous Transmitter EDCA Problem
STA1 non-AP STA is the first TXOP winner
  STA1 begins TX on Link1 to STAw
STAx attempts transmission to STAw during STA1 Link1 TX
  STA1 Link1 TX NEXT causes RX failure at STA1 Link2
At end of TX on Link1, STA1 identifies Link2 as IDLE
  Unless TX on Link2 > -62 at STA1 location
    Actually, no rule yet on STA1 Link2 CCA sensitivity during Link1 TX!
  STA1 Link2 Backoff quickly resumes and hits 0, STA1 TX on Link2 to STAw causes existing Link2 PPDU failures
E.g. STAw == AP
RA=STAw, TA=STA1
LINK1
RA=STAw, TA=STAx
LINK2
BA
R
C
RED is STA1 TX, other colors are STA1 RX
BA
R
R
R
Potential Loss of MPDUs at STAw
Potential Loss of MPDUs at STAx
R
C
STA1 EDCA DEAF
STA1 EDCA Resumes
Potential Loss of MPDUs at STA1

## Slide 7: SyncTX EDCA Analysis (1)
Link1 STA initiates TX, i.e. Link1 Backoff == 0
Link2 NO synchronous TX was possible
  E.g. simultaneous Link2 Backoff == 0 did NOT happen
Link2 EDCA is deaf on Link2, due to Link1 TX
  Link2 indicates BUSY during Link1 TX due to NEXT
    Different implementations might not indicate BUSY!
  Link2 EDCA is in SUSPEND because of BUSY (new rule!)
Link1 TX finishes, what happens on Link2?
  Link2 EDCA is out of synch with any other Link2 activity
  Can Link2 EDCA resume immediately?
  Is a wait period required? See DOZE AWAKE

## Slide 8: SyncTX EDCA Analysis (2)
Link2 goes deaf during every Link1 TX
  Not good, not real EDCA, this is Partial EDCA!
  Worse than Quasi-asynchronous mode!
    I.e. completely deaf vs partially deaf!
    Except for NAV, PHY_LEN
Techniques for PPDU alignment between Link1 and Link2 make EDCA deafness NOT MATTER
  Require Link2 to indicate BUSY during Link1 TX
  Then, when Link2 hearing is restored, a preamble is starting, or the medium has become free
    I.e. once PPDUs are aligned, deaf Link2 EDCA REMAINS IN SYNCH!

## Slide 9: Unrelated Transmission Alignment (1)
STA1 non-AP STA is the first TXOP winner
  STA1 begins TX on Link1 to STAw
STAx attempts transmission to STAw during STA1 Link1 TX
  STAx aligns its PPDU to end at the same time as STA1 PPDU
    E.g. STAx has observed the PHY header of the STA1 TX PPDU
  STA1 Link1 TX NEXT causes RX blindness at STA1 Link2
At end of TX on Link1, STA1 sees start of PPDU on Link2
  EDCA operates correctly
E.g. STAw == AP
RA=STAw, TA=STA1
LINK1
RA=STAw, TA=STAx
LINK2
BA
R
C
RED is STA1 TX, other colors are STA1 RX
BA
R
R
C
STA1 EDCA DEAF
STA1 EDCA Resumes
C
RA=STAw, TA=STA1
BA

## Slide 10: Unrelated Transmission Alignment (2)
Link2 RTS DUR == 9500
Link2 CTS DUR == 3000, AKA Negotiated DUR
CTS indicates amount of time available for PPDU+BA to create aligned operation
  STAx obeys CTS DUR in its following PPDU transmission, causing RX/TX alignment
Alternatively, STAx can read PHY LEN from Link1 TX
  Uses PHY LEN to create alignment
BA+Q contains AMPDU BA + QoS Data
  Enough symbols to align next transmissions, AKA Forced TXOP Sharing
RA=STA1, TA=STAw
RA=STA1, TA=STAx
BA
RA=STA1, TA=STAw
RA=STA1, TA=STAx
Potential Loss of MPDUs
BA
BA
BA+Q
R
C
R
C
3000
2000
LINK1
LINK2
STAx EDCA

## Slide 11: UTA RX RX with T
BA+T contains AMPDU BA + Time/DUR information
  Time/DUR information indicates exact duration of next PPDU
    And other information similar to a Trigger
      E.g. TX power, Target RSSI, MCS, etc, as optionally desired
    And a suggested BA duration
      Same BA transmitter on both links, so they will be aligned
    All to be used if there is a next PPDU
    All intended to create alignment of subsequent PPDUs
RA=STA1, TA=STAw
RA=STA1, TA=STAx
BA+T
RA=STA1, TA=STAw
RA=STA1, TA=STAx
Potential Loss of MPDUs
BA+T
R
C
R
C
3000
2000
BA+T
BA+T
T
LINK1
LINK2
STAx EDCA
Same Transmitter

## Slide 12: Rule Sets
A Rules
  Alignment
B Rules
  Backoff
C Rules
  CTS, CTA

## Slide 13: A Rules (1)
An MLD shall advertise whether it is operating as an SMLD or AMLD for a given pair of links
  The advertisement is dynamic, the relationship may change
An AP MLD shall indicate whether any synchronous mode MLD are operating in the BSS
  The AP shall indicate the condition in Beacons and Probe Responses
  The existence of the condition invokes the use of A Rules, B Rules and C Rules
  The mode of operation is called SLBSS
    Synchronous Link BSS

## Slide 14: A Rules (2)
An MLD that transmits a PPDU on a link to an MLD may request the MLD to transmit a Trigger on another link eliciting a response from the MLD on that other link
  An MLD that receives a request for a trigger may send such a Trigger
An MLD that is receiving a PPDU from an SMLD on Link1 may send a trigger to the same SMLD on Link2
  The trigger shall include an UL Length field value that elicits a response transmission whose last symbol end time matches the last symbol end time of the PPDU on Link1
  The trigger may elicit an SU PPDU or an HE TB PPDU

## Slide 15: A Rules (3)
A non-AP MLD may transmit up to one Trigger per link that is addressed to one user per link
  Including TRS type triggers
An MLD that has received two PPDUs with the same end time from one or more MLDs on two links should ensure that the transmitted response PPDUs have the same end time
An MLD that transmits a response to an MLD may include a Trigger in the response that elicits a PPDU from a different MLD or from the same MLD

## Slide 16: A Rules (4)
An MLD that initiates transmission of a PPDU on a link should attempt to align the end of the last symbol of the transmission with the last symbol of any ongoing transmission on the other link
  If the associated AP MLD of the MLD has indicated that synchronous alignment is requested within the BSS
An AP MLD shall indicate that synchronous alignment of transmissions is requested within the BSS if at least one associated MLD is operating in synchronous mode
  The indication is a dynamic indication and shall appear in the operation information of Beacons and Probe Responses

## Slide 17: A Rules (5)
An MLD that initiates transmission of a PPDU on a link during an ongoing transmission on the other link should attempt to trigger the response to the PPDU to align with the response to the ongoing transmission
  By predicting the response length of the ongoing transmission
  By examining the trigger information from the ongoing transmission
    And using the trigger information to directly determine the length fo the response transmission on the other link

## Slide 18: A Rules (6)
An MLD that initiates transmission of a response PPDU on a link should attempt to align the end of the last symbol of the transmission with the last symbol of any ongoing transmission on the other link
  If the associated AP MLD of the MLD has indicated that synchronous alignment is requested within the BSS
  Including its own transmission

## Slide 19: A Rules (7)
Inserted Triggers should be:
  Repeated in multiple MPDUs within a PPDU
    To allow opportunity for 3rd parties to receive the information and use it for alignment of their transmissions
  As a separate Trigger MPDU, at the start of the PPDU
    To be identified early when decoding is possible
  Indicated in a new PHY Header field Response Length

## Slide 20: A Rules (8)
Add a new PHY Header field
  Response length
Add a new PHY Header field
  “Transmitting MLD is a synchronous mode MLD”

## Slide 21: A Rules (9)
Everything is made simpler if one link is simply always operated as Trigger-only
  The STA that is transmitting the trigger can only transmit a trigger if:
    It knows the condition on the other link
    It creates a trigger that causes PPDU alignment on the triggered link with the ongoing PPDU on the non-triggered link

## Slide 22: A Rules (1)
An MLD that has received two PPDUs with different end times from one or more MLDs on two links should attempt to ensure that the transmitted response PPDUs have the same end time

## Slide 23: B Rules (1)
An SMLD shall suspend EDCA backoff countdown on a link when a transmission by the same SMLD on another link has caused an inability to assess the medium condition on this link within the required performance limit of receiver minimum sensitivity
  NAV counters and PHY Length based BUSY indication shall not be suspended
  The link is called an EBSL

## Slide 24: B Rules (2)
An EBSL of an SMLD shall remain suspended until
  The NEXT disappears
  AND a minimum medium observation time equal to MMOT is performed
    Or
  A BUSY medium indication is detected using either frame detection or energy detection, or received Medium State Information, before MMOT time has elapsed
    Where medium observation time for a link is time during which there is no transmission on an interfering link, and during which there is an attempt to ascertain the state of the medium through detection of frame transmissions and energy detection

## Slide 25: B Rules (3)
An SMLD monitors the medium on both Link1 and Link2 while not transmitting on either Link
  If the SMLD begins a transmission on Link1, then on Link2:
    The Intra NAV and Basic NAV counters continue to count down if not already at zero
    Any BUSY indication that is asserted as a result of a PHY Length field value is maintained per the PHY Length field value
    If the Link1 to Link2 NEXT allows ED operation on Link2 according to the ED threshold, ED operation continues on Link2
      If the NEXT is above the ED threshold, Link2 shall be indicated as BUSY for the duration of the NEXT
Optional transmission allowance
    If the Link2 Intra NAV and Basic NAV both are at or reach 0 and any PHY Length field value based BUSY indication has reverted to IDLE and NEXT is below the ED threshold and the ED indicates IDLE, then the SMLD may transmit on Link2 at DIFS following the transition from BUSY to IDLE of the last of the aforementioned items to have attained its zero or IDLE state, a PPDU from the AC with the lowest current backoff countdown value

## Slide 26: B Rules (4)
A STA performing EDCA on a link for which MLO Synch Rules are enabled should
  Suspend the EDCA function if the start of a preamble is detected on another link of a set which is operating synchronously
  Should resume EDCA function after the PHY Header LENGTH information has been decoded, or has failed to be decoded
    At this resumption, no AIFS needs to be performed before resuming the countdown of IDLE slots
If a STA does not suspend its EDCA function
  At the start of a preamble on another link of a set which is operating synchronously
    Then the STA shall use RTS-CTS or RTS-CTA or RTS-Trigger when it accesses the medium on that link and obey the timing constraints received in those frames

## Slide 27: B Rules (5)
An MLD operating synchronously may
  Provide Medium State Information to another STA

## Slide 28: C Rules (1)
An EHT STA that receives a CTS in response to an RTS where:
  The DUR field value of the CTS is not equal to RTS DUR field value minus 2xSIFS minus CTS Time
    Where CTS Time is the amount of time required to transmit the PPDU containing the CTS
  Shall ensure that the sum of 2xSIFS plus:
      The length in time of the Data PPDU that it transmits in response to the receipt of the CTS
      The length of the PPDU that is elicited in response to the Data PPDU
    Is equal to the value of the DUR field of the CTS
    Note that a value of 0 may be included in the CTS to indicate
      RTS recipient cannot accept the expected Data PPDU at this time
      RTS transmitter should not assume collision failure or BER failure
      RTS transmitter may retain current CW in backoff process instead of CW increment in response to CTS failure

## Slide 29: C Rules (2)
Allow CTA response to RTS
  CTA includes
    DUR field as in CTS
    Specific information for the following frame including:
      PPDU duration
      MCS
      TX power
      Other parameters that would normally be found in a Trigger frame
      Duration of the BA or other elicited response frame
  CTA recipient transmits a PPDU according to the trigger-like information, including a trigger in the PPDU that triggers a response that corresponds to the response duration from the CTA

## Slide 30: C Rules (3)
RTS recipient may respond with
  Trigger instead of CTS or CTA
  Choice of responding with Trigger can be made based on RTS RA value
    RA is set to the unique MLD address of the RTS recipient
    I.e. an RTS transmitter that addresses the RTS to the MLD address is capable of receiving a Trigger in response
    A RTS recipient may choose to attempt to transmit a Trigger in response to an RTS without knowledge of the ability of the RTS transmitter to receive such a sequence
      It might just work

## Slide 31: RTS Trigger Sequence
Trigger response to RTS
  Link1 recipient either:
    Wins contention on Link2 and transmits a Data PPDU that matches the duration of the Link1 transmission
      Not shown in the diagram
    Receives an RTS from some other STA and responds with a Trigger to force alignment of that STA transmission with the Link1 PPDU
      As depicted in the diagram
RA=STAw, TA=STA2
RA=STAw, TA=STA1
BA+T
RA=STAz, TA=STAw+T
R
C
R
T
BA+T
RA=STAx, TA=STA1+T
EDCA
LINK1
LINK2
BA+T
BA+T
Don’t care, potential loss of MPDUs

## Slide 32: Trigger vs TRS
All discussions referring to Trigger frames can be extended to TRS
  Where TRS is a shortened form of a Trigger that is included in an A-control field

## Slide 33: Trigger Modifications (1)
Any STA is allowed to transmit a Trigger
  I.e. not only an AP is allowed to transmit a Trigger
  Either in response to an RTS, or as an initial PPDU of a TXOP
The Trigger should include parameters that cause
  The triggered PPDU to align with the other link PPDU
The trigger is modified to include a field to indicate that the response to the Trigger is an SU PPDU
  Instead of an HE TB PPDU
The Trigger may trigger more than one user to respond
  In which case, the response would be HE TB PPDU, not SU PPDU

## Slide 34: Trigger Modifications (2)
The trigger is modified to allow the trigger to specify that the recipient is allowed to choose some of the parameters of the trigger response PPDU
  E.g. the trigger includes some means to signal that specific parameters are to be chosen by the trigger recipient, parameters, such as:
    MCS, RSSI Target, Spatial Reuse
  But the PPDU duration must be present and must be used by the trigger recipient
    In order to align the PPDU with the PPDU on other link(s)
CS is not required
  Because RTS was used to solicit the Trigger, so medium IDLE condition and backoff access requirement is already satisfied

## Slide 35: Why Use RTS Trigger Sequence
Need LSIG field from DATA PPDU to synchronize PPDU end times of different links
But, what if:
  RTS transmitter only see the CTS, but not the DATA PPDU?
  RTS transmitter’s two link MACs do not talk to each other
    Then RTS transmitter cannot synchronize it’s Link2 PPDU end time with the PPDU end time of Link1
  Trigger solves these problems
  But there’s a period of ignorance to examine:

## Slide 36: RTS Considerations
RTS DUR field value causes NAV to be set at 3rd party STAs
  Trigger might not allow transmission covering entire NAV
  3rd party STAs might be stuck with NAV<>0 after triggered exchange is completed
    Those STAs are locked off of the channel
RTS DUR field value should be a shorter value
  Since the Trigger response will dictate the final duration
    If the Link1 RTS-CTS exchange was observed, then the Link2 RTS should use the same NAV as the Link1 exchange, accounting for the passage of time
    RTS receiver does not know how much time the RTS transmitter needs, because the DUR is short

## Slide 37: Maybe Need to Delay The Trigger
  If Link2 backoff expires in the window from Link1 start of RTS to completion of Link1 Data PPDU LSIG field
    Link1 PPDU LSIG LENGTH not available in this window
    Responder to RTS can use techniques to delay the Trigger transmission until it has the LSIG LENGTH information to transmit
      E.g. send an NDP or two, or otherwise keep the Link2 medium BUSY
      Transmit the trigger once the LSIG LENGTH information is known
RA=STAw, TA=STA2
RA=STAw, TA=STA1
BA+T
RA=STAw, TA=STA2+T
R
C
R
T
BA+T
RA=STAw, TA=STA1+T
EDCA
LINK1
LINK2
BA+T
BA+T
N
LSIG LENGTH info available
LSIG LENGTH not yet available
Don’t care, potential loss of MPDUs

## Slide 38: Or Trigger A Short PPDU
Respond to RTS with a Trigger for a “short” duration
  I.e. a “short” trigger
    Really, a trigger that elicits a “short” response
Follow up with a second trigger that matches the remainder of the Link1 PPDU
  I.e. a trigger that enforces an alignment with the other link
RA=STAw, TA=STA2
RA=STAw, TA=STA1
BA+T
RA=STAz, TA=STA2+T
Don’t care, potential loss of MPDUs
R
C
R
T
BA+T
RA=STAx, TA=STA1+T
EDCA
LINK1
LINK2
BA+T
BA+T
LSIG LENGTH info available
LSIG LENGTH not yet available
RA=STAwTA=STA1
BA+T
First “short” trigger
Second, “alignment” trigger, maybe combined with BA

## Slide 39: UTA TX TX Case RTS Trigger (1)
MLD AP has declared Link2 as Triggered only
STA1 is the first TXOP winner, begins TX on Link1 with RTS
  STAw estimates time when backoff==0 on Link2
    Potentially after the RTS reception
  STAw prepares Link1 Trigger response to RTS based on expected start time of Trigger on Link2, to align Trigger end times
    E.g. create Link1 Trigger that is longer than it needed to be
  STAw prepares Link1 and Link2 Triggers to have identical elicited response PPDU end times
  Link2 EDCA backoff==0 time is fairly predictable because of Trigger-only restricted operation on Link2
  Data PPDUs potentially need TRS or Trigger to ensure that BA response PPDU durations are equal
RA=STAw, TA=STA1
RA=STAw, TA=STA1
BA
R
T
STAw EDCA counts down to 0
BA
LINK1
LINK2
T
BUSY
BUSY
STA1 EDCA counts down to 0
DATA PPDUs

## Slide 40: UTA TX TX Case RTS Trigger (2)
MLD AP has declared Link2 as Triggered only
STA1 is the first TXOP winner, begins TX on Link1 with RTS
  STAw sees start of RTS transmission
  STAw Link2 backoff expires during or even Before RTS reception
    Backoff on Link2 might have expired long before Link1 RTS reception begins!
    In any case, STAw optionally waits for outcome of RTS reception before transmitting on Link2
  STAw detects opportunity for parallel Triggers to STA1 on Link1 and Link2
  STAw transmits parallel Triggers to STA1 on Link1 and Link2
RA=STAw, TA=STA1
RA=STAw, TA=STA1
BA
R
T
STAw EDCA counts down to 0
BA
LINK1
LINK2
T
BUSY
BUSY
STA1 EDCA counts down to 0
STAw chooses to delay transmission

## Slide 41: UTA TX TX Case RTS Trigger (3)
In general in this scheme either:
  AP wins contention on Link1 and begins parallel, synchronized transmissions to one or more recipients
  Non-AP wins contention on Link1 and AP responds to RTS or RFT (see next slide) with Trigger on Link1 and optionally also on Link2
    Triggers with common end times
    Trigger on Link1 is to RTS/RFT transmitter
    Trigger on Link2 is to either RTS/RFT transmitter or to another STA
    AP optionally transmits to data on Link2 to another STA that is synchronized to the Link1 transmission (e.g. TX RX case)
      I.e. synchronized in this case means common start and end times of the PPDUs
  I.e. generally, contention is only performed on Link1 while Link2 is triggered only for uplink (i.e. transmission of data to the AP)
    AP normal access for downlink on Link2, but normally synchronized with PPDUs on Link1

## Slide 42: Additional TX TX Rules
One link is EDCA operation
  Other link(s) triggered only (i.e. number of links may be greater than 2)
Allow Any STA to TX Trigger
  i.e. not only AP
  Non-AP sends modified Triggers only
    I.e. no MU response, only SU response
Generally maintain PPDU alignment between links
  E.g. common start and end times of PPDUs
Create alternate to RTS
  E.g. RFT Request For Trigger
    Similar to RTS, but also:
    Include information in RFT regarding
      Whether RFT transmitter desires Trigger on other links, and if so, which links
      Desired length of trigger-elicited transmissions

## Slide 43: TX TX Last Word, Sort Of
Response to Triggered Link2 PPDU might not match the length of the response to the Link1 PPDU
  Provide response length information in the trigger to ensure that the two responses match
  Not necessary if the responder is the same on both Links
    If responder is the same, then responder should align responses

## Slide 44: Switching TXOP Owners
If AP estimates that Link1 transmitter will not receive a trigger, then AP would likely trigger a different STA
  If AP triggers a different STA, then AP aligns Link transmissions using Trigger parameters
  At end of aligned Link1 and Link2 transmissions, AP responds with BA on each Link
    AP can change the TXOP owner on Link2
    AP can be encouraged to do this by a Trigger request
      Immediate trigger to requester is not possible, so switching TXOP owner is a delayed response to the trigger request
    See next slide

## Slide 45: UTA TX TX Case Triggered Swap
STAw triggers STA2 on Link2 because Trigger reception will fail on Link2 for STA1
  STA1 resumes monitoring Link2 at end of Link1 TX
  STAw BA response on Link2 includes a Trigger for STA1
    I.e. delayed response to the request for trigger
  STA1 is now transmitting synchronously on Link1 and Link2
RA=STAw, TA=STA1
RA=STAw, TA=STA2
BA+T
Q+T TA=STA1
R
C
Trig
Trigger Request
BA+Q
BA+Q
Q+T TA=STA1
STAw EDCA
BA
BA
BA+T
RED is STA1 TX, other colors are STA1 RX
LINK1
LINK2
BA RA==STA2, but T is for STA1
BA RA==STA1, and T is for STA1

## Slide 46: TX TX Priority Access (1)
Allow Link1 Transmitter to transmit on Link2 when NAV and LENGTH collected and active on Link2 has expired:
  I.e. Link2 NAV, CRS LENGTH from before the start of the TX on Link1
    Optionally use only Intra-BSS NAV, i.e. inter-BSS NAV is ignored
  When the last Link2 NAV, LENGTH expires, then:
    Any fully active EDCA STAs on Link2 will be resuming their backoff
      i.e. not initiating any TX
    STA1 may access Link2 after LIFS, no backoff resumption
      No other competition for Link2 because everyone else has a non-zero backoff and
      There is only one TX TX Priority access STA coming from Link1 (i.e. STA1) because there is only one winner on Link1

## Slide 47: TX TX Priority Access (2)
LIFS
  Link IFS, a delay of [SIFS,SIFS+2xSLOT], without examining the medium
Note that Link2 RTS CTS is absent
  RTS CTS exchange is not possible because STA1 cannot RX a CTS on Link2
Optionally only allowed when the previous occupant on Link2 was intra-BSS
  E.g. STA1 BSS Color match observed in PPDU(s) within the preceding Link2 exchange
RA=STAw, TA=STA1
RA=STAw, TA=STA1
BA+T
Q+T TA=STA1
R
C
BA
BA
Q+T TA=STA1
STA1 LIFS
BA+T
RED is STA1 TX, other colors are STA1 RX
LINK1
LINK2
STA1 EDCA
STA1 NAV
BUSY
Data PPDU, TA=STAw
BA
R
C
STA1 BSS Color observed, optional

## Slide 48: TX TX Priority Access (3)
Link2 preceding exchange might be a longer sequence
  E.g. the BA might be followed by another Data PPDU
    E.g. NAV value did not anticipate another transmission
  Add a bit to PHY Header to indicate if another PPDU will follow
    I.e. a bit that indicates that this PPDU is the next to last PPDU of a sequence
    I.e. set this bit to “1” in the PHY header of the Data PPDU with TA = STAw
      Optionally only allow the Priority access when the bit is found set to “1”

## Slide 49: SLBSS Rules
When the AP indicates SLBSS Mode of operation
  All STA should initiate TXOPs with RTS
    Optional, if for example, the initiating STA has received PPDU length information from a link that is synchronous to the link on which it is initiating the TXOP
    In this case, the initiating STA can align its transmission end time to the ongoing PPDU end time without the need for assistance from a trigger

## Slide 50: Resolving Conflict
STA1 tries to force alignment by STAx
  STAx might have its own TX/RX issues and might want to force ailgnment by STA1
  Who has priority?
    First frame transmitted in time determines priority
  How is this resolved?
    No request translates to a requirement
    Each STA receiving instructions can decide on its own to obey or not

## Slide 51: Rules Assuming PPDU SMLD Indication
Same rules, written assuming that each PPDU carries an indication of whether the transmitter of the PPDU is SMLD or not
  An MLD shall enforce PPDU end time alignment of a new transmission on Link2 with the PPDU end time of an ongoing transmission on Link1 if either:
    The Link1 transmission indicates that the source is an SMLD
    The transmitter on Link2 is an SMLD

## Slide 52: Alternate Placement
Any of the aforementioned information for PHY Header or other information for triggering can be placed in an A-control field of an MPDU
  Or within a trigger frame
  Or within a new frame
  Or within the PHY header

## Slide 53: Straw Poll 1
Do you support the inclusion of the following in the SFD:
  802.11be shall define a synchronous transmission mode STA wherein the STA
    Is unable to meet the ED and minimum receiver sensitivity requirements on at least one other link (i.e. an EDCA impaired link) while transmitting on at least one link (i.e. the transmitting link)
    Shall act as though the medium state is BUSY on all EDCA impaired links during transmission on the transmitting link
    Dynamically indicates that it is a synchronous transmission mode STA
  YES
  NO
  ABS

## Slide 54: Straw Poll 2
Do you support the inclusion of the following in the SFD:
  802.11be shall define a trigger message that may be transmitted by an AP or a non-AP STA and elicits an SU PPDU, as a means to assist in creating an alignment of PPDU start and or end times on different links
  YES
  NO
  ABS

## Slide 55: Straw Poll 3
Do you support the inclusion of the following in the SFD:
  802.11be shall define a frame exchange sequence that allows
    A trigger-like frame transmission in response to the receipt of an RTS
  YES
  NO
  ABS

## Slide 56: Straw Poll 4
Do you support the inclusion of the following in the SFD:
  802.11be shall define a rule such that:
    A STA that is the intended recipient of a PPDU that is transmitted by a synchronous transmission mode STA on one link and is the recipient of a PPDU transmitted by any STA on another link that is an EDCA impaired link of the synchronous transmission mode STA should align the end times of the response PPDUs to each of the transmissions
  YES
  NO
  ABS

## Slide 57: Straw Poll 5
Do you support the inclusion of the following in the SFD:
  802.11be shall define a field in the EHT PHY Header that:
    Indicates that the STA that is transmitting the PPDU is a synchronous transmission mode STA
  YES
  NO
  ABS

## Slide 58: Straw Poll 6
Do you support the inclusion of the following in the SFD:
  802.11be shall define an operational mode wherein:
    An AP MLD may define one or more links as EDCA access and one or more links as EDCA-trigger links
      Such that access on the EDCA-trigger link(s) is(are) restricted to trigger-like transmissions and their elicited frames, where the trigger frames are transmitted using EDCA rules by either or both of AP and non-AP(s)
  YES
  NO
  ABS

## Slide 59: Reference
[1] Draft P802.11REVmd_D3.0
[2] Draft P802.11ax_D5.0