## Slide 1: Multi-link TIM design
Date: 2020-1-9
Authors:
Name | Affiliations | Address | Phone | Email
Alexander Min | Intel |  |  | alexander.w.min@intel.com
Minyoung Park |  |  |  | minyoung.park@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Po-kai Huang |  |  |  | po-kai.huang@intel.com
Chittabrata Ghosh |  |  |  | chittabrata.ghosh@intel.com
Dibakar Das |  |  |  | dibakar.das@intel.com
Notes: September 2012

## Slide 2: Abstract
This presentation discusses two options for TIM (Traffic Indication Map) design for 802.11be multi-link PSM operations
  Multi-link TIM (ML-TIM) concept was proposed in [11-19/1544r0]
  We discuss two approaches for multi-link PSM operation
    Reuse legacy TIM element to convey TIM information for all the links
    Use a separate ML-TIM element to convey TIM information for other links
  We compare pros and cons of two design options
  We propose ML-TIM element with an example frame format
    Detailed frame format design is TBD

## Slide 3: Background – Multi-link TIM
Multi-link TIM (ML-TIM) indicates buffered data for other links
  Each AP in AP MLD (multi-link device) conveys a separate ML-TIM element for buffered data information for other links
  Each STA in non-AP MLD can receive Beacons in any link and uses an ML-TIM element to obtain per-link traffic information without needing to receive Beacons in all the links → better power save

## Slide 4: Option 1 : Legacy TIM approach
Reuse legacy TIM to convey TIM information all the links
  Goal is to reuse legacy TIM element in Beacon and include TIM information for other links
  Use different/non-overlapping range of AIDs per link per AP
  STAs in a non-AP MLD gets an AID per link chosen from different range of AIDs
    E.g., AID 5 for STA 1 from AID range [1-600], and AID “610” for STA 2 from AID range [601-1200]
Link 1
AP MLD
AP 1
AP 2
Non-AP MLD
Link 2
time
: Awake
: Doze
: Data frames
: Beacons
…
Tx/Rx activities
…
Beacon
…010…001…
TIM bitmap
Bit locations corresponding to AIDs 5 & 610
Beacon
…001…010.…
TIM bitmap
Bit locations corresponding to AIDs 5 & 610
STA 1
STA 2
(AID: 5)
(AID: 610)
AID range
: [1-600]
AID range
: [600-1200]
TIM
TIM

## Slide 5: Option 2 : ML-TIM approach
Use ML-TIM to convey TIM information per link
  Goal is to avoid the constraints of different non-overlapping range of AIDs
  Include partial virtual bitmaps for other links in a different element with Link ID
  This allows two options for AID allocation
    2-a) Have the same AID for all the STAs in a non-AP MLD
    2-b) Have different AIDs per STA, but with the ability to reuse the range of AIDs used in other links
Link 1
(ID: 1)
Link 2
(ID: 2)
time
: Awake
: Doze
: Data frames
: Beacons
…
Tx/Rx activities
…
TIM indicates data buffered for AID 5 at AP MLD in Link 1
TIM
ML-TIM
Beacon
…00101…
TIM bitmap
…00001…
TIM bitmap
2
Link ID
Bit location corresponding to AID 5
ML-TIM indicates data buffered for AID 5 at AP MLD in Link 2
TIM
ML-TIM
Beacon
…00001…
TIM bitmap
…00101…
TIM bitmap
2
Link ID
Bit location corresponding to AID 5
Non-AP MLD
STA 1
STA 2
(AID: 5)
(AID: 5)
AP MLD
AP 1
AP 2

## Slide 6: Comparison of two options
Comparison of legacy TIM vs. ML-TIM for multi-link PSM
 | Option 1 (Legacy TIM) | Option 2 (ML-TIM)
Per-link AID allocation | Required | Not required
Link ID | Not required | Required
TID-link mapping | Supported (via AID) | Supported (vid Link ID)
AID allocation coordination (example in slide 7) | May require coordination among APs for AID allocation | Require minimal (or no) coordination among APs for AID allocation
AID space | Required # of AID values may increase by # of links | Required # of AID values remains the same as single link
MAC overhead (example in slide 8) | Require a single legacy TIM element but with an extended partial virtual bitmap size | Require multiple partial virtual bitmaps per link

## Slide 7: Example scenario 1
Legacy TIM approach may require coordination among APs to maintain efficiency in TIM bitmap construction
  Consider a scenario where AP 1 and AP 2 in AP MLD shares the entire AID range and allocate consecutive AID values for multiple link
    AIDs 1-2 for links 1 and 2 for STA 1, AIDs 3-4 for links 1 and 2 for STA 2, etc.
  In this case, the total size of partial virtual bitmap field(s) can be the same (i.e., 40 bits) for both legacy TIM and ML-TIM approaches
  However, such operation requires a tight coordination among APs for AID allocation
STA
STA
AP MLD
AP 1
AP 2
Non-AP MLLEs
STAs
STA
STA
STAs
Link 1
Link 2
AID range
: [odd #s]
AID range
: [even #s]
AID allocation
1, 3, …, 39
AID allocation
2, 4, …, 40
20 STAs

## Slide 8: Example scenario 2
ML-TIM can be more efficient in terms of TIM bitmap construction
  Consider a scenario where AP 1 and AP 2 in AP MLD have separate AID range
    1-600 for AP 1 in link 1 and 601-1200 for AP 2 in link 2
  Legacy TIM: Size of the partial virtual bitmap (PVB) can be 620 bits (1-620)
  ML-TIM: Total size of PVB fields can be 2x20 = 40 bits (1-20 and 601-620)
  To avoid such inefficiency in TIM construction, legacy TIM approach requires more careful coordination among APs regrading AID allocation, adding more complexity
STA
STA
AP MLD
AP 1
AP 2
Non-AP MLLEs
STAs
STA
STA
STAs
Link 1
Link 2
AID range
: [1-600]
AID range
: [601-1200]
AID allocation
1, 2, …, 20
AID allocation
601, 602, …, 620
20 STAs

## Slide 9: Example ML-TIM element format
ML-TIM element format includes
  Link ID: indicates target link
  Per-link TIM information: indicates link-specific TIM bitmap information
ML-TIM can convey TIM information for multiple links
  Per-link TIM information subfields can be concatenated (as shown in figure below)
  Example ML-TIM frame format (detailed design is TBD)
1
Element ID
Octets:
Length
1
Element ID
Extension
0 or 1
Link ID
TBD
Per-link TIM Information
TBD
For link “x”
Link ID
TBD
Per-link TIM Information
TBD
For link “y”

## Slide 10: Conclusion
We compare two design options for multi-link PSM
  Option 1 : Reuse legacy TIM element to convey TIM information for all the links
  Option 2 : Use a separate ML-TIM element to convey TIM information for other links
We prefer ML-TIM element approach (Option 2 as shown in Slide 5)
  No need to allocate AID per STA in non-AP MLD
    Reuse the concept of “Link ID” and avoid redundancy with AID
  Achieve high MAC efficiency by minimizing TIM bitmap size
    In addition, a single ML-TIM element can concatenate multiple per-link TIM bitmaps
  Allow more modular design w/ higher efficiency and scalability going forward

## Slide 11: References
[1] 11-19/1544r0, “Multi-link Power Save Operation”

## Slide 12: Straw poll
Which option do you support?
  Option 1: Single TIM (legacy TIM with multiple AIDs assigned to a single non-AP MLD)
  Option 2: Multiple TIM (separate TIM information per link)