## Slide 1: Discussions on U-SIG Content and EHT-SIG Format
Date: 2020-01-13
Authors:

## Slide 2: Introduction
EHT preamble consists of U-SIG and EHT-SIG.
  U-SIG is 2-symbol field modulated on per-20MHz basis.
  Some U-SIG version-independent bits are decided.
  EHT-SIG follows U-SIG.
Further discuss on the U-SIG content and EHT structure.
U-SIG
L-STF
L-LTF
L-SIG
RLSIG
U-SIG
L-STF
L-LTF
L-SIG
RLSIG
U-SIG
EHT-SIG
L-STF
L-LTF
L-SIG
RLSIG
EHT-STF, EHT-LTF, EHT-DATA
…
…
…
;;;
…

## Slide 3: U-SIG Content
U-SIG content
  Two-symbol SIG field, and encoded together.
  version-independent bits followed by version-dependent bits.
Version-independent bits:
  PHY format identifier (3 bits), UL/DL (1 bit),
  BSS color (TBD bits), TXOP (TBD bits)
Version-independent Bits
Version-dependent Bits

## Slide 4: U-SIG Content (2)
Version-dependent bits
  PPDU formats bits:
    Every generation may define different number of PPDU formats
    For EHT, we may only need 1 bit
      EHT SU/MU PPDU: EHT SU/MU can have unified format.
      EHT TB PPDU
  EHT-SIG decoding information bits:
    EHT-SIG can have various MCS and length, depending on PPDU format, number of users, etc.
    EHT-SIG MCS: e.g. 4 bits
    Number of EHT-SIG symbols: e.g. 5 bits

## Slide 5: EHT-SIG Structure
EHT-SIG contains all other PPDU decoding related signaling bits.
Unified EHT-SIG structure for SU/MU transmissions.
  Channel puncturing will be common for EHT, especially for higher BW>160MHz and in 6GHz.
    There is no clear distinction between SU and MU signaling.
    For SU or MUMIMO, channel puncturing information will need to be signaled, similar as the resource allocation for OFDMA.
  EHT-SIG will always exists for SU and MU, there is no preamble structure difference.
    Differently from 11ax where SU does not have SIGB symbols.
    Define specific SU preamble does not save much signaling effort, and not able to simplify receiver design.

## Slide 6: EHT-SIG Content: SU/MU
EHT-SIG for both SU and MU will consist of Common field and User-specific field.
Common field:
  Contains signaling bits that are common for all users: e.g. RU allocation/puncturing, Number of LTFs, GI+LTF size, etc.
User-specific field:
  Contains signaling bits that are specific for each user: e.g. STA_ID, per-user MCS, coding, Nsts, etc.
Common field
User-specific field

## Slide 7: Summary
U-SIG version-dependent field can includes:
  PPDU format bits, and
  EHT-SIG decoding related information: MCS, number of symbols, etc.
EHT-SIG uses unified structure for SU and MU.
  One PPDU format for SU/MU.

## Slide 8: SP1
Do you agree that U-SIG version-dependent bits include PPDU format bits for EHT?
Number of bits TBD

## Slide 9: SP2
Do you agree that EHT defines single PPDU format for EHT SU and EHT MU?

## Slide 10: Reference
[1] Rui Cao, and etc., “EHT Preamble Design”, 11-19/1540.
[2] Sameer Vermani, and etc., “Further Ideas on EHT Preamble Design”, 11-19/1870.