## Slide 1: Multi-AP Coordinated BF in IEEE 802.11be
Date: 2020-01-11
Authors:

## Slide 2: Coordinated BF
Coordinated Beamforming (CBF) has been proposed in [1,2, 3] as one of the Multi-AP coordination schemes.
  Multiple APs are coordinated and transmit in the same time/frequency (each to their own STAs)
  There is no joint data processing across multiple APs
  Data of Each STA is sent from a Single AP
There have been several contributions covering performance gains and use cases for CBF, e.g. [3, 4, 5].
This is shown that CBF provides appealing performance/complexity trade-off.

## Slide 3: Coordinated BF
Transmitter: Interference mitigation (e.g. ZF) and coordinated Scheduling at each AP
Multi-AP Channel Sounding is required to provide some information on interference channel.
There have been several contributions on Multi-AP explicit channel sounding in specific for CBF, e.g. [6-10].
Implicit channel sounding is also proposed in [ 6, 11,12] to reduce network overhead.
In summary, the study on Multi-AP Coordinated BF is mature enough to prove major Sum Throughput gain over single AP in many use cases.
In this contribution, we recommend including Coordinated BF in .11be.
In view of prioritization of technologies proposed in [13], CBF may be considered for Rel. 2.

## Slide 4: SP
Do you support adding “Multi-AP Coordinated BF” to 802.11be SFD as one of the multi-AP coordination schemes?
  Note: This feature is for rel. 2
  Y
  N
  A

## Slide 5: References
[1]: Terminology for AP Coordination, doc.: IEEE 802.11-18/1926r2
[2]: Considerations on AP Coordination, doc.: IEEE 802.11-18/1576
[3]: Multi-AP Collaborative Beamforming in IEEE802.11, doc.: IEEE802.11-19/0772r1
[4]: Nulling and Coordinated Beamforming, doc.: IEEE802.11-19/0638
[5]: Performance of Coordinated Null Steering in 802.11be, doc.: IEEE802.11-19/1212
[6]: Coordinated Beamforming/Null Steering Protocol in 802.11be, doc.: IEEE802.11-19/1594r2
[7]: Sounding procedure in AP collaboration, doc.: IEEE802.11-19/1097r0
[8]: Sounding for AP Collaboration, doc.:IEEE802.11-19/1535r2
[9]: Consideration on Multi-AP Sounding, doc.: IEEE802.11-19/1134r1
[10]: Channel Sounding for Multi-AP CBF, doc.: IEEE802.11-20/0123
[11]: Implicit Channel Sounding in IEEE 802.11, doc.: IEEE802.11-19/0768r0
[12]: Multi-AP Implicit Channel Sounding, doc.: IEEE802.11-20/0089
[13]: Adopting a release framework to meet 802.11be timeline, doc.: IEEE 802.11-19/2153

## Slide 6
Back Up

## Slide 7: Example I:Two Single-user Cells [3]
AP: 4 antennas
STA: 2 antennas
2 Overlapping Cells, distance between APs=45 m
One STA in each cell.
STA’s distance from in-cell AP changes (1: 30 m)
STA-1
STA-2
AP-1
AP-2
45 m
Int.
30 m

## Slide 8: Example II: 3 APs [3]
3 overlapping APs: Single user/ AP1 and AP3, Two STAs/ MU MIMO/AP2
One SS to each STA
STA-4
AP-3
STA-3
AP-2
50 m
STA-2
STA-1
AP-1
30 m

## Slide 9: Example III: Two STAs per AP [3]
Distance between APs=45 m, Two STA (MU-BF) in each cell (dropped randomly in (1:30 m) from in-cell AP).
One SS to each STA
STA-3
AP-2
STA-4
STA-1
AP-1
45 m
Int.
STA-2
30 m