## Slide 1: Block Ack Window Extension
Date: 2020-01-10
Authors:

## Slide 2: Motivation
IEEE 802.11be EHT PHY supports 320 MHz bandwidth, 16 spatial streams, 1024 QAM, and multi-link aggregation.
In order to fully utilize the increased PHY rates, improving the MAC efficiency is more important.

## Slide 3: Block Ack Window and Block Ack Bitmap
Maximum Block Ack Window and supported Block Ack Bitmap of 802.11ax and 802.11ay.
 | 802.11ax | 802.11ay | 802.11be
Max PHY Peak Rate (Mbps) | 9,607.8 | 37,917.00 | About 48,000
aPPDUMaxTime (ms) | 5.484 | 2 | 5.484
aPSDUMaxLength (Octets) | 6,500,631 | 4,194,303 | About 32,900,000
Maximum Block Ack Window | 256 | 1K | ???
Block Ack Bitmap | 16 (Fragment Level 3), 64, 256 | 64, 128, 256, 512, 1K | ???

## Slide 4: Block Ack Window and Block Ack Bitmap
If 802.11be MAC supports similar MAC efficiency with 802.11ax,
  The maximum Block Ack Window and the maximum number of MSDUs/A-MSDUs of the 802.11be that can be acknowledged (maximum Block Ack Bitmap) should be 5 times (32,900,000/6,500,631) higher value than 802.11ax.
 | 802.11ax | 802.11ay | 802.11be
Max PHY Peak Rate (Mbps) | 9,607.8 | 37,917.00 | About 48,000
aPPDUMaxTime (ms) | 5.484 | 2 | 5.484
aPSDUMaxLength (Octets) | 6,500,631 | 4,194,303 | About 32,900,000
Maximum Block Ack Window | 256 | 1K | 1.3 K
Block Ack Bitmap | 16 (Fragment Level 3), 64, 256 | 64, 128, 256, 512, 1K | 16 (Fragment Level 3), 64, 256, 512, 1K, 1.5K

## Slide 5: Block Ack Window and Block Ack Bitmap
It seems that TGbe MAC should extend the maximum Block Ack Window to at least 1.3K, and allow the Block Ack Bitmap of 512, 1K and 1.5K.
  Extending the maximum Block Ack Window to more than 2K may be needed for the multi-link operation that uses more than 2 links which have 320MHz and 16 SS.
  In such case, the Sequence Number space has to be extended. But, this should be an optional feature. Because it is not common use case.

## Slide 6: Unified Sequence Control
The A-MPDU does not aggregate the fragment MDPUs except for a dynamic fragment MPDU.
So, a basic idea is to unify the Fragment Number space into the Sequence Number space.
  So, the Sequence Number space can be extended from 12 bits (4K) to 15 bits (32K).
    In consequence, the A-MPDU can aggregate more MPDUs.

## Slide 7: Unified Sequence Control
Unifying the Fragment Number space into single Sequence Number space. [1]
 | Preceding Fragments (PF) | Sequence Number (SEQ)
Bits: | B0 | B1 B15
<Frame Control field>
<Unified Sequence Control field>
(MF)

## Slide 8: Unified Sequence Control
Fragmentation Identification
  The Preceding Fragments subfield and the More Fragments subfield indicates whether the MPDU contains an unfragmented MSDU or a fragmented MSDU.
  Also, when the MPDU contains a fragmented MSDU, the Preceding Fragments subfield and the More Fragments subfield indicates whether it is the first fragment, the last fragment, or the middle fragment.
Preceding Fragments (PF) | More Fragments (MF) | 
0 | 0 | Unfragmented MSDU
0 | 1 | Fragmented MSDU (First fragment)
1 | 1 | Fragmented MSDU (Middle fragment)
1 | 0 | Fragmented MSDU (Last fragment)

## Slide 9: Unified Sequence Control
Ordering of a MSDU
  Regardless of whether the MSDU is fragmented or not fragmented, each MPDU that contains either the unfragmented MSDU or fragmented MSDU has an consecutive and unique value in the Sequence Number subfield (SEQ) in the Sequence Control field.

## Slide 10: Unified Sequence Control
Example
  MSDU1 is carried in MPDU1 having SEQ(1), MF(0) PF(0).
  MSDU2 is carried in MPDU2 having SEQ(2), MF(0) PF(0).
  MSDU3 is fragmented and is carried in MPDU3, MPDU4, MPDU5, and MPDU6.
    MPDU3 has SEQ(3), MF(1) PF(0).
    MPDU4 has SEQ(4), MF(1) PF(1).
    MPDU5 has SEQ(5), MF(1) PF(1).
    MPDU6 has SEQ(6), MF(0) PF(1).
  MSDU4 is carried in MPDU7 having SEQ(7), MF(0) PF(0).

## Slide 11: Unified Sequence Control
Example
  An EHT STA sends MPDU1, MPDU2, MPDU3, MPDU4, MPDU5, MPDU6, and MPDU7 to the peer EHT STA.
    Those MPDUs can be aggregated into an A-MPDU.
  The peer EHT STA can defragment the fragmented MSDUs by identifying the fragmentation with the Preceding Fragments subfield (PF) and the More Fragments subfield (MF).
    The order of the fragmentation is identified by the Sequence Number subfield.
    When the first fragment, the last fragment and all other middle fragments are correctly received, the peer EHT STA defragments those fragmented MSDUs. Otherwise, all fragments are discarded.

## Slide 12: Unified Sequence Control
MPDU1 - SEQ(1) - PF(0) - MF(0)
MPDU2 - SEQ(2) - PF(0) - MF(0)
MPDU3 - SEQ(3) - PF(0) - MF(1)
MPDU4 - SEQ(4) - PF(1) - MF(1)
MPDU5 - SEQ(5) - PF(1) - MF(1)
MPDU6 - SEQ(6) - PF(1) - MF(0)
MPDU7 - SEQ(7) - PF(0) - MF(0)
MSDU1
MSDU2
MSDU3
MSDU4
MPDU1 - SEQ(1) - PF(0) - MF(0)
MPDU2 - SEQ(2) - PF(0) - MF(0)
MPDU3 - SEQ(3) - PF(0) - MF(1)
MPDU4 - SEQ(4) - PF(1) - MF(1)
MPDU5 - SEQ(5) - PF(1) - MF(1)
MPDU6 - SEQ(6) - PF(1) - MF(0)
MPDU7 - SEQ(7) - PF(0) - MF(0)
MSDU1
MSDU2
MSDU3
MSDU4
Fragmentation
Defragmentation

## Slide 13: Unified Sequence Control
MPDU1 - SEQ(1) - PF(0) - MF(0)
MPDU2 - SEQ(2) - PF(0) - MF(0)
MPDU3 - SEQ(3) - PF(0) - MF(1)
MPDU4 - SEQ(4) - PF(1) - MF(1)
MPDU5 - SEQ(5) - PF(1) - MF(1)
MPDU6 - SEQ(6) - PF(1) - MF(0)
MPDU7 - SEQ(7) - PF(0) - MF(0)
MSDU1
MSDU2
MSDU3
MSDU4
MPDU1 - SEQ(1) - PF(0) - MF(0)
MPDU2 - SEQ(2) - PF(0) - MF(0)
Error
MPDU4 - SEQ(4) - PF(1) - MF(1)
MPDU5 - SEQ(5) - PF(1) - MF(1)
MPDU6 - SEQ(6) - PF(1) - MF(0)
MPDU7 - SEQ(7) - PF(0) - MF(0)
MSDU1
MSDU2
MSDU4
Fragmentation
Discarded because first fragment is missed

## Slide 14: Unified Sequence Control
MPDU1 - SEQ(1) - PF(0) - MF(0)
MPDU2 - SEQ(2) - PF(0) - MF(0)
MPDU3 - SEQ(3) - PF(0) - MF(1)
MPDU4 - SEQ(4) - PF(1) - MF(1)
MPDU5 - SEQ(5) - PF(1) - MF(1)
MPDU6 - SEQ(6) - PF(1) - MF(0)
MPDU7 - SEQ(7) - PF(0) - MF(0)
MSDU1
MSDU2
MSDU3
MSDU4
MPDU1 - SEQ(1) - PF(0) - MF(0)
MPDU2 - SEQ(2) - PF(0) - MF(0)
MPDU3 - SEQ(3) - PF(0) - MF(1)
MPDU4 - SEQ(4) - PF(1) - MF(1)
MPDU5 - SEQ(5) - PF(1) - MF(1)
Error
MPDU7 - SEQ(7) - PF(0) - MF(0)
MSDU1
MSDU2
MSDU4
Fragmentation
Discarded because lastf fragment is missed

## Slide 15: Unified Sequence Control
MPDU1 - SEQ(1) - PF(0) - MF(0)
MPDU2 - SEQ(2) - PF(0) - MF(0)
MPDU3 - SEQ(3) - PF(0) - MF(1)
MPDU4 - SEQ(4) - PF(1) - MF(1)
MPDU5 - SEQ(5) - PF(1) - MF(1)
MPDU6 - SEQ(6) - PF(1) - MF(0)
MPDU7 - SEQ(7) - PF(0) - MF(0)
MSDU1
MSDU2
MSDU3
MSDU4
MPDU1 - SEQ(1) - PF(0) - MF(0)
MPDU2 - SEQ(2) - PF(0) - MF(0)
MPDU3 - SEQ(3) - PF(0) - MF(1)
Error
MPDU5 - SEQ(5) - PF(1) - MF(1)
MPDU6 - SEQ(6) - PF(1) - MF(0)
MPDU7 - SEQ(7) - PF(0) - MF(0)
MSDU1
MSDU2
MSDU4
Fragmentation
Discarded because middle fragment is missed

## Slide 16: Unified Sequence Control
The Unified Sequence Control field can be used in the Data frame of the TID on which the block ack agreement that enabled the Unified Sequence Control has been established.
  Without the block ack agreement, the Unified Sequence Control field is not used in the Data frame.

## Slide 17: Conclusion
The Block Ack Window extension and the Block Ack Bitmap extension are proposed to improve the MAC efficiency 802.11be.
  If more than 2K Block Ack Window is necessary, the Sequence Number space extension is needed..
    As discussed in [1], when extending the Sequence Number space, partitioning of Sequence Number and Fragment Number in the Sequence Control field is not necessary.
    So, the unified Sequence Control field is proposed.

## Slide 18: References
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-1575-00-00be-multi-link-ba-operation.pptx

## Slide 19: Straw Poll 1
Do you support to extend the maximum Block Ack Window to 1K and allow the Block Ack Bitmap of 512 and 1K?

## Slide 20: Straw Poll 2
Do you support the following Unified Sequence Control field and the Fragmentation Identification rule?
 | Preceding Fragments (PF) | Sequence Number (SEQ)
Bits: | B0 | B1 B15
<Unified Sequence Control field>
Preceding Fragments (PF) | More Fragments (MF) | 
0 | 0 | Unfragmented MSDU
0 | 1 | Fragmented MSDU (First fragment)
1 | 1 | Fragmented MSDU (Middle fragment)
1 | 0 | Fragmented MSDU (Last fragment)

## Slide 21: Straw Poll 3
Do you support to use the Unified Sequence Control field in the Data frame of the TID on which the block ack agreement that enabled the Unified Sequence Control has been established?