## Slide 1: Multi-Link Feature Candidates For Release 1
Date: 2020-01-10
Authors:
Name | Affiliations | Address | Phone | email
Huizhao Wang | Quantenna, a division of ON Semi |  |  | huizhao.wang@onsemi.com
Sigurd Schelstraete |  |  |  | 
Abhishek Agrawal |  |  |  | 
Debashis Dash |  |  |  | 

## Slide 2: Introduction
Contribution [1] recommends 11be to adopt phased releases to address time to market concern. And it proposes Release 1 of 11be to have following key features:
  320 MHz bandwidth
  4K QAM
  Multiple RUs to a single STA
  Multi-link operation
We support the phased release and the key feature set of Release 1.
Multi-Link has attracted the most attentions from 11be group, many features have been proposed. Some of them are straight forward and some of them are complicated.
In order to meet the proposed Release 1 timeline, we recommend to define a limited scope of Multi-Link feature set for Release 1 as well

## Slide 3: Limited Multi-Link Feature Set For Release 1
Multi-Link Association
Multi-Link Security Association: authentication and key-exchange
Multi-Link Link mgmt. & power save
Multi-Link Block Agreement: establishment, tear-down, Tx window, Rx reordering, Block ACK response and retry mechanism
MPDU and A-MPDU forming and Rx CRC checking are done independently on per Link basis
Crypto encryption/decryption/MIC checking are done independently on per Link basis
PPDU (all formats) Tx/Rx operations are done independently on per Link Basis

## Slide 4: Straw Poll #1
Do you agree to define a limited scope of features for Multi-Link for Release 1?
Y/N/A

## Slide 5: Straw Poll #2
Do you agree with the proposed Release 1 Multi-Link feature set on page 3 of this slide deck?
Y/N/A

## Slide 6: References
[1] IEEE802.11-19/2153r0, “Adopting a release framework to meet 802.11be timeline”