## Slide 1: Multi-Link Feature Candidates For Release 1
Date: 2020-01-10
Authors:
Name | Affiliations | Address | Phone | email
Huizhao Wang | Quantenna, a division of ON Semi |  |  | huizhao.wang@onsemi.com
Sigurd Schelstraete |  |  |  | 
Abhishek Agrawal |  |  |  | 
Debashis Dash |  |  |  | 

## Slide 2: Introduction (1/2)
Contribution [1] recommends 11be to adopt phased releases to address time to market concern. And it proposes Release 1 of 11be to have following key features:
  320 MHz bandwidth
  4K QAM
  Multiple RUs to a single STA
  Multi-link operation
We support the phased release and the key feature set of Release 1.
For MLO, we propose that Release 1 to focus on basic functionalities, basic performance enhancements, basic power save modes, and basic non-STR constrains (for non-AP STA only)

## Slide 3: Introduction (2/2)
Proposed basic features to be included for Release 1:
  Multi-link discovery, setup & teardown, Security Association (authentication, PTK, GTK key-exchange)
  TID binding options: allow MPDUs from the same TID to be sent on:
    One link (a.k.a flow based aggregation)
    More than one links (a.k.a packet based aggregation)
  BlockACK agreement with buffer size up to 1K
  For non-AP STA with Tx/Rx constraints: define the minimum solution to ensure better DL/UL performance over non-MLO device
  Power save mode:
    Power save state signaling on per link using existing mechanisms
    MLD level TIM

## Slide 4: Straw Poll 1
Do you agree to identify and select MLO features to be included for Release 1?
Y/N/A

## Slide 5: Straw Poll 2
Do you agree with the selected features in page 3 for MLO Release 1?
Y/N/A

## Slide 6: References
[1] IEEE802.11-19/2153r0, “Adopting a release framework to meet 802.11be timeline”