## Slide 1: Discussion on timeline for 802.11be
Date: 2020-01-12
Authors:
Name | Affiliations | Address | Phone | email
Ming Gan | Huawei Technologies, Co. LTD. |  |  | ming.gan@huawei.com
Yunbo Li |  |  |  | 
Jian Yu |  |  |  | 
Xun Yang |  |  |  | 
Chenhe Ji |  |  |  | 
Shimi Shilo |  |  |  | 
Osama |  |  |  | 
Yan Xin |  |  |  | 

## Slide 2: Background
Reference [1] proposed to split the features into the two phases by the following motivations
  development of 802.11 should respect the timeline
  Market expectation is already built based on the timeline
  Moreover, in [1] it also points out that contributions on the features in release 1 should be prioritized
  Only the features in release 1 would be converted from SFD into spec text in D0.1/1.0
  No need to pay much attention to other features
  The feature selection criteria for release 1[1]
  Complexity/gain tradeoff
  Time to standardize
  time/investment to implement
  Market needs
  Interest in the features

## Slide 3: Background
  Based on the feature selection criteria, the selected features for release 1 listed in [1] are as follows
  320 MHz bandwidth，
  4K QAM,
  multiple RUs to a single STA,
  multi-link operation
  In this contrition, we would like to show our view on this topic
  Drive amendments from technology side, not procedure and timeline
  We will discuss this topic from the following aspects
  Timeline/Time to market
  Multi-release development
  Minimum requirement of the PAR and FRD
  Competitive

## Slide 4: Timeline/Time to market
The first questions, could the time to market/timeline be the only motivation to split the features into different phases? Was there any related discussion before?
Actually, splitting the features was discussed in an early stage of 802.11 ax (see reference [2]), and did not reach an agreement.
  The author proposed to split the features into 2 waves to speed up the first wave, and used the same criteria to select the features
  The author also mentioned that draft 1.0 should focus on providing a mature spec for the features targeted at 11ax wave 1
  The results of straw poll was: Y 39, N 18, A 62
Today it shows that proposal [1] is not necessary given the success of 802.11ax
  The timeline in 802.11 ax was adjusted again and again to satisfy the technology development
  Many features were included in 802.11ax, such as OFDMA, UL MU-MIMO, SR, TWT, 1024QAM , 6GHz and so on, and they are finally finalized
long track
fast track
IEEE802.11
WFA
11ax
11ax/HEW Wave 1
2014
11ax/HEW Wave 2
2015
2016
2017
2018
2019
From reference 2, Laurent Cariou

## Slide 5: Timeline/Time to market
Beside reference [2], reference [3] also raisd some discussion on timeline, the conclusion is that the timeline should be driven by what the technology will require, not imposed by an official order
  It points out that predicting timelines is almost always in error on the very optimistic side.
  Taking 11ax D1.0 for example, most people predicted the time is Jan or July 2016. However, it was done in Dec 2016 [4].
Regarding the market expectation, was that widely built?
  First, the market is busy deploying the WiFi 6 products in a large scale, and does not have enough time to consider full-fledged Wi-Fi 7 features
  Second, there are just some limited number of sources, e.g. [5][6] which mentioned Wi-Fi market expectation
  If we say some references [5] [6] already built market expectation for timeline, then they also built market expectation for the five competitive features in the PAR[7]
  Because they also mentioned the features in the PAR
  Some chip vendors or OEM may also benefit from the predictable features

## Slide 6: Multi-release development
At the beginning of 802.11be, multi-release development was proposed to reform IEEE’s process for developing amendments in [8] [9]
  Following the procedure of 3GPP, features show up in products based on releases (release 1, release 2, etc.), which are launched a few years apart
  Each release has relative short period.
However, it may be premature given the following factors when developing amendments
  Return on investment, not only for the chip vendors but also for consumers
  The market needs more time to build new consumer demand
Moreover, the excluded features from release 1 in [1], such as HARQ, 16ss, Multi-AP, are expected to have some changes to PHY layer design
  They are totally different from 6GHz in 802.11ax (a pure MAC feature)
  Difficult to have a smart preamble design with forward compatibility for these features
  Hence, multi-release development could not work well at this stage
  We already spent much time to limit the scope of feature candidates
  It also adds extra decision steps / more votes, leading to more LBs, longer CR process

## Slide 7: Minimum requirement of the PAR and FRD
If the multi-release development is not feasible, could release 1 (or call it WiFi 7) meet the minimum requirements of the PAR [7] and FRD [10]?
  Requirement : shall enable at least one mode of operation capable of supporting a maximum throughput of at least 30 Gbps, as measured at the MAC data service access point (SAP).
  The above minimum requirement may not be met given the proposal [1], due to the following factors
  Twice the bandwidth (320 MHz) actually can not double the throughput given the EIRP specified by FCC
  Two times or three times the number of the links also can not double the throughput given that it is not easy to implement 8 or more antennas at each STA in MLD with the limited size and obtain clear 320 MHz simultaneously
  4K QAM can be ignored because it will be rarely used (especially with a large number of streams) and yields only 20% throughput gain when employed

## Slide 8: Competitive
  Last but not the least, the selected features in release 1 in [1] are much less comparative than previous main stream WiFi specs, lacking the distinguished features to support this new generation
  Previous specs introduced SU-MIMO and LDPC in 11n, DL MU-MIMO and mandatory large bandwidth in 11ac, OFDMA, UL MU-MIMO and SR in 11ax
  However, what will we have in 802.11be if we adopt the suggested features as in [1]? It seems a relatively minor improvement.
  All the features are just relative simple extension, e.g., multi-RU OFDMA from single RU OFDMA in 802.11ax, multi-link from multi-band in 802.11ad
  Improvement in both MAC and PHY features for a new generation is desirable
  The excluded features from release 1 [1] , such as HARQ 16ss, are PHY features
  We have both PHY and MAC adhocs, but the queue of PHY is empty now while the queue of MAC is still long
  Based on the existing status, adding PHY features will not delay the spec development significantly

## Slide 9: Conclusion
In this contribution, we proposed to drive amendments from technology side, not procedure and timeline
It is not necessary to split the features into different phases
  Adding extra decision steps / more votes may lead to more LBs, longer CR process
  The time of the discussion for all the features should be guaranteed.
  All the motions of SFD should be converted to the spec draft
  To guarantee the time of the discussion for all the features in the PAR, we propose to add regular F2F adhoc meeting time
  F2F meeting is much more efficient than teleconference call because
  Teleconference call separates the presentation from straw poll
  The quality of teleconference call is bad, frequent connection lost or noise
  The time of teleconference call is not friendly to some place, e.g., a call at 2 AM in some place
  Suggest to reduce the frequency of teleconference call
  Suggest to hold regular TGbe ad hoc face-to-face meetings right before IEEE 802.11 F2F meeting

## Slide 10: References
[1] 11-19/2153r0, “Adopting a release framework to meet timeline”, L. Cariou, Jan, 2020
[2] 11-14/0617r1, “Discussion on timeline for 802.11ax”, L. Cariou, T. Derham, May 2014
[3]11-18/1286/r1, “Predicting timelines: the track record” , Sean Coffey, July 2018
[4]11-14/649/r1, “802.11ax Timeline Scenarios” , Rolf de Vegt, May 2014
[5] https://www.cnet.com/news/wi-fi-6-is-barely-here-but-wi-fi-7-is-already-on-the-way/
[6] https://www.u-blox.com/en/beyond/blog/guest-blogs/wi-fi-7-next-generation-wi-fi-technology
[7] IEEE 802.11-18/1231r6, “802.11 EHT proposed PAR”
[8]11-18/1259r1, “A cascading process for major amendments”, R. Stacey et al., July 2018;
[9]11-18/1284r0, “A proposed way forward”, O. Abould-Magd et al., July 2018
[10]11-19/0722r1, “Proposed TGbe Functional Requirements”, Ming Gan, July 2019

## Slide 11: SP 1
Do you support to hold TGbe ad hoc face-to-face meetings right before IEEE 802.11 F2F meeting, starting from March 2020 ?

## Slide 12: SP 2
Which option do you prefer for TGbe ad hoc face-to-face meetings?
  Option 1: 3 days in the working days
  Option 2: 3 days in the weekend