## Slide 1: Follow Up Discussion on Multi-link Operations
Date: 2020-01-10
Authors:

## Slide 2
Abstract
In this contribution, we follow up on the discussion on using a single ID/MAC address to identify MLE and MLD, and include such address in data frames in order to simplify data flows in multi-link operations.

## Slide 3: Introduction
Architectures enabling multi-band/multi-link operations for 802.11be have been discussed, e.g., in [1] [2]
  Multi-link Device (MLD), AP MLD and non-AP MLD have been defined
  A MLD has a MAC address that identifies the MLD management entity
We have had some discussions on design choices that may simplify data flow [4][5]
  MLD should be identified by the ID or MAC address of their “high” MAC SAPs
  For multi-link data flows, it may be beneficial to include in the data frames a single ID or MAC address of the “high” MAC-SAP of the target MLD
  Some approaches to include such single ID or MAC address of the “high” MAC-SAP have been discussed
In this contribution, we continue to discuss some of the approaches
  To provide more information for some of the questions raised

## Slide 4: Recap of the previous multi-link discussion in [4]
UL and DL data flows are between the “high” MAC-SAPs of the MLDs that contain APs and non-AP STAs
  This “high” MAC-SAP is not the same as MLD Management entity
Hence, the “high” MAC-SAPs should be identified by IDs or MAC addresses
  This “high” MAC-SAPs may share the same ID or MAC address as the MLD Management entity
Therefore, it is beneficial to have these IDs or MAC addresses included in the MAC frames
  E.g., in one of the address fields in data frames

## Slide 5: Recap of benefits using a single ID for multi-link data transmissions
A data frame can be clearly identified to be meant for higher layers if it contains the ID or MAC address of the target higher MAC SAP of the target MLD or MLE
Sequence numbers can be generated uniquely from the same sequence number space and it is easy to re-assemble fragments, packets and detect duplication
If dynamic link switching is desired, a packet can be transmitted over any link without having to regenerate MAC headers
It is easier to identify packets when multi-channel/multi-band aggregation is used to transmit a wide-bandwidth frame
Some of these benefits may depend on the particular design of multi-link operations defined in 802.11be

## Slide 6: Possible approaches
Some possible approaches were discussed in [5] to indicate “high” MAC SAP ID in a data frame/PPDU may be:
  In the preamble
  In the MAC header
  In the Frame body
  Not include “high” SAP ID in data frames/PPDUs, instead making the mapping internal to an MLE/MLD
    May require additional operations
  We want discuss the two highlighted options in more details

## Slide 7: Option 2 Data Packets in Dynamic Link Switching (1/2)
When dynamic link switching is desired, a data packet identified by “high” MAC-SAP address/ID in the MAC header can be transmitted over any link without having to regenerate MAC headers

## Slide 8: Option 2 Data Packets in Dynamic Link Switching (2/2)
Backwards compatibility issues for legacy STAs
  If data packets for EHT STA contain ID/MAC Address of the “high” MAC SAPs, EHT STA needs to filter based on the “high” MAC SAPs
  Legacy STA may not be able correctly detect the “high’ MAC SAPs
It is desirable to avoid causing problems for legacy STAs
  E.g., only sending EHT data frames with “high” MAC SAP IDs to EHT STAs

## Slide 9: Option 2 Data Packets with Link Aggregation
Data packets identified by “high” MAC SAP in the MAC headers can easily be identified as destined for “high” MAC SAP in Link Aggregation
EHT link aggregated PPDUs likely use newly defined EHT format
Hence no backwards compatibility issues are expected

## Slide 10: Option 4 Data Packets
Option 4: Not include the “high” MAC SAP ID in data frames/PPDUs, instead making the mapping to “high” MAC SAP ID internal within an MLE/MLD
  No changes to the current over the air MAC protocols
  Requires additional queueing/duplication detection designs over multiple links
  May require new acknowledgement procedures for multi-link operations
  Requires additional rules between “low” MAC and “high” MAC SAP
  May not be able to be link-agnostic for link switching, link aggregation, etc., depending on the MAC header addressing schemes
  Requires STAs indicating their “high” MAC SAP ID/address to enable the mapping
    This “high” MAC SAP is not the same functionality block as the MLD management entity
    It may use the same as the MAC address as the MLD management entity
  The last requirements need to be clarified, e.g., in the SFD

## Slide 11: Conclusions
In this contribution, we followed up on the topic of including a single ID/MAC address of the “high” MAC SAP of the target MLE/MLD in data frames, which may be beneficial for multi-link data flows
We provided analysis of a number of approaches of providing such indication for data frames/PPDUs

## Slide 12
References
[1] IEEE 11-19/0822r0, Extreme Efficient Multi-band Operation, May 2019
[2] IEEE 11-19/0823r0, Multi-link Aggregation, May 2019
[3] IEEE 11-19/0731r0, Multi-link Operation, May 2019
[4] IEEE 11-19/1213r0, Discussion on Multi-link Operation, July 2019
[5] IEEE 11-19/1568r0, Further Discussion on Multi-link Operation, September 2019

## Slide 13: Straw poll 1
Do you agree that an EHT data frame contains the MLD MAC Address of the receiving MLD device?
Y/N/Abs:

## Slide 14: Straw poll 2
Do you agree that an EHT MLD shall indicate its MLD MAC address during ML setup?
Passed with unanimous consent