## Slide 1
Multilink channel access considering STR capability
Date: 2020-01-13
Authors:

## Slide 2: Introduction
The multi-link operation includes the operation of non-STR capable operation[1]
The AP MLD’s multi-link operation with non-STR capability should be carefully considered[2]
The channel access method for non-STR multi-link should be clarified
This presentation continue to discuss multi-link channel access operation

## Slide 3: Recap: multi-link operation and channel access
Asynchronous multi-link operation: When simultaneous TX on one link with RX on other links is supported
Synchronous multi-link operation: Same time of Tx-Rx
  Similar to the 80+80 operation or preamble punctured operation

## Slide 4: Regarding AP MLD’s STR capability
When AP MLD cannot simultaneously transmit and receive using some of enabled links, following problem may be occurred as in [2]
  Assumption:
    Link 2 and Link 3 generates high IDC interference: Simultaneous transmission on link 2 and reception on link 3 is unavailable
    Non-AP MLD 1 enables Link 1 and Link 2: performs asynchronous operation
    Non-AP MLD 2 enables Link 2 and Link 3: performs asynchronous operation
    One legacy STA is associated with AP in Link 2

## Slide 5: Regarding AP MLD’s STR capability
Since simultaneous transmission in Link 2 and reception in Link 3 is not available and vice versa,
  AP MLD may not be able to transmit the BlockAck to MLD 2 during the reception of PPDU from MLD 1 in Link 2
  AP MLD may not be able to transmit the BlockAck to legacy STA during the reception of PPDU from MLD 2 in Link 3

## Slide 6: Options for supporting Multi-link with non-STR capable links
Option 1: Define primary link for channel access among interfered links
  The EDCA operation is allowed only in the primary link
  The association of legacy STAs is allowed only in the primary link
  The channel access in other links without primary link operation is not allowed
Option 2: AP MLD should be STR capable in all enable links

## Slide 7: Synchronous channel access for non-STR capable non-AP MLD
For non-STR capable non-AP MLDs, the basic operation of multi-link is based on synchronous operation
  Transmission time of each link is aligned
  The transmission using only one link may be permitted
    During the transmission in one link, the transmission using the other links is not permitted
    The transmission using one link in any link is TBD
  Channel access method is TBD

## Slide 8: Semi-synchronous multi-link operation
To enhance the latency of multi-link operation in case of high IDC coexistence, semi-synchronous multi-link is available [3][4][5]
  Based on independent EDCA backoff in each link
  May need to define the backoff operation in each link
    PD in link 2 is not available during the Tx in link 1

## Slide 9: Channel access operation for semi-synchronous operation
As in [6], IDC interference level may be classified to two cases
  The interference prevents the reception of Data frame in another link
  The interference ceases backoff procedure of another link
Appropriate sensing level of other links is needed[4]
  May define new sensing level in case of transmission on link 1

## Slide 10: Channel access operation for semi-synchronous operation
The channel sensing period should be defined in case of unavailable PD operation
  PD in link 2 is not available during the Tx in link 1
    The remained NAV operation may be performed in Link 2
    For new busy indication, the sensing period should be defined
      In the baseline, EIFS period is used to protect ACK frame from hidden node, in case of frame decoding error
      Definition of backoff operation only using ED should be defined

## Slide 11: Conclusion
In this presentation, several issues on channel access with STR capabilities are discussed
For AP MLD, non-STR capabilities in some links may cause transmission problem of ACK frame
  May need to define a dedicated link for EDCA operation
  May mandate the AP’s STR capability
The channel access for non-AP MLD without STR capabilities may performed with synchronous or semi-synchronous operation
  For synchronous operation, the fair and efficient channel access method should be defined
  For semi-synchronous operation, the sensing level and sensing period of the other links should be defined

## Slide 12: Reference
[1] 11-19/1262r6 Specification Framework for Tgbe
[2] 11-19/1405 Multi-Link Operation Channel Access Discussion, Sharan Naribole (Samsung)
[3] 11-19/1546 Legacy Performance Impact on Multi-link Operation, Yongho Seok (MediaTek)
[4] 11-19/1916 MLO-Asynch-Qsynch-Synch, Matthew Fischer (Broadcom Inc)
[5] 11-19/1917 Considerations for multi-link channel access without simultaneous TX/RX capability, Insun Jang (LG Electronics)
[6] 11-19/1541 Performance aspects of Multi-link operations with constraints, Dmitry Akhmetov (Intel)