## Slide 1: Target STA Announcement in AP TXOP of MLO Operation
Date: 2020-03-08
Authors:

## Slide 2: MLO Operations and STR
Multi-link operation (MLO)
  A multi-link device can perform channel access (e.g., EDCA) on multiple wireless links independently
Simultaneous Transmit Receive (STR)
  A multi-link device is capable of independent transmission and receive on each link
  Devices may not be able to perform STR due to hardware constraints or frequency band assignment
In this contribution, we assume that MLD AP is capable of STR and explore issues when STAs are non-STR during an AP TXOP only on one link

## Slide 3: Problem Statement (1/2)
When AP grabs a TXOP only on a link (say, Link 1), and starts DL/UL frame exchange with some STAs on Link 1
During the TXOP
  Different frame exchange may happen on Link 2
  When non-STR STAs monitor frame exchange on Link 1, their Link 2 is almost useless. These non-STR STAs downgrade to single link operation and are stuck on Link 1 during the TXOP if eventually no frame exchange happens with AP on Link 1.
Frame exchange with non-STR STAs?

## Slide 4: Problem Statement (2/2)
Examples:
  STA can not transmit on Link 2 when its Link 2 EDCA counter goes to zero and STA is decoding a Link 1 DL frame (it happens before STA knows the DL frame’s RA)
  STA may lose a DL frame for it on Link 1 because before its UL frame on Link 2 ends, a DL frame on Link 1 arrives
      AP may schedule a DL frame for the STA before it decodes a UL frame from that STA on Link 2
Example 1
Example 2

## Slide 5: Ideas
Knowledge of which STAs to have frame exchange during the Link 1 AP’s TXOP helps improving non-STR STA efficiency if they can doze (suspend, or shutdown) Link 1 during the TXOP and use Link 2 regardless what happens on Link 1
  Non-STR STAs capable of more links benefit more

## Slide 6: Re-Cap of VHT TXOP power save
Motivations
  A station can save power when it knows that there are no frames for it during a downlink MU-TXOP
A non-AP VHT STA that is in TXOP power save mode may enter the doze state until the end of that TXOP when one of the following conditions is met:
  On receipt of a VHT MU PPDU, the STA determines that it is not a member of the group indicated by the RXVECTOR parameter GROUP_ID.
  On receipt of an SU PPDU, the STA determines that the RXVECTOR parameter PARTIAL_AID is not equal to 0 nor does it match the STA’s partial AID
  and, …etc
Drawbacks for those STA allowed to enter doze state
  VHT MU PPDU from AP: any STAs do not belong to the MU group may go to doze
  VHT SU PPDU from AP: any STAs do not match their partial_AID may go to doze
  A single MU/SU PPDU may cause many STAs to go to doze
VHT TXOP power save is not a good solution to the problem in MLO

## Slide 7: Scenario 1
An AP of an AP MLD grabs a TXOP of a link and based on its buffer, it plans to load only DL frames to several target STAs
  An announcement frame of which STAs to have frame exchange during the TXOP is sent before DL data frames
STAs not listed in the announcement frame may make the link enter doze state
  In the end of the TXOP, those STAs resume the link to regular operation

## Slide 8: Scenario 2
An AP of an AP MLD grabs a TXOP of a link and it plans to load both DL and UL frames
  In addition to AP’s own buffer, AP sends BSRP/BSR frames to inquiry STAs’ buffer status
  AP determines which STAs to have frame exchange (UL or DL) during the TXOP and sends an announcement frame before data frames
STAs not listed in the announcement frame may make the link enter doze state
  In the end of the TXOP, those STAs resume the link to regular operation

## Slide 9: Benefits and Discussion
DL TXOP power save for STAs not listed in the announcement frame
Non-STR MLD STA to have no frame exchange during the DL TXOP owns a free link to use
AP may do different levels of estimation of STAs to be listed in the announcement frame
With More Data bit in DL frames, there can be further improvement
Instead of using a specific announcement frame, using an element carried in a broadcast frame is another implementation method
  Frame or element details are TBD

## Slide 10: Straw Poll 1
Do you support that during a DL TXOP of an AP of an AP MLD, the AP may send a broadcast frame carrying information about which STAs to have frame exchange with the AP during the TXOP?

## Slide 11: backup

## Slide 12: Announcement Frame (Element) Content Ideas
Broadcast on specific link(s)
Announcement may contain different contents to save frame size
  Use similar indication as TIM
  Use AID
    AIDs of all STAs expected (not) to have frame exchange during the link’s TXOP
    AIDs of non-STR STAs only expected (not) to have frame exchange during the link’s TXOP (Save announcement size)
    Group ID if necessary
    1 bit indicates “not”
More details are TBD

## Slide 13: Supplemental Data
DL TXOP occupied most of transmission time >70%
Using EDCA to access the channel, the traffic of the access category is allocated in advance
From existed TIDs and STA traffic history, AP has knowledge about
  STAs are running low latency applications
  STAs may have urgent service request
For low latency applications, most of them generate periodic and burst traffic
  The bottleneck is how AP gets a TXOP to transmit in time other than TXOP utilization