## Slide 1: Low Latency Enhancements for R1
Date: 2020-07-28
Authors:
Name | Affiliation | Address | Phone | Email
Duncan Ho | Qualcomm Inc. |  |  | dho@qti.qualcomm.com
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 
Abhishek Patil | Qualcomm Inc. |  |  | 

## Slide 2
Slide 2
A. Asterjadhi (Qualcomm), et. al.,
Three main latency regions (categories) are identified for low latency applications
  10~50ms
    E.g., interactive video, automated vehicles
  1~10ms
    E.g., AR/VR, gaming
  1ms or less
    E.g., TSN-like applications
New emerging cases (e.g., AR/VR) fall into Category B
Background
AR/VR

## Slide 3: Background
Various low latency enhancement proposals have been presented in TGbe
Categories:
  Techniques/mechanisms to improve latency in the MAC [1][2]
  Signaling to convey traffic pattern and QoS demands from non-AP to AP [2]
  Latency measurements and reports [3][4][5]
  Admission control [6]

## Slide 4: Proposed Techniques in IEEE
Summary of techniques/proposals:
  Link-domain/Frequency-domain
    MLO – multi-primary contention and tput aggregation
    TID-to-link mapping – confines less well-behaving or best effort traffic within certain link(s) and reserve other links for low latency apps
    Multiple-channels within a band. EDCA per channel [7]
  Time-domain
    Separate queue at the transmitter that has preferential treatment w.r.t other traffic (intra-MLD) [2]
    New TIDs to indicate low latency traffic (intra-MLD) [2]
    Prioritized EDCA (both intra-BSS and inter-MLD) [1]
    TXOP sharing (given by non-AP to AP) [8], CAP (inter-MLD)
    TSN (both intra-MLD and inter-MLD) [9]
The goal of this contribution:
  Provides a low-latency frame-work for R1, which can be extended for R2

## Slide 5: Achievable Approach in R1
One way to achieve tighter, more predictable latency bound is to use AP Scheduling (what 11ax supports and promotes) combined with MLO
  Step 1: STA indicates its traffic pattern and QoS demand to the AP
  Step 2: AP accepts/rejects per the current condition of the network
  Step 3: If accepted, AP guarantees QoS for the STA using different techniques (e.g., put STA on diff links/MLO/TWT/use currently defined EDCA settings, and any combos etc.)
What’s needed?
  A STA needs to know if an AP offers this type of low-lat service (AP capability) so the STA can request
  Some way for the STA to indicate the traffic pattern and QoS demand (e.g., using MSCS, TCLAS, TSPEC, etc)
  What links the STA prefers (e.g., local co-existence or power save may impact a STA’s preference)
Main Considerations in this proposal
  How to ensure the medium is not occupied by other STAs (e.g., OBSS)
  Can confine 11ax STAs/non-real-time traffic to 2.4 and 5GHz and dedicate 6GHz for low-lat. Still probabilistic in an environment with OBSS but green field 6GHz should be good for some time assuming AP avoids busy 6GHz channels and pick a free 6GHz channel.
Limit to a single BSS optimization in R1

## Slide 6: What’s Needed for R1 (low hanging fruits)
Starting point: 11be already provides MLO. Add the following to enhance low latency support in 11be:
A way for an AP to advertise its low latency service capability
A way for a STA to indicate its traffic pattern and QoS demand
  Indicates period, actual data arrival offset, avg data rate, delay bound, etc.
  E.g., Can use TSPEC, TCLA, MSCS or have a more customized version for low-lat
A way for the AP to redirect the less-latency sensitive traffic (e.g., best-effort/high-volume) on one link to reduce their impact on the low latency traffic
  Allow TID-to-link mapping to confine a TID on a set of specific link(s)
    We have a separation contribution on this to allow negotiation to converge
  Restrict TIDs of BE/high-volume to some links and map low latency TID to other link(s)
Some latency measurement reports from the AP (SP already passed in [4])
User scheduling within 6GHz using 11ax defined TWT with a minor rule change
Use TWT framework with stricter access requirements. Broadcast or Individual TWTs is TBD

## Slide 7: Things to Consider for R2
CAP
For individual AP MLD
  TWT sessions co-ordination
  TSN support
  Enhanced reliability

## Slide 8: SP1
Do you agree to add to the TGbe SFD:
  An AP MLD shall be able to advertise in its capability that it is latency-aware for a non-AP MLD to request QoS treatment
  A non-AP MLD may indicate its traffic demand of a specific flow to an AP MLD that is capable
    TBD what mechanism to use (e.g., TSPEC, TCLA, MSCS or have a more customized version for low-lat)

## Slide 9: SP2
Do you agree to add to the TGbe SFD:
  Allow TID-to-link mapping to confine a TID to a subset of the setup links following the TID link mapping

## Slide 10: SP3
Do you agree to add to the TGbe SFD:
  Allow the use of the existing TID values (0-7) for any traffic
  Allow any TID to map to any AC (mechanism TBD)

## Slide 11: Reference
[1]: 11-20/697: Supporting latency-sensitive applications in 11be (Chunyu Hu, Facebook/NTT/LGE/Tencent)
[2]: 11-20/418: Low latency service in 802.11be (Dave Cavalcanti, Intel)
[3]: 11-20/003: Discussion on latency metric (Suhwook Kim, LG)
[4]: 11-20/105: Link Latency Statistics of Multi-band Operations in EHT (Frank Hsu, Mediatek)
[5]: 11-20/484: Latency Measurement for Low Latency Applications (Liuming Lu, ZTE Corporation)
[6]: 11-19/1615: Multi-band/Multi-channel Operation for Low Latency and Jitter (Liuming Lu, ZTE Corporation)
[7]: 11-20/093: Multi-Link for Low Latency (Adrian Garcia-Rodriguez, Nokia)
[8]: 11-20/005: Proposals on Latency Reduction (Shubhodeep Adhikari, Broadcom)
[9]: 11-19/1287: TSN support in 802.11 and potential extensions for TGbe (Dave Cavalcanti, Intel)