## Slide 1: CID 4076 Technical Motivation
Date: 2020-01-15
Authors:

## Slide 2: Abstract
Technical motivation for 8PSK modes for the DMG SC PHY

## Slide 3: Outline
Background
Proposed new constellations and code rates
Simulation Results
Summary

## Slide 4: Background (1)
The primary market today for Clause 20 / DMG STAs is backhaul
60 GHz backhaul applications will benefit from greater range
  Backhaul typically uses highly directional antennas
  Resulting channel has few reflections and therefore low inter-symbol interference
  Range is limited by available transmit power and required receiver SNR
  Friis Equation and the definition of receiver signal-to-noise ratio
  Combine and solve for range, R, as a function of SNR and transmitter power

## Slide 5: Background (2)
Combined Equation
Range is limited by the square root of the ratio of available transmit power to required SNR at the receiver
By using 8 PSK instead of 16 QAM for MCS 10 and 11, we can greatly increase this ratio

## Slide 6: Background (3)
DMG contains moderate rate MCS modes with 16 QAM constellations
QAM modulation will increase the peak to average ratio of transmitted signals relative to PSK modulations
Practical transmit power amplifiers can transmit much more power using PSK modulation

## Slide 7: Background (4)
For a given constellation, the peak power is the power of the constellation point at the greatest distance from the origin (center). The average power is the mean over all constellation points.
Circular constellations, such as 8 PSK have a peak power equal to the average power. Thus, their peak-to-average power ratio (PAPR) is minimized
16 QAM PAPR = 18/10 = 2.55 dB
8 PSK PAPR = 1/1 = 0.0 dB
16 QAM PAPR = 18/10 = 2.55 dB
8 PSK PAPR = 1/1 = 0.0 dB

## Slide 8: Background (5)
Compression of QAM signals in non-linear components, such as mmwave power amplifiers, low noise amplifiers, and mixers, will also have greater impact on QAM signals than it will on PSK signals
  Compression tends to reduce the minimum distance between outer constellation points and increases the average EVM (error vector magnitude)
  Since bit error rate is a function of minimum distance, the bit error rate increases more for QAM

## Slide 9: Background (6)
8PSK and 16QAM shown with EVM = -19 dB
16 QAM has a much higher peak-to-average ratio and requires a much greater back off from amplifier saturation
This results in a lower transmitter power for 16 QAM.

## Slide 10: Background (7)
16QAM constellation after distortion created with the Rapp Model in the 802.11ay Evaluation Methodology
4.8 dB backoff
-19 dB EVM

## Slide 11: Background (8)
8 PSK Constellation
-1.0 dB backoff
-19 dB EVM
Even at a higher average output power, the 8PSK constellation is more tolerant of amplifier distortion than 16 QAM

## Slide 12: Proposal
Add options to use MCS 10 and 11 with 8-PSK instead of 16-QAM
Signal the capability to employ this option on the DMG Capabilities Field
Signal the use of this option in the DMG SC Mode PPDU Header
Use existing LDPC codes with shortening
Add 8-PSK modulation

## Slide 13: MCS 10 and 11 with 8PSK (1)
8 PSK constellations with higher code rates can be employed instead of QAM constellation with lower code rates
MCS 10: 8 PSK with a rate 2/3 code instead of 16-QAM with rate ½ code
  Rate 2/3 code is generated by shortening the Clause 20 rate ¾ LDPC code
    On encoding, pad 168 zero bits to fill the codeword
    Do not transmit pad bits
    No new LDPC code is needed
Apply pi/2 phase shift per symbol to 8PSK the same way we do for existing DMG SC modulations

## Slide 14: MCS 10 and 11 with 8PSK (2)
MCS 11 – 8 PSK with rate 5/6 code instead of 16QAM with rate 5/8
  Shorten the draft 802.11ay rate 7/8 code to rate 5/6 by padding with zeros to fill the information part of the codeword
  Padded zeros are not transmitted
New LDPC code matrices are not needed
Shortening code words is already a part of 802.11

## Slide 15: MCS 10 Simulation Results
MCS 10 PER with 4096 byte packets, phase noise, and PA distortion. EVM = -19 dB
10 iterations on LDPC decoder
8 PSK requires 0.6 dB greater SNR at 1% PER
8 PSK TX power is 3.9 dB higher
Range increase of 47%

## Slide 16: MCS 11 Simulation Results (1)
MCS 11 PER with 4096 byte packets, phase noise, and PA distortion. EVM = -20 dB
10 iterations on LDPC decoder
8 PSK requires 2.1 dB greater SNR at 1% PER
8 PSK TX power is 4.0 dB higher
Range increase of 27%

## Slide 17: Summary
8 PSK has been evaluated using the phase noise, PA models, and EVM targets for DMG STAs
Range increases of 27% to 47% are possible with MCS10 and MCS11 using 8 PSK instead of 16 QAM
Existing Clause 20 LDPC codes can be shortened to achieve the rate 2/3 and rate 5/6 codes required for 8 PSK
  No new encoder / decoder
We propose adding this feature to 802.11md Clause 20

## Slide 18: Backup

## Slide 19: AWGN Channel Capacity Comparison
From “Bit-Interleaved Coded Modulation” by G. Caire, G. Taricco, and Ezio Biglieri
MCS11 (2.5 bits per symbol)
MCS10 (2 bits per symbol)