## Slide 1: Overview of Target ITU Recommendations and Outline of Required Updates
Author:
Date: 2020-01-15

## Slide 2: Background: Updates to the Recommendations Needed
Inclusion of new IEEE 802.11 technologies
Updates regarding 5GHz and DFS
Characteristics of 6GHz for sharing studies
Recommendation ITU-R M.1450-5: Characteristics of broadband radio local area networks (02/2014)
Recommendation ITU-R M.1801-2: Radio interface standards for broadband wireless access systems, including mobile and nomadic applications, in the mobile service operating below 6 GHz (02/2013)

## Slide 3: Recommendation ITU-R M.1450-5 Outline
Scope
  TABLE 2: Characteristics including technical parameters associated with broadband RLAN standards
Annex 1: Obtaining additional information on RLAN standards
Annex 2: Basic characteristics of broadband RLANs
and general guidance for deployment
  Introduction
  Mobility
  Operational environment and considerations of interface
  System architecture including fixed applications
  Interference mitigation techniques under frequency sharing environments
  General technical characteristics
  TABLE 3: General technical requirements applicable in certain administrations and/or regions

## Slide 4: TABLE 2: Characteristics including technical parameters associated with broadband RLAN standards
Characteristics | IEEE Std 802.11-2016 (Clause 21, commonly known as 802.11ac) | IEEE Std 802.11ah-2016 (TBD) | IEEE Std 802.11ax-2016 | IEEE Std 802.11ay-2016 | IEEE Std 802.11ba-2016 (TBD) | IEEE Std 802.11az-2016 (TBD)
Access method |  |  |  |  |  | 
Modulation |  |  |  |  |  | 
Data rate |  |  |  |  |  | 
Frequency band |  |  |  |  |  | 
Channel indexing |  |  |  |  |  | 
Spectrum mask |  |  |  |  |  | 
Tx Interference mitigation |  |  |  |  |  | 
Rx Sensitivity |  |  |  |  |  | 
To add new STDs and update to the previous STDs (references, 5.1GHz, etc.)

## Slide 5: Annex 1: Obtaining additional information on RLAN standards (updates)
“The IEEE 802.11 standards can be downloaded from: http://standards.ieee.org/getieee802/index.html.
IEEE 802.11 has developed a set of standards for RLANs, IEEE Std 802.11 – 2012, which has been harmonized with IEC/ISO. The medium access control (MAC) and physical characteristics for wireless local area networks (LANs) are specified in ISO/IEC 8802-11:2005, which is part of a series of standards for local and metropolitan area networks. The medium access control unit in ISO/IEC 8802-11:2005 is designed to support physical layer units as they may be adopted dependent on the availability of spectrum. ISO/IEC 8802-11:2005 contains five physical layer units: four radio units, operating in the 2 400-2 500 MHz band and in the bands comprising 5 150‑5 250 MHz, 5 250-5 350 MHz, 5 470-5 725 MHz, and 5 725-5 825 MHz, and one baseband infrared (IR) unit. One radio unit employs the frequency-hopping spread spectrum (FHSS) technique, two employ the direct sequence spread spectrum (DSSS) technique, another employs the orthogonal frequency division multiplexing (OFDM) technique, and another employs a multiple input multiple output (MIMO) technique.
ISO/IEC 8802-11:2005, Information technology – Telecommunications and information exchange between systems – Local and metropolitan area networks – Specific requirements – Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) specifications.”

## Slide 6: IEEE 802.11 Coverage in the Recommendations
IEEE 802.11 Standards/Specifications to be Considered
  IEEE Std P802.11ac-2013, 2013-12-09
  IEEE Std P802.11ah-2016 (?)
  IEEE Std P802.11ax, Nov 2020
  IEEE Std P802.11ay, Dec 2020
  IEEE Std P802.11ba, Sep 2020 (?)
  IEEE Std P802.11az, Mar 2021 (?)
  Others?
IEEE 802.11 technologies should have STD status by the time of approval in SG5 for Publication (that is two months after WP 5A submission of Recommendations to SG5)
WP5A members may request delayed submission to SG5 for publication of STDs

## Slide 7: Annex 2 TABLE 3: General technical requirements applicable in certain administrations and/or regions
“6 General technical characteristics
Table 3 summarizes technical characteristics applicable to operation of RLANs in certain frequency bands and in certain geographic areas. Operation in the 5 150-5 250 MHz, 5 250-5 350 MHz and 5 470-5 725 MHz frequency bands are in accordance with Resolution 229 (Rev.WRC‑12).”
Table 3 updates as related to Res 229 needs to be updated based on result of WRC-19. This may be done directly in 5A; Recommend excluding Table 3 for now.

## Slide 8: Recommendation ITU-R M.1801-2 Outline
Annex 1: Broadband radio local area networks
  1 IEEE 802.11
  2 ETSI BRAN HIPERLAN
  3 MMAC HSWA
Annex 2: IMT-2000 terrestrial radio interfaces
  1 IMT-2000 CDMA Direct Spread
  2 IMT-2000 CDMA Multi-Carrier
  3 IMT-2000 CDMA TDD
  4 IMT-2000 TDMA Single-Carrier
  5 IMT-2000 FDMA/TDMA
  6 IMT-2000 OFDMA TDD WMAN
Annex 3: IMT-Advanced terrestrial radio interfaces
  1 LTE-Advanced
  2 WirelessMAN-Advanced
Annex 4: Harmonized IEEE 802.16 and ETSI radio interface standards, for broadband wireless access (BWA) systems including mobile and nomadic applications in the mobile service
Annex 5: ATIS WTSC radio interface standards for BWA systems in the mobile service
Annex 6: “eXtended Global Platform: XGP” for broadband wireless access (BWA) systems in the mobile service
Annex 7: IEEE 802.20: Standard air interface for mobile broadband wireless access supporting vehicular mobility
Annex 8: Air interface of SCDMA broadband wireless access system standard
Annex 9: Key characteristics of standards
  TABLE 5: Key technical parameters

## Slide 9: Annex 1: Broadband radio local area networks (updates?)
“Radio local area networks (RLANs) offer an extension to wired LANs utilizing radio as the connective media. They have applications in commercial environments where there may be considerable savings in both cost and time to install a network; in domestic environments where they provide cheap, flexible, connectivity to multiple computers used in the home; and in campus and public environments where the increasing use of portable computers, for both business and personal use, while travelling and due to the increase in flexible working practices, e.g., nomadic workers using laptop personal computers not just in the office and at home, but in hotels, conference centres, airports, trains, planes and automobiles. In summary, they are intended mainly for nomadic wireless access applications, with respect to the access point (i.e. when the user is in a moving vehicle, the access point is also in the vehicle).
Broadband radio local area network standards are included in Recommendation ITU‑R M.1450, and can be grouped as follows:
  – IEEE 802.11
  – ETSI BRAN HIPERLAN
  – ARIB HiSWANa.”

## Slide 10: Annex 1: 1 IEEE 802.11 (updates)
“1 IEEE 802.11
The IEEE 802.11™ Working Group has developed a standard for RLANs, IEEE Std 802.11‑2012, which is part of the IEEE 802 series of standards for local and metropolitan area networks. The medium access control (MAC) unit in IEEE Std 802.11 is designed to support physical layer units as they may be adopted dependent on the availability of spectrum. IEEE Std 802.11 operates in the 2 400-2 500 MHz band and in the bands comprising 3 650‑3 700 MHz, 4.94-4.99 GHz, 5.03‑5.091 GHz, 5.15‑5.25 GHz, 5.25-5.35 GHz, 5.47‑5.725 GHz and 5.725‑5.850 GHz. IEEE Std 802.11 employs the frequency hopping spread spectrum (FHSS) technique, direct sequence spread spectrum (DSSS) technique, orthogonal frequency division multiplexing (OFDM) technique, and multiple input and multiple output (MIMO) technique.
Approved amendments to the IEEE 802.11-2012 base standard include Prioritization of Management Frames (IEEE 802.11ae), and Robust Audio Video Streaming (IEEE 802.11aa).
The URL for the IEEE 802.11 Working Group is http://www.ieee802.org/11. IEEE Std 802.11‑2012 and some amendments are available at no cost through the Get IEEE 802™ program at http://standards.ieee.org/about/get, and future amendments will become available for no cost six months after publication. Approved amendments and some draft amendments are available for purchase at http://www.techstreet.com/ieeegate.html.”
Consider removing detailed bands or frequency ranges; like other technologies up-level to high-level ranges

## Slide 11: TABLE 5: Key technical parameters
To add key technical parameters for the new STDs
Standard | Nominal RF channel bandwidth | Modulation/ coding rate(1) upstream downstream | Coding support | Peak channel transmission rate per 5 MHz channel (except as noted) | Beam-forming support (yes/no) | Support for MIMO (yes/no) | Duplex method | Multiple access method | Frame duration | Mobility capabilities (nomadic/ mobile)
IEEE Std 802.11-2016 (Clause 21, commonly known as 802.11ac) |  |  |  |  |  |  |  |  |  | 
IEEE Std 802.11ah-2016 (TBD) |  |  |  |  |  |  |  |  |  | 
IEEE Std 802.11ax-2016 |  |  |  |  |  |  |  |  |  | 
IEEE Std 802.11ay-2016 |  |  |  |  |  |  |  |  |  | 
IEEE Std 802.11ba-2016 (TBD) |  |  |  |  |  |  |  |  |  | 
IEEE Std 802.11az-2016 (TBD) |  |  |  |  |  |  |  |  |  | 

## Slide 12: Summary
Recommendation ITU-R M.1450-5
  Table 2: “Characteristics including technical parameters associated with broadband RLAN standards” Need to add new STDs and update to the previous STDs (references, 5.1GHz, etc.)
  Annex 1: “Obtaining additional information on RLAN standards” needs updates
  Annex 2 TABLE 3: “General technical requirements applicable in certain administrations and/or regions” Recommend no update for now; to be done by 5A directly
Recommendation ITU-R M.1801-2
  Annex 1: “Broadband radio local area networks” may need update (TBD)
  Annex 1: “1 IEEE 802.11” needs updates; Consider removing detailed bands or frequency ranges; like other technologies up-level to high-level ranges
  Annex 9 TABLE 5: “Key technical parameters” add key technical parameters for the new IEEE 802.11 STDs