## Slide 1: Beacon at PIFS
29 January 2020
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com

## Slide 2: A change to allow PIFS for Beacons is required to ensure equal access to the mechanism for all
Executive Summary
  CID 4001 during the initial SA ballot on 802.11md requested a change to allow Beacons at PIFS
  TGmd decided in Jan 2020 that a submission is required to progress consideration of CID 4001
  Mark Rison made a case by e-mail that using CAPs for Beacons allows the use of PIFS … but analysis shows Mark’s reasoning is a stretch
  It was also claimed it is better to allow some to use PIFS non-compliantly than to allow it … contrary to best practice
  A change to allow PIFS for Beacons is required to ensure equal access to the mechanism for all

## Slide 3: CID 4001 during the initial SA ballot on 802.11md requested a change to allow Beacons at PIFS
CID 4001 comment (with corrections in red)
  There has been discussion in the Coexistence SC as to whether the IEEE 802.11 WG should support the proposal in ETSI BRAN to further constrain the use of "short LBT" (like a PIFS) for short control signalling.
  When this proposal was made, it was believed that this would mainly affect the transmission of DRS (like a Beacon) by NR-U. Simulations seemed to show that use of "short LBT" for DRS by NR-U would have an unreasonable adverse affect on 802.11 systems.
  However, there was resistance to supporting the proposal from some 802.11 stakeholders, for reasons that the stakeholders did not want to discuss. It turns out that at least two 802.11 chip vendors often use PIFS without any backoff for the transmission of Beacons. At least one 802.11 chip vendor mostly/always does not.
  …

## Slide 4: CID 4001 during the initial SA ballot on 802.11md requested a change to allow Beacons at PIFS
CID 4001 comment (with corrections in red)
  …
  The problem is that the 802.11 standard does not appear to support the transmission of Beacons at PIFS by these vendors. Instead, the 802.11 standard specifies (11.1.3.2) that Beacons are sent "using the the medium access rules specified in Clause 10", ie DCF or EDCA (HCCA does not seem to apply, given many APs do not implement HCCA). Other clauses (from 802.11ae) in 802.11 suggest that Beacons should be sent using EDCA at AC-VO. Noting that an AP can use an AIFS of 1, this means that Beacons can be sent at PIFS at least sometimes, but this is only because the random backoff is sometimes 0.

## Slide 5: CID 4001 during the initial SA ballot on 802.11md requested a change to allow Beacons at PIFS
CID 4001 proposed change (with corrections in red)
  My personal view is that vendors should not be sending Beacons (or any other similar frames) at PIFS without a backoff, because doing so is known to cause harm to the overall system. However, I will defer to the majority view on this question at this time. That said, if it is desired that Beacons can be sent at PIFS without any backoff then it should be explicitly allowed by the 802.11 standard, so that all implementers are aware of the possibility.
  There are multiple locations in the 802.11 standard where this could be specified. I will leave it to the experts in 802.11 TGmd to determine the most appropriate location for this change, and therefore it most appropriate form. If desired by the BRC, I am willing to provide explicit text.

## Slide 6: TGmd decided in Jan 2020 that a submission is required to progress consideration of CID 4001
  There was a brief discussion about CID 4001 at the TGmd in Irvine in January 2020
  Some speakers seemed to suggest that there was no need to change the standard because anyone who needs to know using PIFS for Beacons is possible is doing so already
    Apologies if this argument is mischaracterised; it is by memory
  Mark Rison suggested that using PIFS for Beacons might be justified by assuming APs transmit Beacons using the CAP generation mechanism (10.23.3.2.2) for HCCA
  Ultimately, it was decided by consensus that CID 4001 included insufficient detail, and that a submission was required

## Slide 7: Mark Rison made a case by e-mail that using CAPs for Beacons allows the use of PIFS …
Summary of e-mail sent by Mark Rison on 14 Jan 2020
  Mark Rison noted that 10.3.2.3.4 allows PIFS to be used for
    An HC starting (M53)a TXOP, as described in 10.23.3.2.2 (CAP generation)
  He also highlighted definitions that explained:
    An HC is a coordinator that implements the frames exchanges defined by HCF
    HCF includes functionality provided by both EDCA & HCCA
  Finally he makes a case that 802.11md D3.0 can be interpreted to allow the use of PIFS for Beacons by using an HCCA CAP for the Beacon
    I don't think anything requires an AP that is an HC and hence implements the HCF to actually use HCCA; it can validly just use EDCA. Hence an AP that implements EDCA that transmits a beacon (and thereby starts a TXOP) may use PIFS.

## Slide 8: … but analysis shows Mark’s reasoning is a stretch
The use of 10.23.3.2.2 to justify sending a Beacon at PIFS requires all APs to contain some HCCA functionality, in conflict with common understanding (1)
  Mark noted that in relation to 10.23.3.2.2 that, “I don't think anything requires an AP that is an HC and hence implements the HCF to actually use HCCA”
  It is true that nothing requires an HC to use HCCA; however, the use of 10.23.3.2.2 to justify sending a Beacon at PIFS does require the use of HCCA because 10.23.3.2.2 is part the HCCA clause
  It should be noted that this is not fatal to the argument that 10.23.3.2.2 can be used justify sending a Beacon at PIFS
  It just means all APs will need to implement at least some of HCCA, which is contrary to common understanding that the use HCCA for transmission is completely optional

## Slide 9: … but analysis shows Mark’s reasoning is a stretch
The use of 10.23.3.2.2 to justify sending a Beacon at PIFS requires all APs to contain some HCCA functionality, in conflict with common understanding (2)
  Mark noted that “I don't think anything requires an AP that is an HC and hence implements the HCF to actually use HCCA; it can validly just use EDCA. Hence an AP that implements EDCA that transmits a beacon (and thereby starts a TXOP) may use PIFS”
  Mark seems to suggest that an EDCA-only AP can use the 10.23.3.2.2 clause to justify sending a Beacon at PIFS
  This is not true because 10.23.3.2.2 is part of the HCCA clause and thus requires an AP sending a Beacon at PIFS to at least partially implement HCCA, which is contrary to common understanding that the use of HCCA for transmission is completely optional

## Slide 10: … but analysis shows Mark’s reasoning is a stretch
The use of 10.23.3.2.2 to justify sending a Beacon at PIFS is obscure, contrary to best practice
  It was noted on a previous page that one could require all APs to implement at least part of HCCA to justify sending Beacons at PIFS
  However, this interpretation is obscure, and seems more like an attempt to justify behaviour after the fact of some vendors using PIFS for Beacons, rather than a process to assist vendors implement intended behaviour in an interoperable/coexistent manner
  It is best practice for standards to be clear and unambiguous and it is poor practice for them to contain obscure mechanisms, especially one for a function as important as medium access for Beacons

## Slide 11: … but analysis shows Mark’s reasoning is a stretch
The use of 10.23.3.2.2 to justify sending a Beacon at PIFS imposes additional constraints on Beacons, contrary to any known practice
  10.23.3.2.2 requires that a CAP complete before the next TBTT
  In the vast majority of cases a Beacon will not cross a TBTT boundary (at least partially because a Beacon delayed for so long will usually be cancelled)
  However, the CAP rule does impose an additional constraint on Beacons that was previously unknown

## Slide 12: It was also claimed it is better to allow some to use PIFS non-compliantly than allow it … contrary to best practice
  Another correspondent agreed that using the text highlighted by Mark Rison to justify PIFS for Beacons was a stretch
  However, he also stated that PIFS for Beacons should not be explicitly specified because it might set a precedent within 802.11 for APs to transmit at PIFS
  He later expressed clarified his concern by noting that PIFS for Beacons was sometimes inappropriate, but defining when it was appropriate would be too difficult
  He preferred the standard say nothing, implying it was OK for “responsible” people in “the know” to violate the standard, but not others
  It is best practice for standards to be clear and unambiguous and it is poor practice for them to contain “unwritten rules” for those “in the know”, especially rules as important as those related to medium access for Beacons

## Slide 13: A change to allow PIFS for Beacons is required to ensure equal access to the mechanism for all
  The various reasons put forward for making no change to allow the use of PIFS for Beacons are uncompelling, representing stretches of logic or violations of best practice
  On the other hand, it is vital that the 802.11 document make it clear to all stakeholders that PIFS for Beacons is allowed, rather than allowing just a few in “the know” to violate the standard with a “nod and wink”
  CID 4001 does not contain an explicit change, preferring to defer to the experts in TGmd, but it appears TGmd would like to see a proposal for an explicit change
  It is now proposed a change be made to the PIFS clause (10.3.2.3.4) that is relatively simple
    Making it clear that PIFS can be used for Beacons …
    … but also making clear that caution should be applied when doing so to avoid undue interference to other systems

## Slide 14: The proposed change to allow PFS for Beacons is limited to the PIFS clause
  10.3.2.3.4 PIFS
  The PIFS is used to gain priority access to the medium.
  The PIFS may be used as described in the following list and shall not be used otherwise:
  …
  A STA transmitting a Beacon frame, as described in 11.1.3.2 (Beacon generation in non-DMG infrastructure networks). The use of PIFS for Beacons should be used with caution, in particular by avoiding undue interference to other systems

## Slide 15: Change log
  R1: changed “illegally” to “ non-compliantly” on pp 2 & pp 12 because some members noted 802.11 is mostly not enforced by law