## Slide 1: MLO: Need for sync PPDUs
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
George Cherian | Qualcomm Inc. |  |  | 
Duncan Ho | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Date: 2020-03-15

## Slide 2: Overview
Several contributions [1 -14] have discussed the case where an MLD has constraints due to which it cannot be in transmit and receive state on two links simultaneously.
Some of the above contributions have also proposed channel access schemes to help mitigate the problem by having the device in Tx/Tx or Rx/Rx state.
Contributions [15] suggests that there isn't much performance impact if all transmissions are async and that no additional action is needed in the standard
This contribution continues the discussion on sync PPDU and provides simulation results which cover a broadcast set of use cases.

## Slide 3: Related Motions
[Motion 38]
  A MLD that supports multiple links can announce whether it can support transmission on one link concurrent with reception on the other link for each pair of links.
    NOTE 1 – The 2 links are on different channels.
    NOTE 2 – Whether to define a capability of announcing the support transmission on one link concurrent with transmission on the other link is TBD.
[Motion 46]
  802.11be shall allow a MLD that has constraints to simultaneously transmit and receive on a pair of links to operate over this pair of links.
    Signaling of these constraints is TBD.

## Slide 4: What is Sync PPDUs?
Two types, depending on regulatory rule
  PIFS access allowed. For fairness reasons, ED on 2nd link is checked at -72dBm
  PIFS access NOT allowed. Start times may be different. End time is aligned.
    This mode is possible for DL (assuming AP is STR capable)
    Not possible for UL, except for adding additional signaling
Additional terminologies described in appendix

## Slide 5: Motivation
Contribution [15] provides simulation results which imply that the 11be standard may not need to specify any rules for generating sync PPDU.
However, our analysis show that the use case considered in the above contribution is one specific case and leads to an inaccurate conclusion
We further show, with the aid simulation results, that a protocol without sync PPDU would have very poor performance when you consider a broad set of use cases.

## Slide 6: When does no sync PPDUs approach work
For cases involving DL-only traffic, the UL traffic is limited to short BA frames.
  The BA frames cause (short) self interference which would knock off a small portion of the DL on the other link
  Such loss (as shown in [15]) is ~10%.
Therefore async mode operation may work in such cases
  However, if the UL were to happen during the pre-amble of an upcoming DL on the other link, it can wipeout the entire DL.

## Slide 7: Pitfalls of no sync PPDUs
There is no such case as DL-only on traffic
  Even DL only TCP has TCP Acks that need to be sent in UL
Further, when there is bi-directional traffic, the UL traffic would wipeout a significant portion of the DL
  This would bring down the overall system throughput as the medium time for the lost DL is wasted
  UL transmission can lead to full DL loss if the DL’s pre-amble is hit
Therefore, DL aggregation is possible only when UL is not present

## Slide 8: Performance analysis w, w/o sync PPDUs
Simulation setup:
  Most basic case: Single non-AP MLD associated with an AP MLD
Configuration:
  AP is STR: Can perform simultaneous Tx/Rx
  Non-AP is Non-STR: Can’t perform simultaneous Tx/Rx
    Significant self-interference on second link when Tx-ing on first link
Simulator emulates a 100 second run
Traffic Model:
  DL only (with UL Ack): Full Buffer DL
  DL heavy (DL:UL = 3:1 ratio), Full buffer
  Bi-directional (DL:UL = 1:1), Full buffer
Objective: Compare performance between non-Sync PPDU and Sync PPDU (JMPC) schemes

## Slide 9: Scenarios compared
JMPC (sync PPDU)
  Multi-Primary with ED based aggregation
Non-sync mode 1 (N.Sync M1)
  Ignore DL state on other link and perform UL
    Loss of DL due interference from UL
  UL is blocked due to self-ACI when in UL state on another link
Non-sync mode 2 (N.Sync M2)
  Don’t perform UL when receiving DL on another link
  UL is blocked due to self-ACI when in UL state on another link
  Results in appendix

## Slide 10: Results
Aggregation gains disappear when there is bidirectional traffic
  Most of the medium time is wasted as an on-going DL is wiped out
  Will bring down the overall system throughput.
 | SL | JMPC | N.Sync M1
DL Only | 443 | 886 | 767
Gain w.r.t Single Link | - | 2x | 1.73x
DL:UL = 3:1 (DL heavy) | SL | JMPC | N.Sync M1
DL | 361 | 722 | 484
UL | 119 | 237 | 198
Total | 480 | 959 | 682
Gain w.r.t Single Link |  | 2x | 1.4x
DL:UL = 1:1 (Bi-directional) | SL | JMPC | N.Sync M1
DL | 240 | 480 | 240
UL | 240 | 480 | 324
Total | 480 | 960 | 564
Gain w.r.t Single Link |  | 2x | 1.18x
Results similar to the ones seen in [15]
Only 40% gains
Only 18% gains
* No UL opportunities with N.Sync M2
see additional results in appendix

## Slide 11: Analysis of the results

## Slide 12: Summary
We discuss the topic of supporting sync PPDUs in MLO design
  Provide simulation results and analysis showing the need to specify rules in the standard to support sync PPDUs when at least one MLD is non-STR
  Adding Sync PPDUs is critical for MLO gains during bi-directional traffic

## Slide 13: References
[1]: 11-19/1305: Synchronous Multi-link Operation (Yongho, MediaTek)
[2]: 11-19/1547 Multi-link-operation-and-channel-access-discussion (Kaiying, MediaTek)
[3]: 11-19/1548 channel access design for synchronized multi-links (Yunbo, Huawei)
[4]: 11-19/1550 Simultaneous Tx/Rx Capability indication for multi-link operation (Yifan, Huawei)
[5]: 11-19/1574 Multi-Link-Auxiliary-Link (Matthew, Broadcom)
[6]: 11-19/1633 Performance and Fairness of Multi-link Operations (Wisnu, SeoulTech)
[7]: 11-19/1678 Multiple Links Asynchronous and Synchronous Transmission (Alan, Unisoc)
[8]: 11-19/1916 MLO-Asynch-Qsynch-Synch (Matthew, Broadcom)
[9]: 11-19/1993 Discussion about single and multiple primary channels in synchronous multi-link (Yunbo, Huawei)
[10]: 11-20/0014 Operation of Non-AP MLD with Constraints (Insun, LGE)
[11]: 11-20/0026 MLO: Sync PPDUs (Duncan, Qualcomm)
[12]: 11-20/0081 MLO-Synch-Transmission (Matthew, Broadcom)
[13]: 11-20/0082 Synchronous-Transmitter-Medium-State-Information (Matthew, Broadcom)
[14] 11-20/0134 Multilink channel access considering STR capability (Hanseul, Yonsei Univ)
[15] 11-20/0106 Follow up on performance aspects of mlink ops with constrains (Dmitry, Intel)
[16]: 11-19-1262 Specification Framework for TGbe

## Slide 14: Appendix

## Slide 15: Simulation Results
 | JMPC DL-only | NSM1 DL-only | NSM2 DL-only | JMPC Bi-Dir asym. (75/25) | NSM1 Bi-Dir asym. (75/25) | NSM2 Bi-Dir aysm. (75/25) | JMPC Bi-Dir FB (100/100) | NSM1 Bi-Dir FB (100/100) | NSM2 Bi-Dir FB (100/100)
DL Mbps | 886 | 767 | 943 | 722 | 484 | 821 | 480 | 240 | 822
UL Mbps | 73 (BA) | 69 (BA) | 0 | 237 | 198 | 0 | 480 | 324 | 0
Back

## Slide 16: Terminology
STR (simultaneous Tx and Rx)
  An MLD that is capable of simultaneous Tx/Rx on multiple links even when the links are near band
Non-STR
  An MLD that is not capable of simultaneous Tx/Rx on multiple links when the links are near band
    i.e., it can only do Tx/Tx or Rx/Rx on all links
Sync PPDUs
  Two PPDUs that are transmitted from two STAs of a Tx-ing MLD such that:
    The end time of the PPDUs are within SIFS of each other
    The start time of the PPDUs may or may not be within SIFS of each other (depending on if PIFS access is allowed on the second link)