## Slide 1: MLO Typical Usage Cases and Sub-Feature Prioritization
Date: 2020-01-20
Authors:
Name | Affiliations | Address | Phone | Email
Zhou Lan | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | zhou.lan@broadcom.com
Albert Bredewoud |  |  |  | 
George Kondylis |  |  |  | 
Matthew Fischer |  |  |  | 
Notes: September 2012

## Slide 2: Summary
This contribution discusses the MLO typical operation scenarios and proposes MLO sub-feature prioritization

## Slide 3: Today
  Today, AP with 4x4 antenna, STA with 2x2 antenna become mainstream devices on the market
  Most of APs support bandwidth 160 MHz, a few STAs support bandwidth 160 MHz
  Dual/Tri-band APs are available
    E.g. 2.4GHz+5GHz(low)+5GHz(high)
    Each band establishes its own BSS and operates independently
      i.e. each band supports “aysnc.” mode without coordination (no sync. mode)
      Two 5 GHz radios can be configured to operate on the same channel sharing the same bandwidth
    Peak system throughput (SU or MU) on one 5GHz reaches 2.4Gbps (160MHz, 2SS, 1024QAM)
    Throughput can not be aggregated across BSSs (i.e. across links)
      Some proprietary implementation may support link aggregation, but there is no standard specified to guarantee the interoperability

## Slide 4: One baby step towards real MLO
  802.11be decides to supports 240/320 MHz bandwidth and 4K QAM
  Per the current timeline (D1.0 ready @May 2021), it is realistic to assume STA may only support 2 or less antennas
  Peak throughput on each link: 4.3 Gbps@5GHz (2SS, 240 MHz, 4K QAM) and 5.7 Gbps@6GHz (2SS, 320 MHz, 4K QAM)
  By defining a mechanism to support multiple links operating in a single BSS boosts the system throughput to 10 Gbps (4.3+5.7)
    Call this mode of MLO operation as flow level aggregation in this presentation
      No intention to propose such terminology in 11BE spec
    10 Gbps throughput is shared by multiple applications (i.e. multiple ACs, multiple TIDs), which should be sufficient to cover all the current and near future usage cases (e.g. AR/VR, HD Video Streaming)
    Example operation
      MLO association
      Each TID maps to a single link
      BA agreement on MLD level
      No simultaneous outstanding MPDUs (i.e. MPDUs that are not ACKed) on multiple links

## Slide 5: Single TID split across links
  802.11be decides to support a MLO mode that can split single TID QoS data to multiple available links
    There can be outstanding MPDUs on multiple available links at the same time
    Call this mode of MLO operation as packet level aggregation in this presentation
    Packet level aggregation offers single TID throughput gain
    Packet level aggregation also offers latency gain on both DL and UL[1] [2]
      E.g. 2.4 + 5/6 concurrent operation provides more channel access opportunities

## Slide 6: Pursuing peak system throughput
  The main role of MLO should be boosting system throughput to reach the maximum PHY capability, which is difficult to be achieved with SU operation
  DL MU MIMO + MLO boosts the system throughput to 20 Gbps
    8.6 Gbps @ 5GHz (4SS, 240 MHz, 4K QAM)
    11.4 Gbps @ 6GHz (4SS, 320 MHz, 4K QAM)
  Packet level aggregation is complimentary to the MU operation for latency improvement, however has implementation implication of complicated queue management etc.

## Slide 7: Device Type
EHT AP MLD:
  STR AP MLD
  Non STR AP MLD (TBD)
EHT non AP MLD:
  STR Multi Radio/Link non AP MLD (e.g. a non AP MLD with 2.4 + 5/6 GHz Radios)
  Non STR Multi Radio/Link non AP MLD (e.g. a non AP MLD with 5 + 6 GHz Radios)
  Single Radio/Link non AP MLD
  Enhanced Single Radio/Link non AP MLD [3]

## Slide 8: Mode of operation
  For multi Radio/Link non AP MLD
  For single Radio/Link non AP MLD
Down/Up Link | STR AP MLD TX/RX
Single Radio/link non AP MLD TX/RX | R1
Enhanced Single Radio/Link non AP MLD TX/RX | R1
Down Link | STR AP MLD full Async. TX | STR AP MLD TX (ending time alignment) | STR AP MLD TX (start and end time alignment)
Multi Radio STR Non AP MLD RX | R1-Note there is no extra rule need to be defined | Not relavent | Not relevant
Multi Radio Non STR Non AP MLD RX | R1-Note there is no extra rule need to be defined | R1 | R1
Up Link | Multi Radio STR non AP MLD full Async. TX | Multi Radio non STR non AP MLD TX (start and end time alignment)
STR AP MLD RX | R1-Note there is no extra rule need to be defined | R1

## Slide 9: Straw poll 1
  Do you agree the following mode of MLO operations are in 11be R1 sub-features? Other mode of operation is TBD (e.g. mode to support NSTR AP)
    Yes No Abstain
Down Link | STR AP MLD full Async. TX | STR AP MLD TX (ending time alignment) | STR AP MLD TX (start and end time alignment)
Multi Radio STR Non AP MLD RX | R1-Note there is no extra rule need to be defined | Not relavent | Not relevant
Multi Radio Non STR Non AP MLD RX | R1-Note there is no extra rule need to be defined | R1 | R1
Up Link | Multi Radio STR non AP MLD full Async. TX | Multi Radio non STR non AP MLD TX (start and end time alignment)
STR AP MLD RX | R1-Note there is no extra rule need to be defined | R1
Down/Up Link | STR AP MLD TX/RX
Single Radio/link non AP MLD TX/RX | R1
Enhanced Single Radio/Link non AP MLD TX/RX | R1

## Slide 10: Reference
https://mentor.ieee.org/802.11/dcn/20/11-20-0026-06-00be-mlo-sync-ppdus.pptx , Duncan Ho etc. (Qualcomm)
https://mentor.ieee.org/802.11/dcn/20/11-20-0106-04-00be-follow-up-on-performance-aspects-of-mlink-ops-with-constrains.pptx, Dmitry Akhmetov etc. (Intel)
https://mentor.ieee.org/802.11/dcn/20/11-20-0562-03-00be-enhanced-multi-link-single-radio-operation.pptx, Minyoung Park etc. (Intel)