## Slide 1: Agenda for IEEE 802.11 Coexistence SC meeting in Atlanta in March 2020
26 February 2019
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com
Meeting cancelled – the material in this deck is draft for information only

## Slide 2: Welcome to the 17th F2F meeting of the Coex SC in Atlanta in March 2020
  The IEEE 802.11 PDED ad hoc was formed in September 2016 at the Warsaw interim meeting
  The IEEE 802.11 PDED ad hoc met in San Antonio (Nov 2016), Atlanta (Jan 2017), Vancouver (Mar 2017) and Daejeon (May 2017)
  In Daejeon in May 2017 it was decided to convert the IEEE 802.11 PDED ad hoc into the IEEE 802.11 Coexistence SC
  The IEEE 802.11 Coexistence SC met in Berlin (July 2017), Hawaii (Sept 2017), Orlando (Nov 2017), Irvine (Jan 2018), Chicago (Mar 2018), Warsaw (May 2018), San Diego (July 2018), Hawaii (Sept 2018), Bangkok (Nov 2018), St Louis (Jan 2019), Vancouver (Mar 2019), Atlanta (May 2019), Vienna (Jul 2019), Hanoi (Sep 2019), Hawaii (Nov 2019) & Irvine (Jan 2020)

## Slide 3: Coex SC minutes today will be kept by our permanent SC secretary
  It is important to keep proper minutes of all Coexistence SC meetings
  Fortunately, Guido Hiertz (Ericsson) agreed in Berlin (in July 2017) to be appointed the IEEE 802.11 Coexistence SC’s permanent Secretary …

## Slide 4: Meetings shall be conducted in compliance with all applicable laws, including antitrust & competition laws
  Don’t discuss the interpretation, validity, or essentiality of patents/patent claims
  Don’t discuss specific license rates, terms, or conditions
    Relative costs of different technical approaches that include relative costs of patent licensing terms may be discussed in standards development meetings
      Technical considerations remain the primary focus
  Don’t discuss or engage in the fixing of product prices, allocation of customers, or division of sales markets
  Don’t discuss the status or substance of ongoing or threatened litigation
  Don’t be silent if inappropriate topics are discussed … do formally object
  For more details, see IEEE-SA Standards Board Ops Man, 5.3.10 and Antitrust and Competition Policy: What You Need to Know available here
  If you have questions, contact the IEEE-SA Standards Board Patent Committee Administrator at patcom@ieee.org
Approved slide

## Slide 5: Participant behavior in IEEE-SA activities is guided by the IEEE Codes of Ethics & Conduct
  All participants in IEEE-SA activities are expected to adhere to the core principles underlying the:
    IEEE Code of Ethics
    IEEE Code of Conduct
  The core principles of the IEEE Codes of Ethics & Conduct are to:
    Uphold the highest standards of integrity, responsible behavior, and ethical and professional conduct
    Treat people fairly and with respect, to not engage in harassment, discrimination, or retaliation, and to protect people's privacy.
    Avoid injuring others, their property, reputation, or employment by false or malicious action
  The most recent versions of these Codes are available at
    http://www.ieee.org/about/corporate/governance
Approved slide

## Slide 6: Participants in the IEEE-SA “individual process” shall act independently of others, including employers
  The IEEE-SA Standards Board Bylaws require that “participants in the IEEE standards development individual process shall act based on their qualifications and experience”
  This means participants:
    Shall act & vote based on their personal & independent opinions derived from their expertise, knowledge, and qualifications
    Shall not act or vote based on any obligation to or any direction from any other person or organization, including an employer or client, regardless of any external commitments, agreements, contracts, or orders
    Shall not direct the actions or votes of other participants or retaliate against other participants for fulfilling their responsibility to act & vote based on their personal & independently developed opinions
  By participating in standards activities using the “individual process”, you are deemed to accept these requirements; if you are unable to satisfy these requirements then you shall immediately cease any participation
Approved slide

## Slide 7: IEEE-SA standards activities shall allow the fair & equitable consideration of all viewpoints
  The IEEE-SA Standards Board Bylaws (clause 5.2.1.3) specifies that “the standards development process shall not be dominated by any single interest category, individual, or organization”
    This means no participant may exercise “authority, leadership, or influence by reason of superior leverage, strength, or representation to the exclusion of fair and equitable consideration of other viewpoints” or “to hinder the progress of the standards development activity”
  This rule applies equally to those participating in a standards development project and to that project’s leadership group
  Any person who reasonably suspects that dominance is occurring in a standards development project is encouraged to bring the issue to the attention of the Standards Committee or the project’s IEEE-SA Program Manager
Approved slide

## Slide 8: IEEE SA Copyright Policy
  By participating in this activity, you agree to comply with the IEEE Code of Ethics, all applicable laws, and all IEEE policies and procedures including, but not limited to, the IEEE SA Copyright Policy.
    Previously Published material (copyright assertion indicated) shall not be presented/submitted to the Working Group nor incorporated into a Working Group draft unless permission is granted.
    Prior to presentation or submission, you shall notify the Working Group Chair of previously Published material and should assist the Chair in obtaining copyright permission acceptable to IEEE SA.
    For material that is not previously Published, IEEE is automatically granted a license to use any material that is presented or submitted.
Approved slide

## Slide 9: IEEE SA Copyright Policy
  The IEEE SA Copyright Policy is described in the IEEE SA Standards Board Bylaws and IEEE SA Standards Board Operations Manual
    IEEE SA Copyright Policy, see:
      Clause 7 of the IEEE SA Standards Board Bylaws
      Clause 6.1 of the IEEE SA Standards Board Operations Manual
  IEEE SA Copyright Permission
  IEEE SA Copyright FAQs
  IEEE SA Best Practices for IEEE Standards Development
  Distribution of Draft Standards (see Clause 6.1.3 of the SASB Operations Manual)
Approved slide

## Slide 10: The Coex SC will meet twice during the Atlanta meeting in March 2020
 | Mon | Tue | Wed | Thu | Fri
AM1 |  |  |  |  | Closing
AM2 |  |  |  |  | 
PM1 |  |  | COEX SC | COEX SC (motions) | 
PM2 |  |  |  |  | 
EV1 |  |  | Social |  | 

## Slide 11: The Coex SC will consider a proposed agenda for Atlanta in March 2020
Proposed Agenda
  Bureaucratic stuff
    Scope of IEEE 802.11 Coexistence SC (a reminder)
    Approve minutes
  What is happening this week? (in no particular order)
    Update of unlicensed LTE deployment
    Review of “important issues”
    …

## Slide 12: The Coex SC will consider a proposed agenda for Atlanta in March 2020
Proposed Agenda
    Review of recent ETSI BRAN activities
      EN 301 893 issues (5 GHz)
      EN 303 687 issues (6 GHz)
    Possible LS to ETSI BRAN
    Review of recent 3GPP RAN/RAN1 activities
    Review of recent WBA activities
    Discussion of extension of Coex SC charter
    Plans for next meeting
  Other business

## Slide 13
  Scope of IEEE 802.11 Coexistence SC

## Slide 14: The agreed Coex SC scope focuses on ensuring 802.11ax has fair access to global unlicensed spectrum
Discuss the use of PD, ED or other 802.11 coexistence mechanisms with the goal of promoting “fair” use of unlicensed spectrum
Promote an environment that allow IEEE 802.11ax “fair access” to global unlicensed spectrum
Will initially focus on liaising with 3GPP RAN/RAN1/RAN4 but may also lead to interactions with regulators and other stakeholders
Will probably not conclude at least until RAN4’s 802.11/LAA coexistence testing is defined and successfully executed
May require the SC to consider other simulations and results of tests of potential LAA/802.11 coexistence mechanisms
Will initially focus on encouraging a “technology neutral” solution in the next revision of EN 301 893 that allows IEEE 802.11ax fair access to unlicensed spectrum in Europe (noting the European approach is likely to have global impact)
The effort will also focus on allowing 802.11ax to use innovative mechanisms for frequency reuse without compromising the goal of fair access

## Slide 15: Coex SC will close when determined by the 802.11 WG or 802.11ax is ratified
IEEE 802.11 Coexistence SC close down criteria
  The SC is closed by the IEEE 802.11 WG
    … after it is determined that the SC is unlikely to make further progress towards its goals
  IEEE 802.11ax completes Sponsor Ballot
    … noting that the Coexistence SC ad hoc is unlikely to be relevant at that point anyway

## Slide 16
  Minutes

## Slide 17: The Coex SC will consider approval of its meeting minutes from Irvine in Jan 2020
  The minutes for the Coex SC at the Irvine meeting in Jan 2020 are available on Mentor:
    See 11-20-0334-01
    R1 corrects voting result (from 3/4/10 to 5/4/10) and minor editorials
  Motion:
    The IEEE 802 Coex SC approves 11-20-0334-01 as minutes of its meeting in Irvine in Jan 2020
    Moved:
    Seconded:
    Result:

## Slide 18
  Agenda items
  Unlicensed LTE deployment

## Slide 19: Latest stats confirm that there is some interest in LAA, suggesting good coexistence may be important
Tech-nology | Stage | GSMA1 (July 2018) | GSA2 (Oct 2018) | GSA3 (Jan 2019) | GSA4 (Jul 2019) | GSA5 (Nov 2019) | GSA6 (Dec 2019)
LAA | Planned | 23 | 22 | 26 | 29 | 30 | 29
 | Deployed | 4 | 6 | 6 | 8 | 8 | 8
eLAA | Planned | ? | 1 | 1 | 1 | 1 | ?
 | Deployed | ? | 0 | 0 | 0 | 0 | ?
LWA | Planned | ? | 2 | 2 | 2 | 2 | 2
 | Deployed | ? | 1 | 1 | 1 | 1 | 1
LTE-U | Planned | ? | 8 | 8 | 8 | 8 | 9
 | Deployed | ? | 3 | 3 | 3 | 3 | 3
1 GSMA (July 2018)
2 GSA: Evolution from LTE to 5G: Global Market Status (Nov 2018)
3 GSA: LTE in unlicensed and shared spectrum (Jan 2019)
4 GSA: Evolution from LTE to 5G: Global Market Status (Aug 2019)
5 GSA: LTE Unlicensed - LTE in Unlicensed and Shared Spectrum (Nov 2019)
6 GSA: LTE and 5G Market Statistics (Dec 2019)

## Slide 20: The number planned/testing and deployed LAA networks is slowly increasing (mostly!)
Chart: Globally planned/testing & deployed LAA networks
| 43282 | 43374 | 43466 | 43647 | 43770 | 43800
Planned, testing | 23 | 22 | 26 | 29 | 30 | 29
Deployed | 4 | 6 | 6 | 8 | 8 | 8

## Slide 21
  Agenda items
  Important issues?

## Slide 22: WBA & post workshop surveys will guide the SC on the importance of various coexistence issues
Chart: 
| Use of 802.11 preambles or common preambles for coexistence | Energy Detection only vs. Preamble or Energy Detection vs. both | Multi-channel sharing mechanisms | Use of no/short LBT for control signaling | Blocking energy/reservation signals | Synchronous access proposals in U-NII-7 | Contention Window adjustment mechanisms with delayed acknowledgements | Something else | Don't know | None of these | Prefer not to say
Post workshop survey | 0.57143 | 0.55556 | 0.31746 | 0.38095 | 0.30159 | 0.1746 | 0.2381 | 0.063492 | 0.063492 | 0.031746 | 0.095238
WBA survey | 0.5 | 0.36 | 0.36 | 0.22 | 0.1 | 0.08 | 0.04
Qualcomm proposal to ETSI BRAN & FCC
Follow up on LS to ETSI BRAN
Postponed for future discussion
(part of CW adjustment)
Discussed recently in BRAN
Issue resolved (see later for 11md update)
Most discussion

## Slide 23
  Relationship topics
  ETSI BRAN activities

## Slide 24: ETSI BRAN is currently discussing various technical issues of interest to the Coex SC
Open technical issues in ETSI BRAN
  EN 301 893 (5 GHz)
    What is a preamble?
    Contention Window update
    Technology neutrality
    Use of short LBT in multi-channel
    Use of PD/ED and ED-only modes
    Spectral Mask
  EN 303 687 (6 GHz)
    ED Threshold (EDT) in 6 GHz
    Technology neutrality

## Slide 25
  Relationship topics
  EN 301 893
  What is a preamble?

## Slide 26: The definition and testing of PD continues to be controversial
Executive summary
  The definition of a common preamble for EN 303 687 continued to be an issue at BRAN#104
  At BRAN#104, Broadcom & Qualcomm reported on testing of a possible common preamble
  At BRAN#104, Ericsson used the “broken” preamble to assert PD/ED shouldn’t be used in 6 GHz
  BRAN#104 highlighted at least some agreement during an ad hoc on PD
  The Wi-Fi community still have an opportunity to select a common preamble aligned with Wi-Fi practice
  The BRAN#104d teleconference did not reach consensus of how PD should be documented or tested

## Slide 27: The definition of a common preamble for EN 303 687 continued to be an issue at BRAN#104
Documents on preamble from BRAN#104
  BRAN(19)104008: Preamble Detection Update (Broadcom & Qualcomm)
  BRAN(19)104009: Preamble Detection issues (Ericsson)
  BRAN(19)104031: Results of ad-hoc meeting on PD
Summary of discussion on preamble from BRAN#104
  In BRAN#103 it was discovered that the 20 µs 802.11a preamble was insufficient to trigger PD on many Wi-Fi implementations
    This was a surprise to many in the Wi-Fi community
    This would have been a real problem if 3GPP RAN1 had adopted the 802.11a preamble – fortunately they didn’t! 
  BRAN#104 spent some time discussing the implications, including in an ad hoc session, with some consensus but also some ongoing contention

## Slide 28: At BRAN#104, Broadcom & Qualcomm reported on testing of a possible common preamble
Summary of BRAN(19)104008 (Broadcom & Qualcomm)
  BRAN(19)104008 followed on from the successful initial preamble detection testing using a possible PD test signal & methodology previously detailed in BRAN(19)103035r2
  Broadcom & Qualcomm proposed a possible PD test signal (common preamble) with total duration of 1 ms
    Comprising an 802.11a OFDM header (STF/LTF/L-SIG)
    Followed by two BPSK symbols with random data
    Followed by AWGN, followed by a SIFS gap
  A continuous test signal would be used to check that it effectively blocked the channel
  They reported that testing was taking place to clarify this interpretation of the preamble is workable
    At the time, all the results were positive

## Slide 29: At BRAN#104, Ericsson used the “broken” preamble to assert PD/ED shouldn’t be used in 6 GHz
Summary of BRAN(19)104009 (Ericsson)
  Based on a legalistic analysis of the 802.11 standard, Ericsson concluded that a 20 µs 802.11a preamble should work
    Note: there was disagreement from some in relation to Ericsson’s legalistic interpretation; 802.11 is not well enough written to be analysed in this way 
  Ericsson also claimed that 20 µs 802.11a preamble should work based on quotes in 3GPP submissions from Intel, Broadcom, Apple & Cisco
    Note: these companies have also since agreed that they were incorrect in their understanding of the preamble
  Ericsson then claimed that PD should not be used in 6 GHz because the 20 µs 802.11a preamble did not work as expected
    Despite the fact no one has been affected by the misunderstanding
  However, Ericsson stated they are prepared to give 802.11a/n/ac/ax an “exception” in 5 GHz, as long as only ED-only is applied to 6 GHz

## Slide 30: BRAN#104 highlighted at least some agreement during an ad hoc on PD
Summary of BRAN(19)104031 (ad hoc on PD)
  The disagreement abut the various issues during the formal BRAN sessions led to the formation of an ad hoc, led by a Cablelabs employee
  There was consensus in the ad hoc that a preamble for the PD test in EN 301 893 should be based on Fig. 17.4 in clause 17.3.3 of IEEE 802.11-2016
    Short Training Symbol
    Long Training Symbol
    SIGNAL field (rate @ 6Mb/s)
    DATA 1 symbol (BPSK)
    DATA 2 symbol (BPSK)
  Note: since the ad hoc, Fig. 17.4 has been refined by TGmd to make it clearer the preamble includes the two data sytmbols
  …

## Slide 31: Fig 17.4 has been refined by TGmd to make it clearer the preamble includes the two data sytmbols
Old
New
Cut off
Not cut off

## Slide 32: BRAN#104 highlighted at least some agreement during an ad hoc on PD
Summary of BRAN(19)104031 (ad hoc on PD)
  …
  Various stakeholders wanted to try:
    Length set to 1ms with AGWN (proposed by Broadcom & Qualcomm)
    Length set to 1ms with no AGWN (proposed by Ericsson/Nokia)
      Note: this is not a very realistic signal
    Length set to 32us with AGWN (very short) (proposed by Ericsson/Nokia)
      Note: it is not clear why this is important to Ericsson/Nokia
  It is planned that BRAN#105 will decide on the appropriate test signal, according to most common intended behavior of legacy devices
  There was also some ongoing contetion about whether EN 301 893 can reference the 802.11 standard that will also need to be resolved in BRAN#105

## Slide 33: The Wi-Fi community still have an opportunity to select a common preamble aligned with Wi-Fi practice
Discussion of preamble for PD
  The discovery that the 20 µs 802.11a preamble was insufficient for PD was a big surprise to many
  It would have been a real problem if 3GPP had adopted the previous interpretation of a preamble ... but they didn’t
    It was explicitly decided in RAN to not adopt PD
  Therefore, it is still reasonable for ETSI BRAN to choose a preamble for PD that is compatible with:
    current Wi-Fi practice for preambles in 5 GHz
    the well established Wi-Fi plans for preambles in 6 GHz

## Slide 34: The BRAN#104d teleconference did not reach consensus of how PD should be documented or tested
Documents on preamble from BRAN#104d teleconference
  BRAN(20)104d002r2: Agenda & document list
  BRAN(19)104d004: Results of ad-hoc meeting on PD
  BRAN(20)104d003: PD Signal Testing (Broadcom)
  BRAN(20)104d001: Response to BRAN(20)104d003 (Ericsson)
Summary of documents on preamble at BRAN#104d teleconference
  The discussion of these documents focused on
    How PD operation is documented in EN 301 893
    How PD is tested in EN 301 893
  There was consensus that PD should be properly documented & tested,
  However, opposition from Ericsson meant there was not consensus on the details

## Slide 35: Broadcom suggested a clarification of PD in EN 301 893 and a single realistic test signal
Summary of BRAN(20)104d003 (Broadcom)
  Broadcom noted that the reference to PD in EN 301 893 could beeasily clarified with an appendix that better described how PD is used to determine a channel is occupied
    They later volunteered to bring a proposal to BRAN#105; Ericsson objected to work on an appendix until more testing is completed
  Broadcom also supported some sort of [90%] detection criteria test, but asserted there was no need to test the 4 us criteria for detecting energy
  Broadcom recommended the use of signal i) to test PD
    i) 1 ms packet with 28 us preamble plus AGWN worked as a test signal for APs and clients
    ii) 1ms packet with 28 us preamble with no additional energy does not work to test PD, because most devices reasonably consider it be an unrealistic signal
    iii) 32 us packet with 28 us preamble plus AGWN worked the same as i) and so is unnecessary, particularly as not clear what it is testing

## Slide 36: Ericsson objected to the use of PD for adaptivity, using a menagerie of objections
Summary of BRAN(20)104d001 (Ericsson)
  It is difficult to characterize Ericsson’s comments, commenting on various aspects of Broadcom’s submission, except that it was clear Ericsson still objects to the use of PD for adaptivity
  A number of participants commented that Ericsson focused on a series of “edge conditions” with the purpose of “backing Wi-Fi into a corner”
    eg, they insist on treating the length in a preamble as a PHY layer NAV, despite this not being its function
    eg, they insist on testing minor aspects of 802.11 such as detection within 4 us, despite this feature being mostly irrelevant to coexistence
    eg, they objected to further work by Broadcom to documents the use of PD until some unspecified but large amount of testing was completed
    eg, they continue to want the use of PD to be characterised as an “exception”, only available to Wi-Fi, and only in the 5 GHz band
    eg, they made some incorrect analogies between DFS and PD testing

## Slide 37: The discussion in BRAN#104d highlighted that Ericsson disagrees with other participants
Discussion on preamble at BRAN#104d teleconference
  There was an extended discussion, in which everyone who spoke disagreed with Ericsson; some on the call did not speak
  One participant summarised the PD situation as follows:
    Sadly, the use of PD has been mis-described (by Wi-Fi industry) & misunderstood (by Ericsson et al)
    This would have been a major problem if any technology other than Wi-Fi had adopted PD; but none have!
    The reality is that we know PD works in practice after 20 years of experience
    The remaining challenge is to document how it works so it can be used by all (in an appendix) and test it appropriately (with as little testing as possible)
  Another participant from Qualcomm noted the urgency of completing EN 301 893, otherwise products will be placed on the market using Notified Bodies, not necessary fulfilling all the important requirements

## Slide 38: There will be a submission defining PD and its testing at BRAN#105
Likely next steps on preamble at BRAN#105
  It is expected that Broadcom & Qualcomm will submit further test results showing that test signal i) works with APs and clients
    It is possible that Ericsson may submit further test results too; apparently thye have sent 6 Wi-Fi devices to R&S for testing
  Broadcom will lead and effort to write an appendix that clarifies the use of PD so that it can be used by any technology, and not just Wi-Fi

## Slide 39
  Relationship topics
  EN 301 893
  Contention Window

## Slide 40: The CW adjustment issue is still open
Executive summary
  BRAN#104 did not make much progress in relation to CW adjustment text in EN 301 893 (or EN 303 687)
  At BRAN#104b the CW adjustment text was accepted into EN 301 893 but is still open for discussion
  There are no known plans to discuss the CW adjustment requirements in BRAN#105

## Slide 41: BRAN#104 did not make much progress in relation to CW adjustment text in EN 301 893 (or EN 303 687)
Documents on CW from BRAN#104
  BRAN(19)104021: ETSI BRAN – Response to LS re: Contention Window Update in Initiating Device Channel Access (IEEE 802.11 WG)
Summary of discussion on CW from BRAN#104
  After BRAN#103, ETSI BRAN sent a LS to IEEE 802.11 WG and 3GPP notifying them of the proposed CW adjustment text, which enabled:
    Broadcasts explicitly
    Delayed acks (mostly not relevant to 802.11 because of deprecation of delayed acks on TGmd, but of great relevance to LAA/NR-U)
  IEEE 802.11 WG responded before BRAN #104 that the proposal was acceptable
  …

## Slide 42: At BRAN#104b the CW adjustment text was accepted into EN 301 893 but is still open for discussion
  …
  3GPP RAN1 was apparently planning to respond in Feb 2020, but that plan may be delayed because their February meeting was changed into an e-mail only meeting
    It has been reported that some 3GPP RAN1 participants are concerned about the “no bias” language that means that a random selection of feedback must be used rather than a biased selection that results in more CW resets
  The CW adjustment text was accepted into the latest draft of EN 301 893 during the BRAN104b teleconference (in early Feb 2020) based on the documented consensus on the topic in BRAN#103
  However, it was made very clear during the teleconference that the topic is still open for further discussion …

## Slide 43: There are no known plans to discuss the CW adjustment requirements in BRAN#105
  The progress on the CW adjustment requirements will depend on any liaison response from 3GPP RAN1
  There are no plans to discussion the CW adjustment requirements at BRAN#105 at this time

## Slide 44
  Relationship topics
  EN 301 893
  No/short LBT for short control signalling

## Slide 45: The no/short LBT for SCS issue is closed with most recent TGmd agreement
Executive summary
  At BRAN#104, Cisco announced the withdrawal of the proposal to constrain use of no/short LBT for SCS
  TGmd have agreed to explicitly allow the use of PIFS for Beacons, reflecting implementation reality

## Slide 46: At BRAN#104, Cisco announced the withdrawal of the proposal to constrain use of no/short LBT for SCS
Documents on short LBT from BRAN#104
  BRAN(19)104013: Short LBT update (Cisco)
Summary of discussion on short LBT from BRAN#104
  BRAN(19)104013 (Cisco) stated the proposal to constrain the use of no/short LBT for short control signaling (SCS) had been withdrawn
  The proposal was withdrawn because it is unlikely there would ever be sufficient support in ETSI BRAN, rather than it not being appropriate
      LAA/NR-U use the full 5% in many cases
      As do many Wi-Fi stakeholders when they use PIFS for Beacons, albeit contrary to the 802.11 standard
  There were complaints that many hours were wasted in 3GPP, ETSI BRAN and IEEE 802.11 WG discussing the issue
    The response from Cisco was that the problem was that there was not support for the proposal, not that it was not the right thing to do!

## Slide 47: TGmd have agreed to explicitly allow the use of PIFS for Beacons, reflecting implementation reality
Discussion on the use of short LBT for Beacons in TGmd
  A submission was made to the recent ballot on 802.11md asking that the standard explicitly allow the use of PIFS for Beacons, given that is what some/many vendors already do at least some of the time
  It is reported that TGmd have agreed to do so, along with a note warning about the overuse of PIFS
    Adding to the list of PIFS uses:
        –A STA transmitting a Beacon frame, as described in 11.1.3.2 (Beacon generation in non-DMG infrastructure networks).
    Note warning about use of PIFS generally:
        NOTE–An extended period during which the medium is busy after the TBTT can increase the probability for collisions between PIFS transmissions from nearby STAs on the same channel. The use of a random backoff instead of PIFS can reduce the collision probability in this case."

## Slide 48
  Relationship topics
  EN 301 893
  User setting of PD/ED thresholds

## Slide 49: There will be further discussion in BRAN#105 on the need to require devices to follow the threshold rules
Executive summary of BRAN#104b teleconference
  During BRAN#104b, Ericsson highlighted a potential issue with users modifying PD/ED thresholds
  During BRAN#104b, Ericsson proposed constraints on users modifying PD/ED thresholds
  During BRAN#104b, there was general support for Ericsson’s proposal wrt PD/ED thresholds
  There will be further discussion in BRAN#105 on the need to require devices to follow the threshold rules

## Slide 50: During BRAN#104b, Ericsson highlighted a potential issue with users modifying PD/ED thresholds
  During the BRAN#104b teleconference on 6 February 2020, Ericsson presented BRAN(19)104b002: Legacy PD Issues
  Ericsson noted that some AP vendors provide a feature to their users whereby the users can effectively modify the PDT
    Ericsson noted that the purpose of allowing modification of the PDT is to refine performance in specific high density situations
    While Ericsson did not identify the AP vendors, some simple googling indicates the three cited examples are Cisco, Meraki and Huawei
  Ericsson then highlighted simulation results that showed increasing the PDT can degrade performance
    Ericsson’s simulation results only apply to the simulated scenario; if they were generally correct this discussion would be moot because Ericsson’s simulations show both the victim and aggressor suffer with higher PDT’s in this scenario
    Ericsson noted vendors usually warn that misuse of this capability comes with the risk of degraded performance in some cases

## Slide 51: During BRAN#104b, Ericsson proposed constraints on users modifying PD/ED thresholds
  Ericsson concluded that EN 301 803 should constrain users in the way they modify any thresholds
    Proposal: User access restrictions clause (§4.2.9) should restrict devices from setting the absolute ED/PD threshold values above what is specified in §4.2.7.
  Ericsson then suggested specific text for inclusion in EN 301 893
    The equipment shall be so constructed that settings (hardware and/or software) related to Adaptivity, in particular ED and PD thresholds shall not be accessible to the user if changing those settings result in the equipment no longer being compliant with the Adaptivity requirements in clause 4.2.7.

## Slide 52: During BRAN#104b, there was general support for Ericsson’s proposal wrt PD/ED thresholds
  During BRAN#104b, a number of participants indicated in-principle support for constraining modification of PD/ED thresholds in a way that caused devices to not be compliant with EN 301 893 requirements
  Cisco et al noted that in those situations where it was appropriate to increase the PDT above -82 dBm, the device would transition to the ED-only mode with a lower EDT, thus maintaining compliance with EN 301 893 requirements
    On hearing this, Ericsson pivoted their argument to assert frequent flipping from mode to mode could cause a problem
  Qualcomm noted that there was no risk of this mode switching mechanism being misused because a mode switch between PD/ED & ED-only modes is only allowed every 60 s, which is sufficiently long to effectively block any misuse
    At this point it was unclear if Ericsson still supported their own proposal given it could not longer be used to promote an effective ban on PD/ED

## Slide 53: There will be further discussion in BRAN#105 on the need to require devices to follow the threshold rules
  At least one submission has been made to BRAN#105 on this topic
    See BRAN(20)105aaa: User setting of thresholds (Cisco) in which Cisco states it supports Ericsson’s proposal
  The discussion and any conclusions in BRAN#105 will be documented for the Coex SC meeting in May 2020 (Warsaw)

## Slide 54
  Relationship topics
  EN 301 893
  Multi-channel short LBT

## Slide 55: The Coex SC will hear and discuss a proposal in ETSI BRAN to restrict the use of multi-channel
Executive summary
  During the BRAN#104b teleconference …
  ... a proposal to modify the use of 25 µs LBT wrt multi-channel access in EN 301 893 was raised by Ericsson and discussed
  The following slides, adapted from BRAN(20)105xxx (Cisco) …
  … summarise the discussion and provide one (biased) perspective
  They are included in this deck as an easy way of making the Coex SC aware of the substance of the discussions …
  … which ultimately could result in restrictions in Europe on the use of Wi-Fi’s current multi-channel access mechanisms
  The Coex SC will discuss the impact of Ericsson’s proposal in ETSI BRAN on multi-channel access

## Slide 56: ETSI BRAN needs to enable progress by maintaining the 25 µs LBT status quo in EN 301 893
Executive summary
  Ericsson want all uses of 25 µs LBT to use the same option as used to obtain the channel in the first place
  Neither of Ericsson’s two proposals implement their preference, and both make the text messy
  Ericsson’s allegation that 802.11-2016 violates EN 301 893 is also incorrect
  Ericsson’s poorly justified proposals & incorrect allegations should be rejected in favour of balance & technology neutrality
Adapted from BRAN(20)105xxx

## Slide 57: Ericsson want all uses of 25 µs LBT to use the same option as used to obtain the channel in the first place
  During the BRAN#104b teleconference, Ericsson expressed a preference while discussing BRAN(20)104b003 that all uses of 25 µs LBT use the same “umbrella LBT” option that was used to obtain the channel in the first place
  Ericsson particularly focused on the use of 25 µs LBT during:
    Multi-channel operation
    Paused COT
  For example:
    If PD/ED is used for the primary channel then a 25 µs PD/ED should be used for the secondary channel in multi-channel operation (Wi-Fi)
    If ED-only is used for to gain a channel then 25 µs ED-only should be used before restarting a paused COT (LAA/NR-U)
Adapted from BRAN(20)105xxx

## Slide 58: Neither of Ericsson’s two proposals implement their preference, and both make the text messy
  BRAN(20)104b003 includes two possible implementation options of Ericsson’s preference in EN 301 893
  The first option does not seem to actually do anything useful
    It makes a modification to the paused COT mechanism in EN 301 893 that does not seem to have any effect on requirements, but does make the text messier
    It does not address multi-channel operation at all
  The second option contradicts Ericsson’s stated preference, and creates messy text
    It is based on an observation that PD is very not effective in a 25 µs LBT
    It then gives up on Ericsson’s preference, instead proposing that all 25 µs LBT’s are based on ED-only at -72 dBm
    This results in messy text by liberally spreading EDTs around EN 301 893 in clause 4.2.7.3.2.3 & 4.2.7.3.2.7, rather than keeping all EDT definitions in 4.2.7.3.2.5
Adapted from BRAN(20)105xxx

## Slide 59: Ericsson’s allegation that 802.11-2016 violates EN 301 893 is also incorrect
  During BRAN#104b, Ericsson also alleged in BRAN(20)104b003 that 802.11-2016 violates EN 301 893 because it:
    Specifies the use of PD/ED of -72/-62 dBm for secondary channels, whereas EN 301 893 is claimed to specify PD/ED of -82/-62 dBm
    Specifies an LBT for secondary channels of less than 9 µs (in 802.11-2016, 21.3.18.5.4), whereas EN 301 893 is claimed to specify “at least 25 µs”
  In both cases, Ericsson is incorrect:
    In EN 301 893, when PD/ED of -82/-62 dBm is used on the primary channel, the EDT is specified as -62 dBm across all channels; 802.11-2016 exceeds this requirement by specifying PD/ED of -72/-62 dBm in the secondary channel
    802.11-2016 specifies an LBT of PIFS (25 µs) in the secondary channel; the text in 802.11-2016, 21.3.18.5.4 actually relates to the sensitivity requirements rather than the LBT requirements
Adapted from BRAN(20)105xxx

## Slide 60: Ericsson’s proposals & allegations should be rejected in favour of balance & technology neutrality
  The requirements in EN 301 893 were negotiated in good faith to provide a balance between:
    Allowing both existing (eg Wi-Fi) and proposed (eg LAA/NR-U) technologies to operate in the 5 GHz band in Europe (technology neutrality)
    Achieving fair & efficient use of the 5 GHz band by all technologies
  These goals have been successfully achieved in EN 301 893 in a variety of technology neutral ways by broad consensus, including by specifying:
    Both PD/ED at -82/-62 dBm & ED-only at -72 dBm for LBT access by any technology; Wi-Fi is expected to use both options, while LAA/NR-U is expected to mostly only use ED-only
    Two multi-channel mechanisms, where one is based on traditional Wi-Fi mechanism and the other is based on a traditional 3GPP mechanism
    A paused COT mechanism; explicitly included to enable LAA operation
  ETSI BRAN needs to progress rather than providing a forum for those whose prime motivation appears to be to block competitive technology
Adapted from BRAN(20)105xxx

## Slide 61: The Coex SC will discuss the impact of Ericsson’s proposal in ETSI BRAN on multi-channel access
  Should Coex SC recommend any actions?

## Slide 62
  Relationship topics
  EN 301 893
  Spectral Mask

## Slide 63: The Coex SC may discuss any updates on the spectral mask issue

## Slide 64
  Relationship topics
  EN 303 687
  Drafting

## Slide 65: Nothing much of note occurred during a teleconference focused on drafting EN 303 687 (6 GHz HS)
  The BRAN#104e teleconference was focused on drafting of EN 303 687 (6 GHz HS)
  It was planned that 6 GHz adaptivity issues would be addressed if there was time, but there wasn’t
  For those interested the details of the drafting are contained in:
    BRAN(20)104e008: Meeting minutes
    EN 303 687 v0.0.3

## Slide 66
  Relationship topics
  Synchronous access

## Slide 67: The Coex SC may need to pay attention to growing interest in FBE and synchronous access
Executive summary
  In BRAN#104, Qualcomm proposed a new synchronous access method
    Qualcomm claimed the new synchronous access method has significant gains, especially for CoMP
  Many at BRAN#104 thought Qualcomm’s proposal was interesting, albeit immature & so premature
  There were submissions but no discussion of FBE or synchronous access at the BRAN#104e teleconference
  It appears likely that the Coex SC is going to have to pay attention to FBE & synchronous access
  The Coex SC may discuss FBE or synchronous access today …

## Slide 68: In BRAN#104, Qualcomm proposed a new synchronous access method
Documents on synchronous access
  BRAN(19)104018: Technology neutral synchronous access (Qualcomm)
Summary of BRAN(19)104018 (Qualcomm)
  Qualcomm presented a new synchronous access method that builds on the LBT based LBE mechanism already in EN 301 893
    Uses existing LBT to access the channel
    Always completes a COT on a 6 ms boundary established by a global clock
    Adjusts the COT length compared to normal async access
      Normal COT is < 6/10 ms
      Adjusted COT is < 6 ms if COT is not busy at start of 6 ms slot in which COT starts
      Adjusted COT is < 12 ms if COT is busy at start of 6 ms slot in which COT starts
  …

## Slide 69: Qualcomm claimed the new synchronous access method has significant gains, especially for CoMP
Summary of BRAN(19)104018 (Qualcomm)
  …
  It is claimed that this adjustment to the COT length will allow both sync & async devices about the same access to the medium (on average) …
  … but with the benefit of synchronising devices being able to use advanced features like CoMP (Coordinated Multi-Point) more usefully
    The completion of COTs on the 6 ms boundary by sync devices is claimed to tend to cause all devices to often transmit within the 6 ms globally defined slots (even async devices)
  The presentation asserted that there are significant performance gains possible from the use of the proposed synchronous extension
    30-50% over LBE baseline in EN 301 893 from slot synchronisation
    Additional 20-100% by enabling advanced features like CoMP

## Slide 70: Many at BRAN#104 thought Qualcomm’s proposal was interesting, albeit immature & so premature
Discussion of BRAN(19)104018 (Qualcomm)
  Qualcomm made a similar proposal to the FCC in Nov 2019
  The key insight from the presentation is that Qualcomm does not propose changing the basic LBT access mechanism
    There was a concern from some that this was not the case
  Most people at BRAN thought the proposal was interesting & promising
    It may have benefits for 802.11a/n/ac/ax & additional benefits for 802.11be
    It will probably assist good coexistence
  They also noted it was immature and therefore premature to adopt
    Immature in that it has not been fully defined by Qualcomm
    Premature in that it has not been fully reviewed by the broader community
  Questions were also asked about the source of the global clock and what happened when there was more than one global clock

## Slide 71: There were submissions but no discussion of FBE or synchronous access at the BRAN#104e teleconference
Discussion at BRAN#104e teleconference
  Two documents related to synchronous access were submitted to the BRAN#104e teleconference (EN 303 687 drafting)
    BRAN(20)104e004 (Qualcomm) proposed draft text related to Qualcomm’s synchronous access proposal to:
      … illustrate required edits to Table 7 of EN 301 893 standard [3] to accommodate the proposal for synchronous access that utilize globally available reference, such as Universal System Time (UTC)
    BRAN(20)104e007 (Mediatek) argued that BRAN should focus on FBE rather than Qualcomm’s synchronous access proposal
      It noted a variety of issues with both the FBE & synchronous access proposals
      It asserted that FBE can coexist with LBE despite claims by others to the contrary; it also noted FBE can’t coexist with FBE!
  Neither submission was presented or discussed in BRAN#104e; they will be addressed in BRAN#105
    Apparently additional response documents are being prepared

## Slide 72: It appears likely that the Coex SC is going to have to pay attention to FBE & synchronous access
Discussion about FBE & synchronous access
  BRAN(20)104e007’s comments about synchronous access suggest the Coex SC is going to continuing paying attention
    BRAN(20)104e007’s assertions seem to confirm a comment made in Irvine that the synchronous proposal is “interesting, but immature and so premature”
  BRAN(20)104e007’s comments about FBE suggest the Coex SC is going to have to pay more attention to FBE coexistence with LBE
    Previously it was assumed (and it may still be true) that LBE would dominate FBE, and so FBE could be safely ignored, whereas Mediatek claim this is not the case
    During BRAN#104e, Mediatek asserted that FBE is important because NR-U will use it to access the medium; this is the first time any use of FBE by NR-U has been mentioned, although subsequent investigations confirm NR-U Rel-16 does support the use of FBE

## Slide 73: The Coex SC may discuss FBE or synchronous access today …
  Note: FBE or synchronous access were originally raised in the context of EN 301 893 (5 GHz), but they could equally apply to EN 303 687 (6 GHz)

## Slide 74
  Relationship topics
  PD/ED in 6 GHz

## Slide 75
  The BRAN#104e teleconference (EN 303 687 drafting) there were four submissions related to the use of PD/ED in 6 GHz
    BRAN(20)104e005r1: Sharing in 6GHz (Ericsson)
      Asserts that fair sharing in 6 GHz is best enabled by ED-only at -72 dBm (although it hints that a different level might be even better)
    BRAN(20)104e002: EDT in 6 GHz summary (Cisco)
      A summary of previous discussions
    BRAN(20)104e001: EDT in 6 GHz discussion (Cisco)
      Asserts that fair sharing in 6 GHz is best enabled by starting with ED-only+PD/ED from EN 301 893 based on evidence that sharing is enable by detection at -82 dBm and a recognition that an ED-only option is needed for practical reasons
    BRAN(19)104030r2: Response to BRAN(19)104010r1 Common ED for 6GHz (Broadcom)
      Asserts both ED-only and PD/ED should be allowed because Ericsson assertion that ED-only at -72 dBm is best is contradicted by a wide range of evidence, including submissions by Ericsson
  None were discussed at BRAN#104e but will be discussed at BRAN#105

## Slide 76
  Relationship topics
  EN 303 687
  Technology neutrality

## Slide 77: ETSI BRAN continues to disagree on the relevance or importance of technology neutrality for a HS
  Technology neutrality is a concept that has been (mis)used in ETSI BRAN over a number of years to argue for the use of the ED-only mechanism over the PD/ED+ED-only mechanism
  There is on ongoing disagreement in ETSI BRAN about the relevance or importance of technology neutrality for a HS
    Is it a valid criterion for EN 301 893 (or EN 303 687)?
    Can it be used as the basis of a reasonable argument against the inclusion of PD/ED mechanism in EN 301 893 (or EN 303 687) as an option equal to ED-only?

## Slide 78: Despite a proposal to stop talking about technology neutrality, it is likely to be on the agenda at BRAN#105
  There was a proposal at and after BRAN#104 to stop discussing technology neutrality because it was not helping to progress the development of EN 301 893 (or EN 303 687)
  Unfortunately, there was not consensus on this proposal and so it appears the discussion about technology neutrality as a criteria will continue at BRAN#105
  There is at least one submission to BRA#105 addressing the arguments about technology neutrality … yet again
    See BRAN(20)105xxx
  There is nothing for the Coex SC to do in relation to technology neutrality except observe …

## Slide 79
  Relationship topics
  ETSI BRAN activities
  Next meetings

## Slide 80: ETSI BRAN will next meet face to face at BRAN#105 in March 2020
ETSI BRAN meeting schedule
  BRAN #105 (next week)
    23 March 2020 - 27 March 2020
    Sophia Antipolis
  BRAN #106
    22 June 2020 - 26 June 2020
    Sophia Antipolis
  BRAN #107
    28 September 2020 – 2 October 2020
    Sophia Antipolis

## Slide 81
  Relationship topics
  ETSI BRAN activities
  Liaison (Thu)

## Slide 82: The Coex SC may consider a LS to ETSI BRAN articulating an IEEE 802.11 WG position on 6 GHz
  A key issue in ETSI BRAN is whether EN 303 687 should specify the use of PD/ED and/or ED-only for 6 GHz operation
  Up until now, the assumption of many in the Wi-Fi community is that 802.11 will use the traditional PD/ED mechanism & thresholds in 6 GHz
    This position was considered at the 802.11 WG mid-session plenary where it was determined <what>
  Assuming this is the case, one possibility is that IEEE 802.11 WG recommend to ETSI BRAN via a LS that EN 303 687 adopt the mechanisms for 5 GHz defined in in EN 301 893
    See 11-20-0171-02

## Slide 83: The Coex SC may consider approving a LS to ETSI BRAN on 6 GHz
Motion
  The IEEE 802.11 Coexistence SC recommends to the IEEE 802.11 WG that 11-20-0171-02, articulating a position on adaptivity for 6 GHz in EN 303 687, be liaised to ETSI BRAN
  Moved:
  Seconded:
  Result:

## Slide 84
  Coexistence
  3GPP RAN/RAN1 review

## Slide 85: 3GPP RAN/RAN1 coexistence activities
  …

## Slide 86
  Coexistence
  WBA review

## Slide 87: WBA coexistence activities
  …

## Slide 88
  Coex SC
  Extension of SC charter

## Slide 89: The Coex SC may discuss and consider a new scope to extend its life beyond 802.11ax (again)
  The question of coexistence between Wi-Fi and various LTE based technologies has been “hot” for the last 4+ years
  The Coex SC is scheduled to close when 802.11ax completes SA Ballot in 2020
  However, here is no reason to think that coexistence will not remain a vitally important issue beyond the completion of IEEE 802.11ax as:
    IEEE 802.11be is developed
    ETSI BRAN develops a Harmonised standard for 6 GHz operation
  As the ratification of IEEE 802.11ax get closer the Coex SC may want to consider a scope extension
  There was discussion in relation to expanding the scope of the Coex SC in Irvine in Jan 2020, but at the time … it appeared that many in the SC wanted to wait until they had a chance to consider the issues

## Slide 90: The agreed Coex SC scope focuses on ensuring 802.11ax has fair access to global unlicensed spectrum
Discuss the use of PD, ED or other 802.11 coexistence mechanisms with the goal of promoting “fair” use of unlicensed spectrum
Promote an environment that allow IEEE 802.11ax “fair access” to global unlicensed spectrum
Will initially focus on liaising with 3GPP RAN/RAN1/RAN4 but may also lead to interactions with regulators and other stakeholders
Will probably not conclude at least until RAN4’s 802.11/LAA coexistence testing is defined and successfully executed
May require the SC to consider other simulations and results of tests of potential LAA/802.11 coexistence mechanisms
Will initially focus on encouraging a “technology neutral” solution in the next revision of EN 301 893 that allows IEEE 802.11ax fair access to unlicensed spectrum in Europe (noting the European approach is likely to have global impact)
The effort will also focus on allowing 802.11ax to use innovative mechanisms for frequency reuse without compromising the goal of fair access

## Slide 91: The Coex SC has potential coexistence work related to 802.11be & 6 GHz
Why should the Coex SC charter be extended?
  The existing Coex SC charter is mostly constrained to 802.11ax & 5 GHz coexistence, despite potential coexistence issues with 802.11be & 6 GHz
    It does not cover coexistence with 802.11be (the next big thing )
    It did not explicitly cover coexistence in 6 GHz (the other next big thing )
      It could be argued that is does implicitly cover 6 GHz with the 802.11ax PAR extension covering 6 GHz
  There is likely to be relevant material to review from other organisations related to coexistence
    3GPP RAN1 will probably not provide as much to review as in the past because the NR-U spec is completed (although they are talking about revisions, particularly into 6 GHz)
    ETSI BRAN will continue providing material as the 5 GHz HS (EN 301 893) is completed and the 6 GHz HS (EN 303 687) is developed

## Slide 92: The SC may discuss a possible new scope for a rechartered Coex SC
Possible new scope for Coexistence SC charter extension
  The Coex SC shall promote the establishment of an environment and the use of mechanisms that enable IEEE 802.11 technologies to have “fair access” to global unlicensed spectrum
  The Coex SC should focus particularly on coexistence, for example of 802.11ax & 802.11be with LAA & NR-U in the 5 GHz and 6 GHz bands
  The Coex SC may consider coexistence with other technologies and in other bands as directed by the Chair of the 802.11 WG
Possible close down criteria for Coexistence SC
  The Coex SC will close when it is determined by the 802.11 WG that the SC is unlikely to make further progress towards its goals

## Slide 93: The Coex SC may consider approving the extension of its charter
Possible motion
  The IEEE 802.11 Coex SC recommends to the IEEE 802.11 WG that the Coex SC charter is revised as shown in <see previous slide>
  Moved:
  Seconded:
  Result:

## Slide 94
  Coex SC
  Plans for next meeting

## Slide 95: The Coex SC will continue its normal business in May 2020 in Warsaw
Possible agenda items
  Review ETSI BRAN coex activities
    EN 301 893 (5 GHz)
    EN 303 687 (6 GHz)
  Review 3GPP RAN/RAN1 coex activities
  Review WBA coex activities
  Rechartering of the Coex SC
  …
  Note: it is likely the Coex SC sessions will be early in the week in Warsaw because the Chair needs to travel to an IEEE-SA BoG meeting in Osaka, Japan

## Slide 96: The IEEE 802.11 Coexistence SC meeting in Atlanta in Mar 2020 is adjourned!