## Slide 1: Container for advertising ML Information
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
Duncan Ho | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Date: 2020-03-15

## Slide 2: Recap: Framework for MLO advertisement [1]
Contribution [1] proposes a framework for advertising MLO capabilities
MLO attributes information are classified into three categories:
  Advertising link’s Information
  MLD (common) Information
  Per-link information
Follow inheritance model that exists in 11ax (Multiple BSSID set)
Advertising Link’s Information (STA 1)
Common/MLD
STA 2
STA 3
STA 4
Information of other STAs of the MLD (link profiles)
Capabilities and parameters different from the advertising link
Non-inheritance

## Slide 3: Recap: M-BSSID feature with MLO [2]

## Slide 4: Container for carrying ML information
We looked at existing elements to see if they have the format and properties to carry MLO capabilities information
Four elements that came close to matching the requirements were Neighbor Report, Multi-Band element, Multiple BSSID and Reduced Neighbor Report
  However, these elements either didn’t have structure to make them extensible or were not carried in the frames that would advertise the multi-link attributes
    See appendix for analysis on Neighbor Report, Multi-Band, Multiple BSSID and RNR

## Slide 5: Container for carrying ML information
We propose to define a new element: Multiple Link Attribute (MLA) element
  Exact name TBD
The element would include:
  a set of fields that carry information that is common to all the links
    Common Control could carry indication of presence/absence of certain common fields
  Several sub-elements organized as a profile for each link
    Each profile follows inheritance model to avoid duplication of any information
      same as 11ax Multiple BSSID element
 | Element ID | Length | Element ID Extension | Common Control | MLD Address | MLD SSID | Authentication Algorithm | … | Optional Sub-elements
Octets: | 1 | 1 | 1 | x | 0 or 6 | 0 or 32 | 0 or 2 | … | variable
Common/MLD Capabilities
Set of elements organized as a profile for every other STA of the MLD
Strcuture of Multiple Link Attribute element
MLD Addr Present
MLD SSID Present
Auth Algo Present

## Slide 6: Flexibility to carry variable content
The element would be carried in the mgmt. frames transmitted by AP/non-STA during discovery and ML setup.
  provides a flexible structure to carry variable amount of information
    Sub-fields can indicate the presence of certain fields
Per-link Profiles – same as in 11ax Multiple BSSID element

## Slide 7: RNR for co-located APs
11ax 6 GHz discovery mechanism requires an AP to advertise information of a co-located 6 GHz AP via RNR IE.
However, as discussed in earlier slides, the RNR structure by itself is insufficient to provide MLO information
  Further, RNR lacks the mechanism to indicate affiliation of a reported AP to it’s MLD
    RNR IE can be extended to indicate MLD information (6 octets of MAC addr)
    each reported AP would duplicate this information – which is inefficient
  In addition, in scenarios with multiple BSSID set on a link, the BSSIDs can belong to different MLDs (see contribution [2])
Therefore extending RNR to provide MLD information and other information for each reported AP can lead to bloating
We propose a hybrid approach which utilizes RNR along with MLA IE to provide MLO information

## Slide 8: RNR + MLA for advertising MLO Info.
Beacon and Probe Response frames carry RNR IE to provide basic information of other AP(s) belonging to the MLD
  Same as 11ax 6 GHz discovery
In addition, Beacon, Probe Response and (Re)Association Response frames also carry MLA IE
  The IE provides MLD level (common) information and additional information of other AP(s) of the MLD
  Amount of information carried will vary depending on the scenario
    Beacon is expected to provide basic information (at a minimum MLD/Common, capabilities for each link and critical update indication for each link)
      This will help unassociated STAs identify candidate APs during discovery
  Upon receiving a Beacon frame, non-AP STA may Probe candidate AP(s) to gather additional information
    Probe Response and Association Response is expected to provide complete information for the MLD the non-AP STA is interested in.
  Critical update indication lets an associated STA know if there was any BSS parameter updates without requiring the STA to monitor beacons on each link

## Slide 9: Associate RNR and MLA using Link ID
Use Link-ID to bind a reported AP between RNR and MLA IE
RNR format extended to carry Link-ID field (1 octet)
The per-link sub-element of MLA carries Link-ID for each reported link
  In case of M-BSSID/co-hosted set, the link ID is unique across all the MLDs
Beacon frame
RNR
MLA
Mapping based on Link-ID
AP entries
Per-link profile

## Slide 10: Per-link Profile

## Slide 11: Multiple BSSID with MLO
An AP of an AP MLD may correspond to a nonTxBSSID in a multiple BSSID set on a link (see [2])
In such case, an entry in the reported AP in an RNR can correspond to MLD that the nonTxBSSID is affiliated with.
The profile for the nonTxBSSID would carry MLA IE containing the per-link profile for APs belonging to its MLD
  The binding between the nonTxBSSID and the reported AP is based on the Link-ID
Beacon frame
RNR
MLA
Mapping based on Link-ID
MBSSID
AP entries
Per-link profile
nonTxBSSID profile
MLA
Per-link profile

## Slide 12: Inheritance Model
To avoid frame bloating, the AP should follow inheritance model same as the one described for multiple BSSID feature to reduce duplication of information
An MLA IE may be carried in the core frame or as within a Nontransmitted BSSID profile of multiple BSSID element.
The inheritance model would employ the following rules:
  Core frame to IE
    If an element is not carried in the per-link profile, the value is the same as the element carried in the core frame (this is same as current MBSSID inheritance rule)
  nonTxBSSID to MLA
    If MLA IE is carried within a nonTxBSSID profile and the per-link profile doesn’t include an element carried in the nonTxBSSID profile (or inherited by the profile), the value is the same as that for the profile
Beacon frame
RNR
MLA
Mapping based on Link-ID
MBSSID
AP entries
Per-link profile
nonTxBSSID profile
MLA
Per-link profile

## Slide 13: Capabilities advertisement of non-AP MLD
Probe Request and (Re)Association Request frame from STA of a non-AP MLD includes MLA IE to provide capability information of other STA(s) of its MLD

## Slide 14: Summary
This contribution defines a container for carrying MLO capabilities information
  Element provides a flexible structure to carry variable amount of information
  Utilize RNR IE and MLA IE to provide MLO information
  Element included in an ML AP’s Beacon, Probe Response and ML setup frames
  Element included in a non-AP STA’s Probe Request or ML setup frames

## Slide 15: SP #1
Do you agree that MLO framework should define a new element (Multiple Link Attribute element) to carry:
  Information of the transmitting MLD
  Information common to all the links of the transmitting MLD
  Information of all links of the MLD other than the transmitting link
    Referred to as per-link profile
  Note : Exact name TBD
  Y:
  N:
  A:

## Slide 16: SP #2
Do you agree to the high-level format for the new element (Multiple Link Attribute element) as shown in slides 5 & 6
  Note : Exact name TBD
  Y:
  N:
  A:

## Slide 17: SP #3
Do you agree to define a link identifier (Link ID) to efficiently identify a link (Tuple consisting of Operational Class, Channel, BSSID)
  Y:
  N:
  A:

## Slide 18: SP #4
Do you agree to provide a mechanism to carry link identifier (Link ID field) in the Reduced Neighbor Report element?
  Y:
  N:
  A:

## Slide 19: SP #5
Do you agree that the per-link profile carried in the Multiple Link Attribute element include a link identifier (Link ID field) when the element is carried in a management frame transmitted by an AP of an AP MLD?
  Y:
  N:
  A:

## Slide 20: SP #6
Do you agree that an AP of an AP MLD shall set the value of the Link ID field carried in the per-link profile of the Multiple Link Attribute element and Reduced Neighbor Report element to be the same when the reporting the same co-located AP of its AP MLD?
  Y:
  N:
  A:

## Slide 21: SP #7
Do you agree that a STA of a non-AP MLD shall include the Multiple Link Attribute element in Probe Request and (Re)Association Request frames it sends to an AP of an MLD to carry MLD information and capabilities of other STAs of the MLD?
  Y:
  N:
  A:

## Slide 22: Appendix

## Slide 23: References
11-20/0356: MLO: Discovery and Beacon bloating (Abhishek Patil, Qualcomm)
11-20/0358: Multi-BSSID Operation with MLO (Abhishek Patil, Qualcomm)

## Slide 24: Neighbor Report element (NRE)
NRE provides the necessary framework to carry information about each link:
  NRE carries Operating Class, Channel, BSSID  useful for identifying the link
  Optional Subelements field can carry Capabilities and Operation elements
    Ability to carry several other elements of interest (such as provide TSF offset info.)
  11ax additions such as SSID element, BSS Load etc can be useful for MLO
NRE doesn’t have the format to carry MLD/Common information
NRE format allows inclusion of several elements (as sub-elements) which can lead to bloating
  Possibility the reason why NRE is not allowed in Beacon/Probe Response frames in baseline spec
11be spec would need to allow NRE in a non-AP’s Probe Request frame
  This can cause inter-op issues with legacy (pre-11be) APs
Back

## Slide 25: Multi-Band element (MBE)
MBE has fields that can identify a link
  Operating Class, Channel, BSSID
  Carries Beacon Interval and TSF offset
MBE doesn’t have the format to carry MLD/Common information
All other fields are not useful from MLO advertisement point of view
Further, MBE doesn’t have the ability to carry Subelement which would be needed to carry link specific IEs such as Capabilities & Operational parameters
Back

## Slide 26: Multiple BSSID element (MBSSID)
MBSSID has the format to carry profile for each link
  Other properties such as profile straddling and non-inheritance are already defined
MBSSID doesn’t have the format to carry MLD/Common information
Using MBSSID IE for advertising multi-link information will cause legacy compliance issue
  Legacy STAs determine that an AP is MBSSID capable if they see this IE in the Beacon frame.
  Becomes an issue if a single BSSID AP advertises this IE for carrying multi-link information.
Back

## Slide 27: Reduced Neighbor Report (RNR)
RNR has fields that can identify a link
  Operating Class, Channel, BSSID
  Carries TSF offset and short SSID
RNR doesn’t have the format to carry MLD/Common information
However it doesn’t have the ability to carry Subelement which would be needed to carry link specific IEs such as Capabilities & Operational parameters
Back