## Slide 1: Multi-BSSID Operation with MLO
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
Duncan Ho | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Date: 2020-03-15

## Slide 2: Overview
Multiple BSSID set feature enables multiple (virtual) APs hosted on the same device to setup BSS on a link
  Each (virtual) AP has its own capabilities and other attributes
    E.g., SSID, security, feature set etc
In multi-link operation, APs of an MLD share common parameters
  E.g., common security, BA session and possibly SSID
This document takes a closer look on how these two features fit together

## Slide 3: Multiple BSSID set with MLO
Since each (virtual) AP on a link has different set of attributes, they can’t be part of the same AP MLD.
Further, it is possible to have (virtual) APs on different links be part of the same AP MLD
  E.g., an enterprise network utilizes all links and has same SSID, common security and BA session across all links. A guest network uses a subset of the links which share security and BA session.
Therefore, a set of virtual APs from different links would belong to the same AP MLD
  There would be different AP MLDs operating on the same set of links
  Each MLD having its own set of common attributes

## Slide 4: Multiple MLDs for a set of links

## Slide 5: Thoughts on signaling a combination of Multiple BSSID set and MLDs
A beacon for an AP would carry Multiple BSSID element (MBSSID IE) which provides information of all the virtual APs operating on the link
  Same as today – 11ax multiple BSSID feature
The beacon also carries Multi-link Attribute element which provides information of the advertising BSSID’s MLD information and other links that are part of that AP MLD.
  Information of other links can be advertised as partial profile to prevent beacon bloating.
A nontransmitted BSSID profile in the MBSSID IE would carry Multi-Link Attribute element which provides MLD information and partial profile for other links of that AP MLD
  Exact signaling details TBD.

## Slide 6: Co-Hosted BSSID set
Further, APs of a co-hosted set would have similar considerations
11ax introduced the concept of co-hosted BSSID set for supporting legacy clients
  Each AP in a co-hosted BSSID set transmits its own beacon and probe response frames
    Highly inefficient compared to multiple BSSID set where a single beacon carries information for the set
  Operation permitted only for APs operating on 2.4/5 GHz
Since each AP of a co-hosted set has different set of attributes, they can’t be part of the same AP MLD.
  However, an AP of an MLD may be part of a co-hosted set of a link

## Slide 7: Summary
This contribution discusses the support multi-link operation in conjunction with multiple BSSID set or co-hosted BSSID set operation on one or more links
  It is possible that an AP of an AP MLD corresponds to a nonTxBSSID in a multiple BSSID set on a link
  BSSIDs of a multiple BSSID cannot be part of the same AP MLD
  Similarly, an AP of an AP MLD may correspond to an AP in a co-hosted set on 2.4 or 5 GHz link
  Further APs of a co-hosted set cannot be part of the same AP MLD

## Slide 8: SP #1
Do you agree that an AP of an AP MLD can correspond to a transmitted BSSID or a nontransmitted BSSID in a multiple BSSID set on a link?
  Approved with unanimous consent
  Y:
  N:
  A:

## Slide 9: SP #2
Do you agree that APs belonging to the same multiple BSSID set cannot be part of the same AP MLD?
  Note: APs within a multiple BSSID set are, by definition, operating on the same channel
  Approved with unanimous consent
  Y:
  N:
  A:

## Slide 10: SP #3
Do you agree that APs belonging to the same co-hosted BSSID set cannot be part of the same AP MLD?
  Note: APs within a co-hosted BSSID set are, by definition, operating on the same channel
  Approved with unanimous consent
  Y:
  N:
  A:

## Slide 11: SP #4
Do you support that each AP of an AP MLD is independently configured to operate as transmitted or nontransmitted BSSID of a multiple BSSID set or as an AP of a co-hosted BSSID set or not part of either a multiple BSSID set or co-hosted BSSID set?
  Y: 52
  N: 2
  A: 33

## Slide 12: Appendix

## Slide 13: Brief history of VAPs
Types of VAPs | Remark
Multiple BSSID set (same channel) | Introduced by 11v and extended by 11ax Efficient mechanism to advertise multiple VAPs 11be should consider re-using/extending this
Co-Located AP set (same or different channel) | Introduced by 11ax for 6 GHz advertisement  Multi-link can re-use this
Co-Hosted BSSID set (same channel) | Introduced by 11ax for legacy compliance  Each VAP transmits its own beacon (highly inefficient)  11be should not extend or use this due to its inefficiencies
Multi-Link (different channel) | Introduced in 11be co-located AP concept can be extended for advertising link(s)
Time / amendment